Chem 133 – Spring 2008 – Exam #2 – May 6, 2008	Name: ______________________

Possibly useful equations:

Boltzmann’s constant (k) = 1.381x10-23 J K-1		Planck’s constant (h) = 6.626x10-34 J s-1

Speed of light (c) = 2.998x108 m s-1		π = 3.14159

Please read the questions carefully and follow instructions.  Be sure that your handwriting is clear, and indicate your answer.  Use the correct units and a reasonable number of sig figs.  If calculations are required, show your work in order to receive full or partial credit.

1. (4 pts) Choose the one correct answer.  Which of the following excitation methods uses the highest temperature to excite analytes in the sample?

a. flame

b. plasma

c. graphite furnace

d. All have temperatures that are relatively equal.

2. (4 pts) List the following atomic spectroscopy techniques in order from lowest to highest detection limits:

Plasma mass spectroscopy			lowest: __________________

Plasma emission					 __________________

Graphite furnace absorption				 __________________

Flame absorption				highest: __________________

3. (8 pts) What temperature (K) is necessary to excite 15% of Mg atoms in a sample into the excited state?  Mg atoms in the excited state have a ΔE corresponding to light at 589nm.  The degeneracies of the excited and ground states are 2 and 1 respectively.

4. (8 pts) Give the two mechanisms that cause line broadening in atomic spectroscopy beyond the natural line width.

1.

2.

5. (8 pts) List one advantage and disadvantage of the extensive fragmentation pattern created by electron impact ionization.

Advantage: ____________________________________________________

Disadvantage: __________________________________________________

6. (5 pts) For the following ionization techniques, indicate what phase (gas, liquid, or solid) the sample should be to use the technique.  Only indicate one per method.

Atmospheric pressure chemical ionization				__________

Electrospray								__________

Electron impact							__________

Matrix assisted laser desorption/ionization				__________

Fast atom bombardment						__________

# 7. (8 pts) What resolving power does a mass analyzer need to separate two ions with mass to charge ratios of 1050.00 and 1050.05?

8. (6 pts) What are the three major parts that make up any mass spectrometer?

1.

2.

3.

9. (5 pts) Choose the one correct answer.  Which of the following ion separation techniques is the fastest?

a. quadrapole

b. magnetic sector

c. ion trap

d. time of flight

10. (4 pts) NMR depends on radiation in the _________ frequency.

a. infrared

b. radio

c. x-ray

d. microwave

11. (10 pts) What is the 1H Larmor frequency (expressed in MHz) for an NMR instrument with an 11.74 T superconducting magnet?  The magnetogyric ratio for 1H is 2.6752x108 T-1 s-1.

12. (4 pts) Choose the one correct answer.  The coupling constant between two different types of protons on a 600 MHz NMR is 7.4 Hz.  The coupling constant for these same two protons on a 300 MHz NMR is:

a. 3.7 Hz

b. 14.8 Hz

c. 7.4 Hz

d. 22.2 Hz

13. (6 pts) In terms of column efficiency, what is the advantage of open tubular columns used in gas chromatography (describe the mechanism)?

14. (10 pts) Use the chromatographs below to answer the following questions.  The two chromatograms of samples containing A, B, and C were obtained at the same linear velocity with two columns of equal length.

Which column has a smaller plate height?

Which compound has the largest capacity factor?

Is the separation factor for compounds A and B different between columns 1 and 2?

If these were open tubular GC columns, which column would most likely be narrower in diameter?

Column 1

Column 2

15. (10 pts) Give the two major factors that contribute to separation (resolution) in chromatography.

1.

2.

# Text boxes

Retention Time (min)

Retention Time (min)

C

C

B

B

A

A