## Slide 1: Chem. 133 – 1/31 Lecture

## Slide 2: Announcements
Website update
  Web version of homework Set 1 (now complete)
  I have posted solutions to Rubinson & Rubinson problems of set 1.1
  I will post a data set soon for HW 1.2 problem
Quiz 1 – on 2/2 (related to lecture and HW 1.1 set)
Additional Problems also due 2/2
Today’s Lecture
  Continued application of Kirchhoff’s laws
  AC and other time varying circuits
  Capacitors and RC circuits

## Slide 3: Electronics
Applications of Kirchhoff’s Laws
  resistors in series and voltage divider (started last time)
  resistors in parallel
  more complicated circuits

## Slide 4: Electronics Alternating Current
DC = direct current (slowly varying voltage with time)
AC = alternating current (produced by many electric generators
In US 120V, 60 Hz is most common for AC outlet power
Voltage (or current)
time
v = Vpeaksinωt
time period
frequency = 1/(time period)

## Slide 5: Electronics Alternating Current
Related waveforms
Square wave
Sawtooth wave
Voltage
Voltage
time
time

## Slide 6: Electronics Alternating Current
Superposition and Fourier Transforms
Vnet(t) = V1(t) + V2(t)
Sine wave voltage → transforms to single frequency
See example
High frequency wave
frequency
Amplitude
Fourier Transform (of infinite wave)
low frequency wave
Sum (beat frequency)

## Slide 7: Electronics Alternating Current
Other Fourier Transform Examples
Example seen in NMR
Non-infinite decay wave
Finite Width
Fourier Transform

## Slide 8: Electronics Alternating Current – NMR Example – cont.
Most NMR FIDs look messier than shown
Due to a) multiple peaks and b) noisy signal which leads to noisier specra
To reduce the effect of the noise, it is common to increase the decay by multiplying the signal by an exponential decay function (Line Broadening in Bruker TopSpin software)
Non-infinite decay wave
Fourier Transform
Example of Noisier FID
signal rich region
noise rich region
FID processed with exponential decay
New spectrum has reduced noise but broader peak

## Slide 9: Electronics AC/Fourier Transform Question
Which of the following signals when Fourier transformed will show the frequency pattern shown to the right?
frequency

## Slide 10: Electronics Capacitors
Capacitors are devices to store charge
  capacitors are plates with small gap between plates
  charge spreads out along plate inducing opposite charge to other plate
  no dc current across gap (gap is non-conductive)
5 V
Capacitance = C = q/V
In capacitors, C = constant

## Slide 11: Electronics Capacitors
Uses of Capacitors
  Storage of charge to provided needed power
    Power supply may not supply enough power to start motor (start up power > running power)
    with capacitor, initial available I is high
motor

## Slide 12: Electronics Capacitors
Use of Capacitors (continued)
  Analog data filter (RC filter – low pass type shown)
signal in
signal out
Reduction of high frequency noise (example is numerically done filter)

## Slide 13: Electronics RC Circuits
An RC circuit consists of a resistor and capacitor in series
  You are responsible for quantitative understanding of behavior from step change in voltage (see below)
Switch
5 V
Before t = 0, switch in down position so V = 0 all parts but short segment
2) As switch is thrown (t = 0), charge travels through resistor to capacitor, but this takes time
3) After some time, the capacitor is fully charged and current drops to zero
V = 5V