## Slide 1: Chem. 133 – 2/2 Lecture

## Slide 2: Announcements
Turn in Additional Problems (1.1.1 + 1.1.2)
Quiz Today – after announcements
Today’s Lecture
  Capacitors and RC circuits
  Electrical Measurements
    Analog measurement
    Digital voltmeters

## Slide 3: Electronics Capacitors
Capacitors are devices to store charge
  capacitors are plates with small gap between plates
  charge spreads out along plate inducing opposite charge to other plate
  no dc current across gap (gap is non-conductive)
5 V
Capacitance = C = q/V
In capacitors, C = constant

## Slide 4: Electronics Capacitors
Uses of Capacitors
  Storage of charge to provided needed power
    Power supply may not supply enough power to start motor (start up power > running power)
    with capacitor, initial available I is high
motor

## Slide 5: Electronics Capacitors
Use of Capacitors (continued)
  Analog data filter (RC filter – low pass type shown)
signal in
signal out
Reduction of high frequency noise (example is numerically done filter)

## Slide 6: Electronics RC Circuits
An RC circuit consists of a resistor and capacitor in series
  You are responsible for quantitative understanding of behavior from step change in voltage (see below)
Switch
5 V
Before t = 0, switch in down position so V = 0 all parts but short segment
2) As switch is thrown (t = 0), charge travels through resistor to capacitor, but this takes time
3) After some time, the capacitor is fully charged and current drops to zero
V = 5V

## Slide 7: Electronics RC Circuits
Go to blackboard for more details of step change

## Slide 8: Electronics More on RC Circuits
Application in Lab
  when t(pulse period) >> RC, can treat as isolated step changes
  VR quickly returns back to 0 and VC to VIn
  when t(pulse period) ~ or < RC, can not treat as isolated step changes, and need to consider that VC changes slowly so will not reach Vin.
  at the time of a step change to, VRo = Vin - VC and then later VR = (Vin - VC)e-t/RC
Chart: RC Circuit
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 | 44 | 45 | 46 | 47 | 48 | 49 | 50 | 51 | 52 | 53 | 54 | 55 | 56 | 57 | 58 | 59 | 60 | 61
V(C) | 0 | 3.1606 | 4.3233 | 4.7511 | 4.9084 | 4.9663 | 4.9876 | 4.9954 | 4.9983 | 4.9994 | 4.9994 | -1.3214 | -3.6467 | -4.5022 | -4.8169 | -4.9326 | -4.9752 | -4.9909 | -4.9966 | -4.9988 | -4.9988 | 1.3217 | 3.6468 | 4.5022 | 4.8169 | 4.9326 | 4.9752 | 4.9909 | 4.9966 | 4.9988 | 4.9988 | -1.3217 | -3.6468 | -4.5022 | -4.8169 | -4.9326 | -4.9752 | -4.9909 | -4.9966 | -4.9988 | -4.9988 | 1.3217 | 3.6468 | 4.5022 | 4.8169 | 4.9326 | 4.9752 | 4.9909 | 4.9966 | 4.9988 | 4.9988 | -1.3217 | -3.6468 | -4.5022 | -4.8169 | -4.9326 | -4.9752 | -4.9909 | -4.9966 | -4.9988
V(R) | 5 | 1.8394 | 0.67668 | 0.24894 | 0.091578 | 0.03369 | 0.012394 | 0.0045594 | 0.0016773 | 0.00061705 | -9.9994 | -3.6786 | -1.3533 | -0.49784 | -0.18315 | -0.067375 | -0.024786 | -0.0091183 | -0.0033544 | -0.001234 | 9.9988 | 3.6783 | 1.3532 | 0.49781 | 0.18313 | 0.067371 | 0.024784 | 0.0091177 | 0.0033542 | 0.0012339 | -9.9988 | -3.6783 | -1.3532 | -0.49781 | -0.18313 | -0.067371 | -0.024784 | -0.0091177 | -0.0033542 | -0.0012339 | 9.9988 | 3.6783 | 1.3532 | 0.49781 | 0.18313 | 0.067371 | 0.024784 | 0.0091177 | 0.0033542 | 0.0012339 | -9.9988 | -3.6783 | -1.3532 | -0.49781 | -0.18313 | -0.067371 | -0.024784 | -0.0091177 | -0.0033542 | -0.0012339
Vin | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | -5 | -5 | -5 | -5 | -5 | -5 | -5 | -5 | -5 | -5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | -5 | -5 | -5 | -5 | -5 | -5 | -5 | -5 | -5 | -5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | -5 | -5 | -5 | -5 | -5 | -5 | -5 | -5 | -5 | -5
Chart: RC Circuit
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 | 44 | 45 | 46 | 47 | 48 | 49 | 50 | 51 | 52 | 53 | 54 | 55 | 56 | 57 | 58 | 59
V(C) | 0 | 0.47581 | 0.90635 | 1.2959 | 1.6484 | 1.9673 | 2.2559 | 2.5171 | 2.7534 | 2.9672 | 2.9672 | 2.209 | 1.523 | 0.90221 | 0.34054 | -0.16768 | -0.62753 | -1.0436 | -1.4201 | -1.7608 | -1.7608 | -1.1174 | -0.53527 | -0.0085222 | 0.4681 | 0.89937 | 1.2896 | 1.6427 | 1.9622 | 2.2513 | 2.2513 | 1.5612 | 0.93683 | 0.37187 | -0.13933 | -0.60189 | -1.0204 | -1.3991 | -1.7418 | -2.0519 | -2.0519 | -1.3808 | -0.77357 | -0.22414 | 0.273 | 0.72283 | 1.1299 | 1.4982 | 1.8314 | 2.1329 | 2.1329 | 1.4541 | 0.83995 | 0.2842 | -0.21865 | -0.67366 | -1.0854 | -1.4579 | -1.795 | -2.1
V(R) | 5 | 4.5242 | 4.0937 | 3.7041 | 3.3516 | 3.0327 | 2.7441 | 2.4829 | 2.2466 | 2.0328 | -7.9672 | -7.209 | -6.523 | -5.9022 | -5.3405 | -4.8323 | -4.3725 | -3.9564 | -3.5799 | -3.2392 | 6.7608 | 6.1174 | 5.5353 | 5.0085 | 4.5319 | 4.1006 | 3.7104 | 3.3573 | 3.0378 | 2.7487 | -7.2513 | -6.5612 | -5.9368 | -5.3719 | -4.8607 | -4.3981 | -3.9796 | -3.6009 | -3.2582 | -2.9481 | 7.0519 | 6.3808 | 5.7736 | 5.2241 | 4.727 | 4.2772 | 3.8701 | 3.5018 | 3.1686 | 2.8671 | -7.1329 | -6.4541 | -5.8399 | -5.2842 | -4.7813 | -4.3263 | -3.9146 | -3.5421 | -3.205 | -2.9
Vin | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | -5 | -5 | -5 | -5 | -5 | -5 | -5 | -5 | -5 | -5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | -5 | -5 | -5 | -5 | -5 | -5 | -5 | -5 | -5 | -5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | -5 | -5 | -5 | -5 | -5 | -5 | -5 | -5 | -5 | -5
at 10 ms, Vin -> -5V; VC = 3 V (not yet fully charged); VR = - 5V – 3V = -8V

## Slide 9: Electronics More on RC Circuits
For RC >> pulse time, it takes time for VC to become repetitive and a sawtooth wave results
Calculation of t: DVC/Dt = (Vin – VC)/t
or t = (Vin – VC)Dt/DVC
= (-5 – 0.5V)(10 ms)/-0.91V = 60 ms (at 130 ms)
Chart: RC Circuit

## Slide 10: Electrical Measurement/Digitization Ch. 17
Note: this seems out of order (but done to match lab)
Covers:
  types of electrical measurements
  digitization
  errors in measurements
Most Commonly Measured Quantities
  current
  voltage
  resistance

## Slide 11: Electrical Measurement The Ammeter
An analog measurement
Meters respond only to current
Now less common than voltmeters
Will not cover in detail
Current produces magnetic field to deflect needle
Notes: 11

## Slide 12: Electrical Measurements Digital Voltmeter
Main Components
  Analog to digital convertor
  Memory for data storage
  Data Display (decimal readout)
  Circuits for converting R, I measurements to V measurements
Analog vs. Digital
  Analog has continuously varying
  values vs. discrete values for digital
  Analog resolution depends on needle
  and markings vs. number of digits displayed with digital
4 3 7

## Slide 13: Electrical Measurements Digital Voltmeter – Binary Math
While the displays in digital voltmeters are decimal (0 → 9 values for each digit), actual electronics function is closely related to binary math
In binary, two possible states exist, 0 or 1
Binary No. | Name | Nominal Voltage
0 | Low | 0 V
1 | High | 5 V

## Slide 14: Electrical Measurement Binary and Bits
Counting in binary
  Number of digits = # bits = # parallel wires
# Bits | Possibilities | Circuit Values (V) | # posibilities
1 | 0 or 1 | 0 or 5 | 2
2 | 00, 01, 10, or 11 | 0¦0, 0¦5, 5¦0, 5¦5 | 4
3 | 000, 001, 010, 011, 100, 101, 110, 111 | 0¦0¦0, 0¦0¦5, etc. | 8
n | All 0s to all 1s | 0¦...¦0 to 5¦...¦5 | 2n
Notes: 14

## Slide 15: Electrical Measurement Binary to Decimal Conversion (and visa versa)
Go to blackboard
Notes: 15

## Slide 16: Electrical Measurements Analog to Digital Conversion
Camera Example
  3 bit digitizer (= analog to digital convertor)
  Light meter reads 5 V under intense light and 0 V in total darkness
  This will allow 23 = 8 aperture or shutter speed settings.
  The aperture and shutter speed controls light levels for film exposure (analog cameras) or for CCD electronics (digital cameras). The idea is to decrease aperture or exposure time for bright conditions.
  PROBLEM: If the camera is pointed at an object under partly cloudy skies and the light meter reads 2.9 V, what binary # does this correspond to, what decimal # does this correspond to. What is the voltage “read” by the camera?

## Slide 17: Electronics Analog to Digital Conversion
Camera Example (continued)
  How is signal split?
5.0 V
0.0 V
2.9 V = signal
1st Bit
2.5 V
1
0
So first digit is 1
2nd Bit
1.25 V
3.75 V
11
2 bit #
10
01
00
2 bit # is 10
3rd Bit
3.125 V
0.625 V
1.875 V
4.375 V
111
110
101
100
011
010
001
000
3 bit binary # is 100
decimal level
0
3
2
1
4
5
6
7

## Slide 18: Electrical Measurements Analog to Digital Conversion
More on Digital Camera
  So what would the light meter read?
    100 corresponds to any voltage between 2.5 and 3.125 V
    or 4 corresponds to the 5th reading out of 8 possible (0 to 7)
    or “dumb” translation to voltage: (4/8)*5.0 V + 0 V
    = (bin level/# levels)*(range) + min. voltage = 2.5 V
    smarter translation to voltage: 2.5 V(to bottom of 100 level) + ½(bin’s voltage) = 2.5 + 0.3125 = 2.81 V
  Measurement error = 2.81 – 2.90 V = -0.09 V (due to digitization)
  Average error ~ uncertainty ~ 1/2(bin voltage)
  = 0.5(input range/2n) = 0.5(5 V/8) = 0.3125 V
  with lots of bits, figuring how to “read” bin is not important (e.g. if noise > bin’s voltage), whether you read from the bottom, or 2.50 V, middle, or 2.81 V, or top, 3.125 of the bin won’t matter)

## Slide 19: Electrical Measurements Analog to Digital Conversion
Equation for Conversion (use this method instead of bit by bit method in graphic slide)
  decimal # = (meas. V – min. V)*2n/(input range)
  (n = # bits)
  camera example:
    decimal #= (2.90 – 0 V)*23/5 V = 4.6
    round down to 1 integer so 4 (then can convert to binary = 100)