## Slide 1: Chem. 133 – 2/7 Lecture

## Slide 2: Announcements
Return Graded Materials
Sac CT updated (quiz + turn in homework solutions posted + scores)
Today’s Lecture
  Electrical Measurements
    Analog measurement
    Digital voltmeters
    Digitization
    DVM measurement of I and R
    Errors in measurements

## Slide 3: Electrical Measurement/Digitization Ch. 17
Note: this seems out of order (but done to match lab)
Covers:
  types of electrical measurements
  digitization
  errors in measurements
Most Commonly Measured Quantities
  current
  voltage
  resistance

## Slide 4: Electrical Measurement The Ammeter
An analog measurement
Meters respond only to current
Now less common than voltmeters
Will not cover in detail
Current produces magnetic field to deflect needle
Notes: 4

## Slide 5: Electrical Measurements Digital Voltmeter
Main Components
  Analog to digital convertor
  Memory for data storage
  Data Display (decimal readout)
  Circuits for converting R, I measurements to V measurements
Analog vs. Digital
  Analog has continuously varying
  values vs. discrete values for digital
  Analog resolution depends on needle
  and markings vs. number of digits displayed with digital
4 3 7

## Slide 6: Electrical Measurements Digital Voltmeter – Binary Math
While the displays in digital voltmeters are decimal (0 → 9 values for each digit), actual electronics function is closely related to binary math
In binary, two possible states exist, 0 or 1
Binary No. | Name | Nominal Voltage
0 | Low | 0 V
1 | High | 5 V

## Slide 7: Electrical Measurement Binary and Bits
Counting in binary
  Number of digits = # bits = # parallel wires
# Bits | Possibilities | Circuit Values (V) | # posibilities
1 | 0 or 1 | 0 or 5 | 2
2 | 00, 01, 10, or 11 | 0¦0, 0¦5, 5¦0, 5¦5 | 4
3 | 000, 001, 010, 011, 100, 101, 110, 111 | 0¦0¦0, 0¦0¦5, etc. | 8
n | All 0s to all 1s | 0¦...¦0 to 5¦...¦5 | 2n
Notes: 7

## Slide 8: Electrical Measurement Binary to Decimal Conversion (and visa versa)
Go to blackboard
Notes: 8

## Slide 9: Electrical Measurements Analog to Digital Conversion
Camera Example
  3 bit digitizer (= analog to digital convertor)
  Light meter reads 5 V under intense light and 0 V in total darkness
  This will allow 23 = 8 aperture or shutter speed settings.
  The aperture and shutter speed controls light levels for film exposure (analog cameras) or for CCD electronics (digital cameras). The idea is to decrease aperture or exposure time for bright conditions.
  PROBLEM: If the camera is pointed at an object under partly cloudy skies and the light meter reads 2.9 V, what binary # does this correspond to, what decimal # does this correspond to. What is the voltage “read” by the camera?

## Slide 10: Electronics Analog to Digital Conversion
Camera Example (continued)
  How is signal split?
5.0 V
0.0 V
2.9 V = signal
1st Bit
2.5 V
1
0
So first digit is 1
2nd Bit
1.25 V
3.75 V
11
2 bit #
10
01
00
2 bit # is 10
3rd Bit
3.125 V
0.625 V
1.875 V
4.375 V
111
110
101
100
011
010
001
000
3 bit binary # is 100
decimal level
0
3
2
1
4
5
6
7

## Slide 11: Electrical Measurements Analog to Digital Conversion
More on Digital Camera
  So what would the light meter read?
    100 corresponds to any voltage between 2.5 and 3.125 V
    or 4 corresponds to the 5th reading out of 8 possible (0 to 7)
    or “dumb” translation to voltage: (4/8)*5.0 V + 0 V
    = (bin level/# levels)*(range) + min. voltage = 2.5 V
    smarter translation to voltage: 2.5 V(to bottom of 100 level) + ½(bin’s voltage) = 2.5 + 0.3125 = 2.81 V
  Measurement error = 2.81 – 2.90 V = -0.09 V (due to digitization)
  Average error ~ uncertainty ~ 1/2(bin voltage)
  = 0.5(input range/2n) = 0.5(5 V/8) = 0.3125 V
  with lots of bits, figuring how to “read” bin is not important (e.g. if noise > bin’s voltage), whether you read from the bottom, or 2.50 V, middle, or 2.81 V, or top, 3.125 of the bin won’t matter)

## Slide 12: Electrical Measurements Analog to Digital Conversion
Equation for Conversion (use this method instead of bit by bit method in graphic slide)
  decimal # = (meas. V – min. V)*2n/(input range)
  (n = # bits)
  camera example:
    decimal #= (2.90 – 0 V)*23/5 V = 4.6
    round down to 1 integer so 4 (then can convert to binary = 100)

## Slide 13: Electrical Measurements Analog to Digital Conversion
Performance Measures:
  Number of bits (more bits means analog signal is converted to more precisely known digital signal)
  To ensure that digitization is NOT the limiting factor to sensitivity, noise should be seen following digitization
  Speed (frequency): boards used in class could operate at up to ~100kHz. High speeds are needed for fast measurements.
  Input range: the minimum voltage will correspond to all 0s and the maximum voltage will correspond to all 1s. Voltages greater than the maximum will be read as the maximum.

## Slide 14: Electrical Measurements Analog to Digital Conversion
Example of digitization of data (HPLC with fluorescence detector)
Chart: "Analog" flurescence signal
Chart: Flurescence signal
Was digitization o.k.?
digitization at 0.01 level shown

## Slide 15: Electrical Measurements Analog to Digital Conversion
Second Example:
  A pH meter is used to monitor a process where a solution is acidified and then neutralized. The pH range that is desired to measure is 1 to 8.
  The equation for the relationship between voltage and pH is found to be Voltage (in mV) = 231 – 60.1∙pH
  The analog to digital convertor is a 12 bit convertor with the useful input range from -250 to 250 mV.
  Answer the following questions:
    Before the solution is acidified, the binary # = 010 001 011 111. What is the voltage and the pH?
    After acidification, the voltage = 172 mV, what is the decimal # and pH corresponding to this?
    What is the maximum pH that can be read?
    Can a difference between pH = 7.00 and 7.05 be discerned?

## Slide 16: Electronics Digital Volt Meter (DVM) Measurement
Use of DVM for V, I, and R measurements
voltage
Thermocouple
Pair (generates V)
DVM
Current
transducer
Iout
Multimeter
Shunt resistor
DVM
-
+
+
-
I = Vmeter/Rshunt

## Slide 17: Electronics Digital Volt Meter (DVM) Measurement
Resistance Measurement
thermistor
multimeter
Constant I source
DVM
example problem: The power source puts out 1.00 mA and the voltage read is 0.722 V, calculate the resistance

## Slide 18: Electronics DVM Measurements
Errors in Measurements
  Errors in voltage measurements:
    can occur if a device also has "internal resistance"
    in combination with less than infinite resistance in DVM
  Example: measurement of voltage from an ion selective electrode or pH electrode. Calculate the error in voltage if a pH electrode reads 0.721 V and has an internal resistance of 830 kΩ if the DVM has a meter resistance of 10.0 MΩ.
  (go to blackboard)
Cell
DVM
R(cell)
R(meter)
Cell = pH electrode