## Slide 1: Chem. 133 – 2/9 Lecture

## Slide 2: Announcements
Seminars on Friday
  Biochem. Position + Regular seminar
Today’s Lecture
  Electrical Measurements
    DVM measurement of I and R
    Errors in measurements
  Transducers
  Operational Amplifiers (qualitatively – if we get to today)

## Slide 3: Electrical Measurements Analog to Digital Conversion
How signal can be “lost”:
  Exceed maximum voltage
  Below minimum voltage
  Insufficient resolution (bits) to pick up signal
  Insufficient speed to see fast processes
Example question - A portion of a signal is collected from a GC detector and digitized (through an analog to digital converter). A peak comes out where marked. What is a clear problem with the digitization?
a) sampling at too high of a frequency b) input voltage exceeding input range
c) not enough bits in digitizer d) it is missing the Minecraft people
Digitized Signal
peak
time

## Slide 4: Electronics Digital Volt Meter (DVM) Measurement
Use of DVM for V, I, and R measurements
voltage
Thermocouple
Pair (generates V)
DVM
Current
transducer
Iout
Multimeter
Shunt resistor
DVM
-
+
+
-
I = Vmeter/Rshunt

## Slide 5: Electronics Digital Volt Meter (DVM) Measurement
Resistance Measurement
thermistor
multimeter
Constant I source
DVM
example problem: The power source puts out 1.00 mA and the voltage read is 0.722 V, calculate the resistance

## Slide 6: Electronics DVM Measurements
Errors in Measurements
  Errors in voltage measurements:
    can occur if a device also has "internal resistance"
    in combination with less than infinite resistance in DVM
  Example: measurement of voltage from an ion selective electrode or pH electrode. Calculate the error in voltage if a pH electrode reads 0.721 V and has an internal resistance of 830 kΩ if the DVM has a meter resistance of 10.0 MΩ.
  (go to blackboard)
Cell
DVM
R(cell)
R(meter)
Cell = pH electrode

## Slide 7: Electronics Transducers
Definition:
A transducer is a device that converts a physical (or chemical) property into an electrical signal
Classifications:
By output measure (V, I, R, frequency)
By phenomenon measured (charged particle flux, temperature, light intensity, surface modification)
Internally vs. Externally Amplified

## Slide 8: Transducers Charge Particle Detectors
Measurement of electrons, molecular ions and charged aerosol particles
Most common type for GC and MS detectors
Charge Collector or Faraday Cup
I
e-
Can detect currents > 10-15 A

## Slide 9: Transducers Charged Particle Detectors
Detection Process
Charged particle hits cathode
Electrons emitted from collision
Amplificaion occurs with each stage
Current (electron flux) increases before anode
Cathode
Dynodes
M-
e-
e-
I
Electron Multiplier (MS detector)
Example: if each stage produces 6 useful electrons out per ion in, amplification in current would be x63 or x216. With greater amplification, single particle detection is possible

## Slide 10: Transducers Measurement of Temperature
Applications:
  Temperature control (e.g. GC ovens)
  Infrared light
Resistance based
  Thermistors and platinum resistance thermometers (both have R = f(T))
Voltage based
  Thermocouples (voltage generated by metal junction which depends on T)

## Slide 11: Transducers Detection of Light
Vacuum tube types
  Based on photoelectron effect
  Current based detectors
  Photocells (see diagram)
  All have minimum energy (maximum wavelength) where electron ejection just occurs
  Photomultiplier tube (combination of photocell and electron multiplier)
  Photomultiplier tube allows detection of single photons
I
hν
e-

## Slide 12: Transducers Detection of Light
Solid state types
  Typically less expensive than vacuum tube types
  Tend to operate better at longer wavelengths
  Based on promotion of electrons to conducting bands
  Photodiodes (I proportional to intensity)
  Photoconductivity cells (R dependent on intensity)
  Photovoltaic cells (V dependent on intensity)
  Advanced devices (discussed in spectroscopy section)
  Arrays (1D or 2D sets of detectors)
+
-
n
p
Reversed-bias photodiode:
High impedance until photons arrive
e-
e-
e-
1D Photodiode Array

## Slide 13: Some Questions on Transducers
List a transducer with a (primary) current signal.
List a transducer with a (primary) resistance signal.
List a transducer that can be used to measure charged particles.
What is the main reason that a photomultiplier tube is more sensitive than a photocell?
Give an example of a transducer that is readily available in an array form.

## Slide 14: Operational Amplifiers
General Use: Analog Signal Processing
Common Uses
  voltage amplification
  current amplification (removal of effect of internal resistance)
  current to voltage conversion
  differential amplifier to remove common noise
This time – only covering qualitatively (no calculations problems)

## Slide 15: Operational Amplifiers
Function
  Requires power (+15 V/ -15 V)
  Has inverting and noninverting inputs
  Output voltage is equal to (gain)x(V+ – V-) (“real” op amp)
  Main thing to know about real op amp is you can not connect the two input wires
+15 V
-15 V
+
-
inverting input
output

## Slide 16: Operational Amplifiers
“Ideal” Op Amp
  V+ = V- (infinite gain)
  I+ = I- = 0 (infinite input resistance)
Useful Circuits
  All use feedback circuits
  Example: voltage follower (current amplifier)
  V(output) = -V(electrode)
+
-
output
feedback circuit
+
-
electrode with Velectrode

## Slide 17: Operational Amplifiers
Other Useful Circuits
  Inverting amplifier
    in text
    Vout = -RfVin/Rin
    useful for amplifying voltage signals
  Differential amplifier
    in text
    Vout = (Rf/Rin)(V1 - V2)
    allows removal of noise common to V1/V2
  Current to voltage convertor
    Typically uses large Rf for high sensitivity
+
-
transducer with current I
Rf

## Slide 18
Notes: 18