## Slide 1: Chem. 133 – 2/14 Lecture

## Slide 2: Announcements
On Thursday
  HW1.2 problems due (1.2.1 to 1.2.5)
  Quiz 2
Today’s Lecture
  Operational Amplifiers (qualitatively)
  Noise

## Slide 3: Operational Amplifiers
General Use: Analog Signal Processing
Common Uses
  voltage amplification
  current amplification (removal of effect of internal resistance)
  current to voltage conversion
  differential amplifier to remove common noise
This time – only covering qualitatively (no calculations problems)

## Slide 4: Operational Amplifiers
Function
  Requires power (+15 V/ -15 V)
  Has inverting and noninverting inputs
  Output voltage is equal to (gain)x(V+ – V-) (“real” op amp)
  Main thing to know about real op amp is you can not connect the two input wires
+15 V
-15 V
+
-
inverting input
output

## Slide 5: Operational Amplifiers
“Ideal” Op Amp
  V+ = V- (infinite gain)
  I+ = I- = 0 (infinite input resistance)
Useful Circuits
  All use feedback circuits
  Example: voltage follower (current amplifier)
  V(output) = -V(electrode)
+
-
output
feedback circuit
+
-
electrode with Velectrode

## Slide 6: Operational Amplifiers
Other Useful Circuits
  Inverting amplifier
    in text
    Vout = -RfVin/Rin
    useful for amplifying voltage signals
  Differential amplifier
    in text
    Vout = (Rf/Rin)(V1 - V2)
    allows removal of noise common to V1/V2
  Current to voltage convertor
    Typically uses large Rf for high sensitivity
+
-
transducer with current I
Rf

## Slide 7
Notes: 7

## Slide 8: Noise Introduction
Why worry about noise?
  Both noise and signal affect sensitivity (the ability to detect low concentrations
  While it is easy to increase the signal, noise often will also increase (e.g. inverting op amp amplifier circuit)
  It is possible to reduce noise without also reducing the signal (e.g. differential op amp amplifier circuit or transducers with internal amplification)
  If we know the source of the noise we can make improvements more easily

## Slide 9: Noise Definitions
Noise
“variability in a measurement due to (random) errors” (textual)
2) the standard deviation in the values (σ) (mathematical) or the root mean square value (more common in electronics – based on assumption of sine wave form of noise)
3) peak to peak noise (graphical and roughly 6σ)
Peak to peak

## Slide 10: Noise Definitions
Limit of Detection (also see handout)
- Minimum detectable signal (Smin/N = 3 – may be defined alternatively)
- Concentration Detection Limit = concentration that gives minimum detectable signal
- Mass/Mole Detection Limit = mass or amount of sample that gives minimum detectable signal

## Slide 11: Noise Example Calculations
Data Set:
Measurement of Absorbance of 1.00 mM Benzoic Acid
Trial | Blank | Sample
1 | 0.0092 | 0.0251
2 | 0.0108 | 0.0231
3 | 0.0101 | 0.0227
4 | 0.0095 | 0.0244

## Slide 12: Noise Example Calculation
Determine:
  S/N (both for single measurement and in average)
  Relative standard deviation (%RSD)
  Detection Limit
(do calculations on board)

## Slide 13: Signal Averaging
If the noise is random and well known, repeat measurements improve S/N because signal is additive while noise adds as (n)0.5 (based on propagation of uncertainty rules)
Note: in some cases, averaging can affect qualitative information as well as quantitative information (e.g. mass spectrometer measured mass)
(S/N)n = [(S/N)n=1]n/(n)0.5 = [(S/N)n=1](n)0.5

## Slide 14: Signal Averaging - Question
A 1H NMR is performed on a small amount of sample expected to be the compound at right:
With 16 scans the S/N observed for the c 1H peak is 17.
How many scans are needed so that the minimum peak has a S/N of 3? (Assume all peaks have the same width)
a
b
c

## Slide 15: Signal Averaging Another Example
In mass spectrometry, and in particular with time-of-flight mass spectrometers, mass measurement is measured on many ions
Instrument resolution is good, but insufficient for high resolution on single measurements (resolution of 15,000 gives s ~ 0.1 amu for 1344 peak)
To meet “accurate mass” requirement, errors less than 5 ppm (0.007 amu) are required.
2s ~ 0.2 amu
x axis is mass
A single measurement will never meet high resolution requirement, but averaging will result in an improved average value.
For n > 50, 95% CI becomes mean + 1.96s/(n)0.5 or to reach 0.007 amu, would require roughly 784 “counts” or individual measurements

## Slide 16: Noise Sources – Fundamental Types
Thermal Noise = Johnson Noise (voltage associated)
- where:
kB = Boltzmann’s constant, T = temp. (K), R = resistance (W), and B = bandwidth (Hz) = range of frequencies accepted
- Solutions: cool devices, use lower R values, reduce bandwidth
B. Shot noise (current associated)
- Solutions: reduce bandwidth, use internally amplified transducers
where q= fundamental charge = 1.6 x 10-19 C and I = current

## Slide 17: Noise Sources – Other Types
Flicker Noise (or 1/f noise or pink noise)
  Occurs at low frequencies
  Can result from environmental changes (e.g. change in light intensity over time, change in temperature)
  Can be reduced through modulating source

## Slide 18: Noise Flicker Noise Example
lamp
chopper (alternatively reflects light or lets light through)
light detector
sample cell
blank cell
mirrors
Example of equipment for noise reduction
To Digitizer
high pass filter
rectifier
Notes: 18

## Slide 19: Noise Flicker Noise Example: Signals
light detector signal
slow increase in noise over 1st ~100 s
RC Filter only
low f noise removed
RC Filter + diode
Signal following digital filtration
Notes: 19