## Slide 1: Chem. 133 – 2/28 Lecture

## Slide 2: Announcements I
Homework Set 1.3 Solutions Posted (no problems will be collected)
Exam 1
  Mar. 7th
  Will review topics on Thursday
  Will cover all electronics topics and electrochemistry (Ch. 13 + most or all of Ch. 14)
Today’s Lecture - Electrochemistry
  Nernst Equation + Applications
  Relating K to E°

## Slide 3: Announcements II
Today’s Lecture – Electrochemistry – Cont.
  Reference Electrodes
  Types of Indicator Electrodes
  Junction Potentials and Current Effects
  Ion Selective Electrodes (last topic if time)

## Slide 4: Electrochemistry The Nernst Equation
The Nernst Equation relates thermodynamic quantities to electrical quantities for a cell reaction
Thermodynamics:
  ΔG = ΔGº + RTlnQ ΔG = free energy, Q = reaction quotient
  so, -nFE = -nFEº + RTlnQ, or E = Eº – (RT/nF)lnQ
  more often seen as: E = Eº – (0.05916/n)logQ (although only valid at T = 298K)
  Note: in calculations, E is for reductions (even if oxidation actually occurs at that electrode)
  Equation for electrodes or full cells, although text uses Ecell = E+ – E- where + and – refer to voltmeter leads
  Best to use activities in Q (even though we will just use concentrations)

## Slide 5: Electrochemistry The Nernst Equation
Example: Determine the voltage for a Ag/AgCl electrode when [Cl-] = 0.010 M if Eº = 0.222 V (at T = 25°C)?
Notes: 5

## Slide 6: Electrochemistry Applications of The Nernst Equation
Examples:
  The following electrode, Cd(s)|CdC2O4(s)|C2O42- is used to determine [C2O42-]. It is paired with a reference electrode that has an E value of 0.197 V (vs. the S.H.E.) with the reference electrode connected to the + end of the voltmeter. If Eº for the above reduction reaction is -0.522 V, and the measured voltage is 0.647 V, what is [C2O42-]?

## Slide 7: Electrochemistry Applications of The Nernst Equation
Application of Nernst Equation is most common in potentiometry
In potentiometry
  measured voltage is related to log[x] (where x is the analyte)
  this provides a method to analyze analytes over a broad concentration range (e.g. pH electrodes function well from about pH 1 to pH 11 or over 10 orders of magnitude)

## Slide 8: Electrochemistry Applications of The Nernst Equation
Relating the Nernst Equation to Equilibrium Equations
  Example problem: It is desired to use the reaction Zn(CN)2(s) + 2e- ↔ Zn(s) + 2CN- to measure [CN-] in suspected poisoned drinks. However, the Eº value is not available. Given that Eº = -0.762 V for Zn2+ + 2e- ↔ Zn(s), and Ksp = 3.0 x 10-16 for Zn(CN)2(s) ↔ Zn2+ + 2CN-, calculate Eº for the first reaction.

## Slide 9: Electrochemistry Potentiometry Overview (Chapter 14)
Potentiometry is the use of measured voltages to provide chemical information
Equipment
  Reference Electrode
  Indicator Electrode or ion-selective electrode
  Voltmeter
Most Common Applications
  Measurement of specific ions (usually with ion-selective electrodes)
  Redox titrations (to keep track of the extent of a reaction)

## Slide 10: Electrochemistry Potentiometry – Reference Electrodes
Role of Reference Electrodes
  Provide other half-cell to complete circuit
  Designed so that the voltage is near constant (even when conditions change or when current occurs)
Common Reference Electrodes
  silver/silver chloride: AgCl(s) + e- ↔ Ag(s) + Cl-
  calomel (Hg2Cl2): Hg2Cl2(s) + 2e- ↔ Hg(l) + 2Cl-
Purpose of saturated Cl- conditions:
  less variability in [Cl-] as current forces reaction

## Slide 11: Electrochemistry Potentiometry – Indicator Electrodes
Metal (Reactive) Electrodes
  simple electrodes to measure dissolved metal
  use can be extended to anions (e.g. Cl- in Ag/AgCl electrode)
  fairly limited use
Inert Electrodes
  e.g. Pt or graphite electrodes
  serve as an electron conduit to solution without electrode material participating in reaction
  used commonly in redox titrations described in Ch. 15 and in the types of electrolysis methods described in Ch. 16
Ion Selective Electrodes
  membrane based electrode to be described later
Ag(s)
Ag+
e-
Ag(s)
Pt(s)
Fe3+
e-
Fe2+

## Slide 12: Electrochemistry Potentiometry – Other sources of potential
In Potentiometry, ideally,
Emeasured = Eindicator electrode – Ereference electrode
(can be reversed if reference electrode is cathode)
However, other sources of potential exist:
  Emeasured = Eind – Eref – IR + Ejunction
  where: IR is due to non-zero current and resistance (this can be minimized by using voltmeter with very high resistance)
  and Ejunction is due to difference in ion concentrations across salt bridges (see text for details)
  because Ejunction depends on sample matrix, constant systematic errors can occur

## Slide 13: Electrochemistry Potentiometry – Ion Selective Electrodes
Common and low cost method to measure single ion
Most commonly used is pH electrode
Ion selective electrodes contain an internal solution and reference electrode
A membrane is responsible for potential generation
Potential is generated as ions diffuse out of or into membrane and complexes break apart or form
V
sample
internal reference electrode
reference solution
liquid containing double membrane
K+
K+L
K+A-
K+A-
K+A-
K+A-
L
L
K+L
B-
B-
B-
L
net effect of migration is generation of potential
external reference electrode

## Slide 14: Electrochemistry Potentiometry – Ion Selective Electrodes
Other types of ion selective membranes will involve:
  glass with ion sites
  solid state elements with ion sites
All ion selective electrodes function by difference in potential at surface between sample and reference solution ion concentrations
Potential depends on the log of the ion activity (concentration): E = const. + bpX where pX is negative log of the analyte ion activity and slope is positive for anions

## Slide 15: Electrochemistry Potentiometry – Ion Selective Electrodes
Ion selective electrodes have:
  imperfect selectivity (this affects low concentration measurements and in presence of similar ions)
  For example, in a 0.010 M NaOH solution, [Na+] = 0.01 M and [H+] = 1.0 x 10-12 M. If glass membrane is 1010 more selective for H+ than Na+, 100% error will occur.
  and can reach saturation at high concentration (only so many sites for H+ ions)
% Error
pH
7
Na+ interference
saturation

## Slide 16: Electrochemistry Potentiometry – Questions
The purpose of a reference electrode is to:
  provide a stable voltage b) complete the circuit
  provide a source of electrons or positive charges needed by the analyte electrode
  all of the above
For modern pH measurement, one probe will go into solution. How many reference electrodes exist in in this probe?
An F- ion selective electrode is to be used to check that water is properly fluoridated. It is found to work well in most cases, but gives errors in water samples at higher pH. Give a possible explanation for the error, and a possible solution to decrease the error.
A platinum electrode is used as:
a) reference electrode
b) an electrode for determining dissolved Pt
c) an inert electrode for following redox reactions
d) ion selective electrode