## Slide 1: Chem. 133 – 3/2 Lecture

## Slide 2: Announcements I
Exam 1
  Mar. 7th
  Reviewing topics today
  Will cover all electronics topics and electrochemistry (Ch. 13 + all of Ch. 14)
Today’s Lecture
  Ion Selective Electrodes
  Review of Topics on Exam 1
  Start to Spectroscopy (if time)

## Slide 3: Electrochemistry Potentiometry – Ion Selective Electrodes
Common and low cost method to measure single ion
Most commonly used is pH electrode
Ion selective electrodes contain an internal solution and reference electrode
A membrane is responsible for potential generation
Potential is generated as ions diffuse out of or into membrane and complexes break apart or form
V
sample
internal reference electrode
reference solution
liquid containing double membrane
K+
K+L
K+A-
K+A-
K+A-
K+A-
L
L
K+L
B-
B-
B-
L
net effect of migration is generation of potential
external reference electrode

## Slide 4: Electrochemistry Potentiometry – Ion Selective Electrodes
Other types of ion selective membranes will involve:
  glass with ion sites
  solid state elements with ion sites
All ion selective electrodes function by difference in potential at surface between sample and reference solution ion concentrations
Potential depends on the log of the ion activity (concentration): E = const. + bpX where pX is negative log of the analyte ion activity and slope is positive for anions

## Slide 5: Electrochemistry Potentiometry – Ion Selective Electrodes
Ion selective electrodes have:
  imperfect selectivity (this affects low concentration measurements and in presence of similar ions)
  For example, in a 0.010 M NaOH solution, [Na+] = 0.01 M and [H+] = 1.0 x 10-12 M. If glass membrane is 1010 more selective for H+ than Na+, 100% error will occur.
  and can reach saturation at high concentration (only so many sites for H+ ions)
% Error
pH
7
Na+ interference
saturation

## Slide 6: Electrochemistry Potentiometry – Questions
The purpose of a reference electrode is to:
  provide a stable voltage b) complete the circuit
  provide a source of electrons or positive charges needed by the analyte electrode
  all of the above
For modern pH measurement, one probe will go into solution. How many reference electrodes exist in in this probe?
An F- ion selective electrode is to be used to check that water is properly fluoridated. It is found to work well in most cases, but gives errors in water samples at higher pH. Give a possible explanation for the error, and a possible solution to decrease the error.
A platinum electrode is used as:
a) reference electrode
b) an electrode for determining dissolved Pt
c) an inert electrode for following redox reactions
d) ion selective electrode

## Slide 7: Exam 1 Topics to Know
Instrument Performance Measures
  know main measures discussed in class (e.g. sensitivity, selectivity, accuracy, etc.)
Electronics
  DC circuits (know and be able to apply: Kirchhoff’s Laws, Ohm’s Law, Power Law)
  AC Circuits and Fourier Transforms (be able to determine frequency, have qualitative understanding of Fourier transformation of time dependence to frequency dependence)
  RC Circuits (know quantitatively for single step change in voltage, know qualitative effects for other changes such as noise)
  Analog to Digital Signal Conversion (know how to convert between decimal and binary, and between digital signal and voltage, be able to estimate uncertainty in digitizer, significance of input range, know A/D performance parameters)

## Slide 8: Exam 1 Topics to Know – cont.
B. Electronics – cont.
  Measurements with digital voltmeters (know how these can be used for current and resistance measurements; know errors associated with measurements)
  Transducers (know how a few of each type work + how signal is measured)
  Operational Amplifiers (know general use)
  Noise (know how to calculate S/N and limit of detection; know main types of noise; know how to calculate thermal or shot noise; know effect of signal averaging; know ways to reduce noise)

## Slide 9: Exam 1 Topics to Know – cont.
C. Electrochemistry (Ch. 13/14)
  Redox reaction knowledge (be able to identify elements being oxidized and reduced, be able to balance half and full reactions).
  Be able to relate charge to moles of redox reactants consumed and to current and time.
  Know how to calculate electrical energy and relate it to chemical energy.
  Be able to identify anodes/cathodes in galvanic or electrolytic cells and their charge.
  Know what the standard potential is a measure of.

## Slide 10: Exam 1 Topics to Know – cont.
C. Electrochemistry (Ch. 13/14) – cont.
  Know how to use Nernst Equation to calculate potential or unknown concentration (for full cells or electrodes)
  Know how to use Hess’s law to combine redox reactions with equilibrium reactions (for calculation of K or E°)
  Know purpose of reference electrodes
  Know types and uses of indicator electrodes
  Understand how ion-selective electrodes work
  Some failings of ion-selective electrodes under specific conditions

## Slide 11: Exam 1 Equations Given On Exam
VR in response to step change in DVin in RC circuit (VR = DVin·e-t/RC
Equation for standard deviation
Equation for converting between voltage to A/D board and decimal number recorded
(decimal # = (V – Vmin)2n/(Vmax – Vmin)
Equations for thermal and shot noise
Definition of minimum observable signal (e.g. 3s for use in calculating limit of detection)
Nernst Equation and DG° = -RTlnK
You are responsible for all other equations (e.g. V = IR, P = IV, etc.). Constants will also be provided

## Slide 12: Electrochemistry What we are not covering
A. Chapter 15 – Redox Titration (not very instrumental)
Chapter 16 – Current-based Electrochemical Measurements
  These tend to be more modern electrochemical measurements
  Used frequently in electrochemical detectors in chromatography
  Cells used are electrolytic cells (electrical energy used to drive chemical reactions)
  Analyte concentration derived from charge (from current) measured
  Potential allows for selectivity (Ecell > Erxn for oxidation or reduction to occur but Ecell < Einterferant)

## Slide 13: Spectroscopy
A. Introduction
1. One of the main branches of analytical chemistry
2. The interaction of light and matter (for purposes of quantitative and qualitative analysis)
3. Topics covered:
- Theory (Ch. 17)
- General Instruments and Components (Ch. 19)
- Atomic Spectroscopy (Ch. 20)
- NMR (Rubinson and Rubinson)

## Slide 14: Spectroscopy
Fundamental Properties of Light
  Wave-like properties:
λ
λ = wavelength = distance between wave crests
n = frequency = # wave crests/s
= wave number = # wave crests/length unit
v = speed of light
Note in vacuum v = c = 3.00 x 108 m/s
Relationships: v = λ·n and = 1/λ
In other media, v = c/n where n = index of refraction
Note: when n > 1, v < c
Even if light travels through other media, wavelength often is defined by value in vacuum

## Slide 15: Spectroscopy Fundamental Properties of Light
1. Wave-like properties
- other phenomena: diffraction, interference (covered in Ch.19)
2. Particle-like properties
a) Idea of photons (individual entities of light)
b) Energy of photons
E = hn = hv/l
E = hc/l (if l is defined for a vacuum)

## Slide 16: Spectroscopy - Interaction with Matter: Absorption vs. Emission
Absorption
  Associated with a transition of matter from lower energy to higher energy state
Emission
  Associated with a transition from a higher to a lower energy state
E
Ao
A*
A + hn → A* and hn = photon
A * → A* + hn
Photon out

## Slide 17: Spectroscopy Regions of the Electromagnetic Spectrum
Many regions are defined as much by the mechanism of the transitions (e.g. outer shell electron) as by the frequency or energy of the transitions
Long wavelengths
Short wavelengths
High Energies
Low Energies
Gamma rays
X-rays
Nuclear transitions
Inner shell electrons
UV + visible
Outer shell electrons
Infrared
Bond vibration
Molecular rotations
Microwaves
Radio waves
Electron spin
Nuclear spin

## Slide 18: Spectroscopy Regions of the Electromagnetic Spectrum
Note: Higher energy transitions are more complex because of the possibility of multiple ground and excited energy levels
Ground electronic state
Excited electronic state
Vibrational levels
Rotational levels