## Slide 1: Chem. 133 – 3/9 Lecture

## Slide 2: Announcements I
Exam 1
  Ave = 70 (pretty typical)
  Not so usual distribution
  Solutions will be up on
  SacCT
Second Homework Set
  Working on completing
  Set 2.1 will be posted today
  Quiz and additional problems due 3/30
Range | N
90-97 | 2
80s | 0
70s | 4
60s | 4
<60 | 2

## Slide 3: Announcements II
Today’s Lecture
  Spectroscopy (Chapter 17)
    Nature of light (continuing)
    Energy State Transitions
    Fluorescence and Phosphorescence
    Beer’s Law

## Slide 4: Spectroscopy - Interaction with Matter: Absorption vs. Emission
Absorption
  Associated with a transition of matter from lower energy to higher energy state
Emission
  Associated with a transition from a higher to a lower energy state
E
Ao
A*
A + hn → A* and hn = photon
A * → A* + hn
Photon out

## Slide 5: Spectroscopy Regions of the Electromagnetic Spectrum
Many regions are defined as much by the mechanism of the transitions (e.g. outer shell electron) as by the frequency or energy of the transitions
Long wavelengths
Short wavelengths
High Energies
Low Energies
Gamma rays
X-rays
Nuclear transitions
Inner shell electrons
UV + visible
Outer shell electrons
Infrared
Bond vibration
Molecular rotations
Microwaves
Radio waves
Electron spin
Nuclear spin

## Slide 6: Spectroscopy Regions of the Electromagnetic Spectrum
Note: Higher energy transitions are more complex because of the possibility of multiple ground and excited energy levels
Ground electronic state
Excited electronic state
Vibrational levels
Rotational levels

## Slide 7: Spectroscopy Alternative Ground – Excited State Transitions
These can be used for various types of emission spectroscopy
Excitation Method | Related Spectroscopy
Thermal | Atomic Emission Spectroscopy
Charged Particle Bombardment | Electron Microscopy with X-ray Emission Spectroscopy
Chemical Reaction | Chemiluminescence Spectroscopy (analysis of NO)
Transition from even higher levels | Fluorescence, Phosphorescence
Notes: 7

## Slide 8: Spectroscopy Alternative Excited State – Ground State Transitions
Collisional Deactivation (A* + M → A + M + kinetic energy)
Photolysis (A* → B∙ + C∙)
Photoionization (A* → A+ + e-)
Transition to lower excited state (as in fluorescence or phosphorescence)
Some of the above deactivation methods are used in spectroscopy (e.g. photoaccustic spectroscopy and photoionization detector)

## Slide 9: Spectroscopy Questions
Light observed in an experiment is found to have a wave number of 18,321 cm-1. What is the wavelength (in nm), frequency (in Hz), and energy (in J) of this light? What region of the EM spectrum does it belong to? What type of transition could have caused it?
If the above wave number was in a vacuum, how will the wave number, the wavelength, the frequency and the speed change if that light enters water (which has a higher refractive index)?
Is a lamp needed for chemiluminescence spectroscopy? Explain.
Light associated with wavelengths in the 0.1 to 1.0 Å region may be either X-rays or g-rays. What determines this?
Notes: 9

## Slide 10: Spectroscopy Transitions in Fluorescence and Phosphorescence
Absorption of light leads to transition to excited electronic state
Decay to lowest vibrational state (collisional deactivation)
Transition to ground electronic state (fluorescence) or
Intersystem crossing (phosphorescence) and then transition to ground state
Phosphorescence is usually at lower energy (due to lower paired spin energy levels) and less probable
Ground Electronic State
Excited Electronic State
higher vibrational states
Triplet State (paired spin)

## Slide 11: Spectroscopy Interpreting Spectra
Major Components
  wavelength (of maximum absorption) – related to energy of transition
  width of peak – related to energy range of states
  complexity of spectrum – related to number of possible transition states
  absorptivity – related to probability of transition (beyond scope of class)
Ao
A*
DE
dE
A
l (nm)
dl

## Slide 12: Absorption Based Measurements Beer’s Law
Light intensity in = Po
Light intensity out = P
Transmittance = T = P/Po
Absorbance = A = -logT
Light source
Absorbance used because it is proportional to concentration
A = εbC
Where ε = molar absorptivity and b = path length (usually in cm) and C = concentration (M)
b
ε = constant for given compound at specific λ value
sample in cuvette
Note: Po and P usually measured differently
Po (for blank)
P (for sample)

## Slide 13: Beer’s Law – Specific Example
A compound has a molar absorptivity of 320 M-1 cm-1 and a cell with path length of 0.5 cm is used. If the maximum observable transmittance is 0.995, what is the minimum detectable concentration for the compound?

## Slide 14: Beer’s Law – Deviations to Beer’s Law
A. Real Deviations
- Occur at higher C
- Solute – solute interactions become important
- Also absorption = f(refractive index)

## Slide 15: Beer’s Law – Deviations to Beer’s Law
B. Apparent Deviations
1. More than one chemical species
Example: indicator (HIn)
HIn ↔ H+ + In-
Beer’s law applies for HIn and In- species individually: AHIn = ε(HIn)b[HIn] & AIn- = ε(In-)b[In-]
But if ε(HIn) ≠ ε(In-), no “Net” Beer’s law applies Ameas ≠ ε(HIn)totalb[HIn]total
Standard prepared from dilution of HIn will have [In-]/[HIn] depend on [HIn]total
In example, ε(In-) = 300 M-1 cm-1
ε(HIn) = 20 M-1 cm-1; pKa = 4.0

## Slide 16: Beer’s Law – Deviations to Beer’s Law
More than one chemical species:
Solutions to non-linearity problem
Buffer solution so that [In-]/[HIn] = const.
Choose λ so ε(In-) = ε(HIn)