## Slide 1: Chem. 133 – 3/14 Lecture

## Slide 2: Announcements
Second Homework Set
  Set 2.1 posted
  Quiz and additional problems due 3/30
Today’s Lecture
  Spectroscopy (Chapter 17)
    Fluorescence and Phosphorescence
    Beer’s Law – including deviations to it
    Instrumentation (overview)

## Slide 3: Spectroscopy Transitions in Fluorescence and Phosphorescence
Absorption of light leads to transition to excited electronic state
Decay to lowest vibrational state (collisional deactivation)
Transition to ground electronic state (fluorescence) or
Intersystem crossing (phosphorescence) and then transition to ground state
Phosphorescence is usually at lower energy (due to lower paired spin energy levels) and less probable
Ground Electronic State
Excited Electronic State
higher vibrational states
Triplet State (paired spin)

## Slide 4: Spectroscopy Interpreting Spectra
Major Components
  wavelength (of maximum absorption) – related to energy of transition
  width of peak – related to energy range of states
  complexity of spectrum – related to number of possible transition states
  absorptivity – related to probability of transition (beyond scope of class)
Ao
A*
DE
dE
A
l (nm)
dl

## Slide 5: Absorption Based Measurements Beer’s Law
Light intensity in = Po
Light intensity out = P
Transmittance = T = P/Po
Absorbance = A = -logT
Light source
Absorbance used because it is proportional to concentration
A = εbC
Where ε = molar absorptivity and b = path length (usually in cm) and C = concentration (M)
b
ε = constant for given compound at specific λ value
sample in cuvette
Note: Po and P usually measured differently
Po (for blank)
P (for sample)

## Slide 6: Beer’s Law – Specific Example
A compound has a molar absorptivity of 320 M-1 cm-1 and a cell with path length of 0.5 cm is used. If the maximum observable transmittance is 0.995, what is the minimum detectable concentration for the compound?

## Slide 7: Beer’s Law – Best Region for Absorption Measurements
Determine the best region for most precise quantitative absorption measurements if uncertainty in transmittance is constant
A
% uncertainty
0
2
High A values - Poor precision due to little light reaching detector
Low A values – poor precision due to small change in light

## Slide 8: Beer’s Law – Deviations to Beer’s Law
A. Real Deviations
- Occur at higher C
- Solute – solute interactions become important
- Also absorption = f(refractive index)

## Slide 9: Beer’s Law – Deviations to Beer’s Law
B. Apparent Deviations
1. More than one chemical species
Example: indicator (HIn)
HIn ↔ H+ + In-
Beer’s law applies for HIn and In- species individually: AHIn = ε(HIn)b[HIn] & AIn- = ε(In-)b[In-]
But if ε(HIn) ≠ ε(In-), no “Net” Beer’s law applies Ameas ≠ ε(HIn)totalb[HIn]total
Standard prepared from dilution of HIn will have [In-]/[HIn] depend on [HIn]total
In example, ε(In-) = 300 M-1 cm-1
ε(HIn) = 20 M-1 cm-1; pKa = 4.0

## Slide 10: Beer’s Law – Deviations to Beer’s Law
More than one chemical species:
Solutions to non-linearity problem
Buffer solution so that [In-]/[HIn] = const.
Choose λ so ε(In-) = ε(HIn)

## Slide 11: Beer’s Law – Deviations to Beer’s Law
B. Apparent Deviations
2. More than one wavelength
ε(λ1) ≠ ε(λ2)
λ1
λ2
Example where ε(λ1) = 3*ε(λ2)
line shows expectation where ε(λ1) = ε(λ2) = average value
Deviations are largest for large A
A
λ
Notes: 11

## Slide 12: Beer’s Law – Deviations to Beer’s Law
More than one wavelength - continued
When is it a problem?
a) When polychromatic (white) light is used
b) When dε/dλ is large (best to use absoprtion maxima) and Δλ is not small (Δλ is the range of wavelengths passed to sample)
c) When monochromator emits stray light
d) More serious at high A values

## Slide 13: Beer’s Law – Selection of Wavelengths for Quantitative Purposes
How can we apply our knowledge to best analyze 2 or more compounds?
Selection of l values depends on:
  selectivity (isolated peaks best)
  sensitivity (tallest peaks best)
  possible deviations to Beer’s Law (broader peaks better, sloped regions bad)
Absorbance
Wavelength
compound A
Compound B

## Slide 14: Luminescence Spectroscopy
Advantages to Luminescence Spectroscopy
1. Greater Selectivity (most compounds do not efficiently fluoresce)
2. Greater Sensitivity – does not depend on difference in signal; with sensitive light detectors, low level light detection possible
Absorption of light
95% transparent
(equiv. to A = 0.022)
Weak light in black background
Emission of light

## Slide 15: Chapter 19 - Spectrometers
Main Components:
1) Light Source (produces light in right wavelength range)
2) Wavelength Descriminator (allows determination of signal at each wavelength)
3) Sample (in sample container)
4) Light Transducer (converts light intensity to electrical signal)
5 )Electronics (Data processing, storage and display)
Example: Simple Absorption Spectrophotometer
Light Source
(e.g tungsten lamp)
Monochromator
Sample
detector (e.g. photodiode)
Electronics
single l out

## Slide 16: Spectrometers
Some times you have to think creatively to get all the components.
Example NMR spectrometer:
Light source = antenna (for exciting sample, and sample re-emission)
Light transducer = antenna
Electronics = A/D board (plus many other components)
Wavelength descriminator =
Fourier Transformation
Radio Frequency Signal Generator
Antenna
A/D Board
Fourier Transformed Data

## Slide 17: Spectrometers – Fluorescence/Phosphorescence
Fluorescence Spectrometers
  Need two wavelength descriminators
  Emission light usually at 90 deg. from excitation light
  Can pulse light to discriminate against various emissions (based on different decay times for different processes)
  Normally more intense light and more sensitive detector than absorption measurements since these improve sensitivity
lamp
Excitation
monochromator
sample
Emission monochromator
Light detector

## Slide 18: Absorption Spectrometers
Sensitivity based on differentiation of light levels (P vs P0) so stable (or compensated) sources and detectors are more important
Dual beam instruments account for drifts in light intensity or detector response
Light Source
(tungsten lamp)
Monochromator
Sample
Electronics
chopper or beam splitter
Reference
detector

## Slide 19: Some Questions
Does the intensity of a light source have a large effect on the sensitivity of a UV absorption spectrometer? What about a fluorescence spectrometer?
If a sample is known to fluoresce and phosphoresce, how can you discriminate against one of these processes?
If a sample can both fluoresce and absorb light, why would one want to use a fluorescent spectrometer?
What is the advantage of using a dual beam UV absorption spectrometer?
List 5 components of spectrometers.
Why could the use of a broad band light source in the absence of wavelength discrimination lead to poor quantification of light absorbing constituents?