## Slide 1: Chem. 133 – 4/11 Lecture

## Slide 2: Announcements
Homework due 4/13 (2 problems)
Quiz also on 4/13
4/13 Lecture may be guest lecture (Dr. Miller-Schulze on mass spectrometry)
Today’s Lecture
  NMR Spectroscopy (Rubinson & Rubinson Ch. 11)
    Theory
    Effect of Environment on Spectra
    Spin-Spin Coupling
    Instrumentation (if time)

## Slide 3: NMR Spectrometry Some Questions
Modern NMRs continuously monitor 2H absorbance to account for magnetic field drift in the “lock” unit. The frequency of the 2H signal is observed to drift by 30Hz over 1 hour. Given the magnetic field H0= 8.45 T, γ(2H) = 8.22 x 107 radian T-1 s-1 and γ(1H) = 2.68 x 108 radian T-1 s-1, calculate the magnetic field drift and the drift in the 1H frequency in an hour.
17O has an I value of 5/2. How many spin states will it have?
Explain why sensitivity is increased by going to a larger magnetic field.
Will increasing the temperature increase or decrease NMR sensitivity (assuming it has no effect on relaxation processes)?

## Slide 4: NMR Spectrometry Another Question
An 1H nucleus relaxes with a characteristic time of 380 ms. What is the narrowest peak width expected in a spectrum? If this resolution can just be achieved with the instrument at an 1H frequency of 300 MHz, what would be the resolution of the NMR instrument?

## Slide 5: NMR Spectrometry Effect of Environment on Nuclei
Use of NMR for elemental analysis (spectrum shown previously) is of limited use
However, nuclei of given elements also can be affected by their chemical environment (although these effects are very small compared to element – element comparisons)
Both electrons surrounding the nucleus as well as less confined electrons in molecules can affect the magnetic field at the nucleus (our previous assumption that Hnucleus = H0 = HApplied is no longer valid)

## Slide 6: NMR Spectrometry Effect of Environment on Nuclei
Use of NMR for elemental analysis (spectrum shown previously) is of limited use
However, nuclei of given elements also can be affected by their chemical environment (although these effects are very small compared to element – element comparisons)
Both electrons surrounding the nucleus as well as less confined electrons in molecules can affect the magnetic field at the nucleus (our previous assumption that Hnucleus = H0 = HApplied is no longer valid)

## Slide 7: NMR Spectrometry Effect of Environment on Nuclei
Simple example of effect on 1H nuclei
  1H+ (g) (no effects of electrons)
  1H (g)
    applied magnetic field induces electron circulation
    electron circulation induces magnetic field
    Induced magnetic field “shields” nucleus from HApplied (note H0 = const.)
    H0 < HApplied
    (upfield shift)
1H+
HApplied
HApplied
H0 = HApplied
1H+ (g) H0 = HApplied
1H
e-
Hinduced
H0
1H (g)
Hshielding

## Slide 8: NMR Spectrometry Effect of Environment on Nuclei
More complicated example: CH3CH2CH2Cl
  all Hs shielded by C – H σ bond electrons
  shielding from electrons weaker for Hs nearer to Cl due to electron withdrawing nature of Cl
  term for shift for Hs closer to Cl is “deshielding”
Low Resolution Spectrum (no splitting shown)
H
Note on scale: - neither T nor Hz typically used for x-axis
Instead: ppm = (nsample – nstandard)*106/n

## Slide 9: NMR Spectrometry Magnetic Anisotropy
Besides effects from electron withdrawing (or electron supplying), electron currents outside of the σ bonds can affect H0
This can occur from the induction of larger scale electron circulations
Example: benzene ring (δ ~ 7 to 8 ppm – much greater than expected based on local electron density)
H
H
H
H
H
H
HApplied
p-orbitals
π electrons circulate
This induces magnetic field in same direction as Happlied
e-
Effect is the same as deshielding and similar electron currents can originate in alkenes and alkynes

## Slide 10: NMR Spectrometry Other Effects on Spectra
Number of peaks (equal to number of equivalent nuclei)
Peak position (discussed already)
Peak area
  Proportional to number of nuclei of given type/environment (for 1H, not typical for 13C)
  Given by integration
Peak width (affected by relaxation)
Multiplets (next slide)

## Slide 11: NMR Spectrometry Spin – Spin Coupling
We have seen that both H σ bond electrons and neighboring π bond electrons affect H0.
In addition, neighboring NMR active nuclei affect H0.
Example: CHCl2CH2Br
  CH2Br protons are affected by spin of CHCl2 proton (so split into two peaks from spin up and spin down CHCl2 proton)
  CHCl2 proton is affected by two CH2Br protons (three possibilites: two spins up, spins up and down, two spins down)
  Spin up + spin down twice as likely because either nuclei can be spin up
Low Resolution
H0
-CHCl2
-CH2Br
H0
Opposing spins

## Slide 12: NMR Spectrometry Spin – Spin Coupling
Example: CHCl2CH2Br
  Energy view of spin-spin splitting
  CH2Br nuclei can be aligned with or against the magnet
  Each CH2Br state is slightly higher or lower depending on state of CHCl2
  When all spins are “up”, the energy is the lowest
  The unaligned CH2Br (1H) is similarly affected
  Transitions only involve the CH2Br nuclei (see plot) – the CHCl2 nuclei can’t flip
  Splitting of CHCl2 by CH2Br is similar
Ho
CH2Br
CHCl2
E
Down-field coupling
Up-field coupling

## Slide 13: NMR Spectrometry Spin – Spin Coupling
Both homonuclear (1H – 1H) and heteronuclear (1H – 19F) splitting can occur (although homonuclear splitting is more common)
Nuclei must be close enough for magnetic fields to be observable (normally 3 bonds or less for 1H – 1H)
The number of split peaks = n + 1 for n neighboring equivalent nuclei (only for I = ½ nuclei causing splitting)
The distance between split peaks is constant in Hz (not ppm) and is the same for both nuclei (e.g. splitting constant for A proton caused by B proton will be the same for both A and B protons)
In the case of one set of equivalent nuclei causing splitting, you should be able to predict the pattern caused
If more than one set of nuclei cause splitting, the result is “complex” (although you can predict number of peaks if splitting constants are similar)

## Slide 14: NMR Spectrometry Interpretation Examples
Predict Spectra (# equivalent peak, relative locations of peaks, relative peak areas, and splitting patterns) for the following compounds:
  CH3CHBrCH3
  (CH3)2CHCOCH3
  CH3CH2OCH2F
  (CH3)2C=CHCH3
  CHDClOCH3
  CH3CH2CHBr2
  ClCH2CHClF
What type of groups caused this:
Notes: 14

## Slide 15: NMR Spectrometry Instrumentation
Magnet
  Needs a) high field strength and b) very homogeneous field
  Why high field strength?
    greater sensitivity (N*/N0 lower with higher B0)
    easier to resolve overlapping peaks
    (δ const. in ppm, J in Hz)
TMS
overlapping peak of ethyl group
J = 7 Hz
2.35 T Magnet (100 MHz)
Δδ = 0.14 ppm (14 Hz)
J = 7 Hz
Δδ = 0.14 ppm = 70 Hz
11.8 T Magnet (500 MHz)
no longer overlapping

## Slide 16: NMR Spectrometry Instrumentation
Magnet (cont.)
  Why homogeneous field?
    needed to obtain high resolution
    example, to resolve 2 Hz splitting in a 600 MHz instrument, a resolution required is 600,000,000/2 = 3 x 108; so magnetic field (H0) must vary by less than 1 part in 300,000,000 over the region where the sample is detected
    done by shims (small electromagnets in which current is varied) and spinning sample (to reduce localized inhomongenieties)

## Slide 17: NMR Spectrometry Instrumentation
Light Source
  Radio waves produced by RF AC current with antenna
  Continuous in CW (continuous wave) instruments
  Pulsed in FT (Fourier Transform) Instruments
Sample
  Typically contains: active nuclei, sample matrix, and deuterated solvents (for proton NMR)
  Deuterated solvent used to reduce interference and to use “lock” (CW NMR to locate frequency based on D signal)
Light Detector
  same antenna producing light (at least in FT NMR)