## Slide 1: Chem. 133 – 4/18 Lecture

## Slide 2: Announcements I
Pass Back Quiz and Last Homework (solutions posted on SacCT)
Exam 2
  Next Tuesday
  Covering Spectroscopy Chapters (Harris 17, 19, and 20 and NMR) and Mass Spectrometry (Harris Ch. 21 – at least most of it)
Today’s Lecture
  NMR – Questions and Instrumentation

## Slide 3: Announcements II
Today’s Lecture – cont.
  Mass Spectrometry
    Instrmentation – Analyzers
    Resolution
    Isotope Effects

## Slide 4: NMR Spectrometry Interpretation Examples
Predict Spectra (# equivalent peak, relative locations of peaks, relative peak areas, and splitting patterns) for the following compounds:
  CH3CHBrCH3
  (CH3)2CHCOCH3
  CH3CH2OCH2F
  (CH3)2C=CHCH3
  CHDClOCH3
  CH3CH2CHBr2
  ClCH2CHClF
What type of groups caused this:
Notes: 4

## Slide 5: NMR Spectrometry Instrumentation
Magnet
  Needs a) high field strength and b) very homogeneous field
  Why high field strength?
    greater sensitivity (N*/N0 lower with higher B0)
    easier to resolve overlapping peaks
    (δ const. in ppm, J in Hz)
TMS
overlapping peak of ethyl group
J = 7 Hz
2.35 T Magnet (100 MHz)
Δδ = 0.14 ppm (14 Hz)
J = 7 Hz
Δδ = 0.14 ppm = 70 Hz
11.8 T Magnet (500 MHz)
no longer overlapping

## Slide 6: NMR Spectrometry Instrumentation
Magnet (cont.)
  Why homogeneous field?
    needed to obtain high resolution
    example, to resolve 2 Hz splitting in a 600 MHz instrument, a resolution required is 600,000,000/2 = 3 x 108; so magnetic field (H0) must vary by less than 1 part in 300,000,000 over the region where the sample is detected
    done by shims (small electromagnets in which current is varied) and spinning sample (to reduce localized inhomongenieties)

## Slide 7: NMR Spectrometry Instrumentation
Light Source
  Radio waves produced by RF AC current with antenna
  Continuous in CW (continuous wave) instruments
  Pulsed in FT (Fourier Transform) Instruments
Sample
  Typically contains: active nuclei, sample matrix, and deuterated solvents (for proton NMR)
  Deuterated solvent used to reduce interference and to use “lock” (CW NMR to locate frequency based on D signal)
Light Detector
  same antenna producing light (at least in FT NMR)

## Slide 8: NMR Spectrometry Instrumentation
Interaction of light with sample in FTNMR
  Numerous precessing nuclei can be represented by net vector
  RF pulse causes rotation about x-axis (in y-z plane)
  During relaxation back to ground state, RF signal is “picked up” (antenna picks up y-axis component)
B0
z
x
y
supposed to be spiral path made vector head

## Slide 9: NMR Spectrometry Instrumentation
Electronics for Detection
  Antenna picks up RF signal pulse
  RF is difficult to digitize
  So signal split into RF component and lower frequency component
  Lower frequency component is digitized (this is observed FID)
  Digitized signal is then processed (filtered by exponential multiplication and Fourier transformed to to frequency domain)
antenna
Removal of RF signal
Low frequency signal
Conversion to digital
Fourier Transformed Data
Signal Splitting

## Slide 10: NMR Spectrometry Additional Topics
13C NMR
  Lower sensitivity due to lower frequency and lower abundance
  Useful for determining # equiv. C atoms, types of functional groups (particularly for C atoms with no protons attached like C-CO-C)
  Typically done with proton decoupling (removing splitting caused by neighboring protons) to enhance sensitivity
Solids Analysis
  Suffers from wide peak width
  Peak width made narrow by using “magic angle” spinning
Spin Decoupling and 2-Dimensional Methods
  Used to determine connectivity between protons

## Slide 11: NMR Spectrometry Some Questions
The use of a more powerful magnet will result in better sensitivity and better resolution (separation of protons from different environments). Explain why.
What is magnetic field homogeneity and why is it important in NMR? If it is not good, what is the effect?
Why are more repeated scans typically used for 13C NMR?

## Slide 12: Mass Spectrometry Questions – Covered Last Time??
Which ionization method can be achieved on solid samples (without changing phase)
If one is using GC and concerned about detecting the “parent” ion of a compound that can fragment easily, which ionization method should be used?
For a large, polar non-volatile molecule being separated by HPLC, which ionization method should be used?
When analyzing a large isolated peptide by ESI-MS, multiple peaks are observed (at smaller than parent ion mass numbers). What is a possible cause for this?
What ionization method should be used to analyze for lead in a sample?

## Slide 13: Mass Spectrometery Instrumentation
Analyzers
  Separates ions based on mass to charge ratio
  All operate at very low pressures (vacuums) to avoid many ion – ion or ion – molecule collisions
  Analyzers for chromatographic systems must be fast. (If a peak is 5 s wide, there should be 4 scans/s)
  Most common types (as chromatographic detectors):
    Quadrupole (most common)
    Ion Trap (smaller, MS-MS capability)
    Time of Flight (higher speed for fast separations and can be used for high resolution applications)

## Slide 14: Mass Spectrometery Instrumentation
Mass Spectrometer Resolution
  R = M/ΔM where M = mass to charge ratio and is ΔM difference between neighboring peaks (so that valley is 10% or 50% of peak height – see text for exact defintion).
  Standard resolution needed:
    To be able to tell apart ions of different integral weights (e.g. (CH3CH2)2NH – MW = 73 vs. CH3CH2CO2H – MW = 74)
    More important to have higher resolution when analyzing larger compounds (e.g. a resolution of 1000 would be sufficient for GC-MS but not for LC-MS)
  High Resolution MS:
    To be able to determine molecular formulas from “exact” mass
    example: CH3CH2CO2H vs. CHOCO2H; both nominal masses are 74 amu but CHOCO2H weighs slightly less (74.037 vs. 74.000 amu) because 16O is lighter than 12C + 41H (Note: need to use main isotope masses to calculate these numbers – not average atomic weights). Needed resolution = 74/0.037 = 2000
    Resolution > about 104 to 105 is normally needed.

## Slide 15: Mass Spectrometery High Resolution
Calculation of Exact Mass
  Several compounds can have a molecular weight of 84
  Examples:
    C6H12
    C5H8O
    C4H4O2
    C4H4S
    CH2Cl2
  Each example above will have slightly different mass
  (go over mass calculations on board)

## Slide 16: Mass Spectrometery Isotope Effects
It also may be possible to distinguish compounds based on isotopic composition
Compounds in high resolution example will have different expected M+1/M and M+2/M ratios (which will NOT require high resolution to see)
Text does not explain calculations that well
Go over calculations for CH3Cl, CH2BrCl, and CHCl3

## Slide 17: Mass Spectrometery Other Topics – Multiple Charges in ESI
In ESI analysis of large molecules, multiple charges are common due to extra (+) or missing (-) Hs (or e.g. Na+)
The number of charges can be determined by looking at distribution of big peaks
For + ions m/z = (M+1.008n)/n (most common)
For – ions m/z = (M–1.008n)/n
Ion current
m/z
Dm/z
(M+n)/n
(M+n+1)/(n+1)
Example: m/z peaks =711.2, 569.3, 474.8, 407.1
I am only showing an “approximate” method for determining n and M – this usually will work when H+ is causing the charging, but not if Na+ causes charging