## Slide 1: Chem. 133 – 4/27 Lecture

## Slide 2: Announcements I
Exam 2
  Pass back
  Average = 77%
Homework Set 3 – Posted
Last Quiz; next week
Exam Range | N
90-92 | 1
80s | 3
70s | 6
<70 | 2

## Slide 3: Announcements II
Today’s Lecture
  Mass Spectrometry
    Isotope Effects
    Multiple charging
    MS-MS and other topics
  Chromatography
    Overview
    Partitioning

## Slide 4: Mass Spectrometery Isotope Effects
It also may be possible to distinguish compounds based on isotopic composition
Compounds in high resolution example will have different expected M+1/M and M+2/M ratios (which will NOT require high resolution to see)
Text does not explain calculations that well
Go over calculations for CH3Cl, CH2BrCl, and CHCl3

## Slide 5: Mass Spectrometery Other Topics – Multiple Charges in ESI
In ESI analysis of large molecules, multiple charges are common due to extra (+) or missing (-) Hs (or e.g. Na+)
The number of charges can be determined by looking at distribution of big peaks
For + ions m/z = (M+1.008n)/n (most common)
For – ions m/z = (M–1.008n)/n
Ion current
m/z
Dm/z
(M+n)/n
(M+n+1)/(n+1)
Example: m/z peaks =711.2, 569.3, 474.8, 407.1
I am only showing an “approximate” method for determining n and M – this usually will work when H+ is causing the charging, but not if Na+ causes charging

## Slide 6: Mass Spectrometery Questions - #2
A modification is made in a peptide chain of molecular weight 1503 (native form), in which one threonine residue (NH3CH(CHCH3(OH))CO2) is replaced with cysteine (NH3CH(CH2SH)CO2). What resolution is needed to separate the native peptide from the modified peptide?
Predict the M+1/M, M+2/M, M+3/M, and M+4/M ratios for the ion C4H7S2O3-.

## Slide 7: Mass Spectrometery Other Topics - MS-MS
In LC-ESI-MS, little fragmentation occurs making determination of unknowns difficult
In LC-ESI-MS on complicated samples, peak overlap is common, with interferants with the same mass possible (e.g. PBDPs)
In both of above samples, using MS-MS is useful
This involves multiple passes through mass analyzers (either separate MSs or reinjection in ion-trap MS) and is termed MS-MS
Between travels through MS, ions are collided with reagent gas to cause fragmentation

## Slide 8: Mass Spectrometery Interpretation Questions
Determine the identity of the compound giving the following distribution:
m/z | Abundance (% of biggest)
25 | 14
26 | 34
27 | 100
35 | 9
62 | 77
64 | 24

## Slide 9: Mass Spectrometery Interpretation Questions – cont.
2. Determine the identity of the compound giving the following distribution:
m/z | Abundance (% of biggest)
29 | 9.2
50 | 30.5
51 | 84.7
77 | 100
93 | 16
123 | 39

## Slide 10: Chromatography Overview
Chromatography is an area of “Separation Science”
Separation Science also includes other separation techniques (both instrumental, like capillary electrophoresis, and non-instrumental, like liquid-liquid extraction)
Main Purposes of Separations
  Quantitative or qualitative analysis of unknown mixtures
  Isolation of compounds (e.g. from reactions or from biological samples)
Main advantage/disadvantage vs. other methods:
  Better for complex samples (separation gives selectivity)
  Time required for separation to occur

## Slide 11: Chromatography Instrument Overview
Chromatograph = instrument
Chromatogram = detection vs. time (vol.) plot
Chromatograph Components
Mobile Phase Reservoir
Flow/Pressure Control
Sample In
Injector
Chromatographic Column
Detector
Waste or fraction collection
Signal to data recorder
Chromatogram

## Slide 12: Chromatography Partition Theory
All Chromatographic separations involve partitioning between distinct phases (mobile phase and stationary phase)
The first part of Chapter 22-1 deals with liquid – liquid extractions (covered only for understand of partitioning)
Liquid-liquid extraction involves two liquid phases (top phase is less dense)
An analyte (X) will partition between the two phases until equilibrium is reached
Phase 1 = initial (or raffinate) phase, phase 2 = extract phase, K = partition coefficient = constant
X(org)
X(aq)
organic phase
aqueous phase

## Slide 13: Chromatography Partition Theory
Partitioning between phases is more complicated when analyte changes forms in one phase
Example: phenol (HA) extraction from water to octanol
  partitioning of HA reaches an equilibrium
  however, HA can exist as HA (acid form) or A- (base form)
  A- only will exist in water, not in octanol (KA- = 0)
  A distribution coefficient, D, describes the partitioning of total forms of phenol between two phases
  While K is pH independent, D depends on pH (lower equation derived from combining D equation with Ka equation)
  D ~ K at low pH, while at high pH, D gets small

## Slide 14: Chromatography Questions on Partition Theory
The compound 1-butanol has a hexane – water partition ratio (K = [1-but]hexane/[1-but]water) of 11. Will its partition ratio for diethyl ether – water be greater or smaller?
Methyl and ethyl amines are indicators of fish spoilage and are basic (conjugate acids have pKa values around 10 to 11). It is desired to remove the amines from hydrophobic compounds in fish by liquid – liquid extraction using ethyl acetate and water. What pH should be used and in which phase will the amines reside?
Notes: 14

## Slide 15: Chromatography Separation Theory: The good, the bad and the ugly
The Good: Separation based on differential partitioning (differences in K)
The Bad: Band Broadening (limits separation efficiency and dilutes analytes)
The Ugly: Non-ideal behavior (causes non-Gaussian peak shapes)

## Slide 16: Chromatography Partition Theory
Partitioning in Chromatographic Columns
  K = [X]s/[X]m where s is for stationary phase and m is for mobile phase
  Above equation is designed where mobile and stationary phases are liquids, but a related equation can be used with other phases
  K value affects how long it takes a solute to go through column because the solute is only moving when it is in the mobile phase
  Solutes with larger K values (e.g. Y below) move through columns more slowly
X
Y

## Slide 17: Chromatography Basis for Separation
The partition coefficient (K) is not used that much in chromatography
In its place is k, the retention factor
k = ns/nm where n = moles of analyte (in stationary and mobile phases)
k is used because it is easily measured
tr = retention time = total time spent on column
tm = time required for mobile phase to flow through column (every compound spends the same time in the mobile phase)

## Slide 18: Chromatography More on Stationary Phases
Open Tubular
(end on, cross section view)
Column Wall
Mobile phase
Stationary phase (wall coating)
Packed column (side view) (e.g. Silica in normal phase HPLC)
Packing Material
Stationary phase is outer surface
Bonded phase (liquid-like)
Expanded View
Stationary Phase
Chemically bonded to packing material
Packing Material
View showing pores

## Slide 19: Chromatography Parameters from Chromatograms
Determination of parameters from reading chromatogram (HPLC example)
tM = 2.37 min. (normally determined by finding 1st peak for unretained compounds – contaminant below)
1st peak, tR = 4.96 min.
k (1st peak) = (4.96 -2.37 min.)/2.37 min. = 1.09