## Slide 1: Chem. 133 – 5/4 Lecture

## Slide 2: Announcements
Homework Set 3 – due date for collected homework: 5/9
Last Quiz – Today
Today’s Lecture
  Chromatography
    Partitioning and Retention (just final questions
    Selectivity
    Band broadening

## Slide 3: Chromatography Some Questions – Did 1st 2 last time
List 3 main components of chromatographs.
A chemist purchases a new open tubular GC column that is identical to the old GC column except for having a greater film thickness of stationary phase. How will the following parameters will be affected (assuming column run as before): K, k, tM, tR(component X)?
What “easy” change can be made to increase k in GC? In normal phase HPLC using a hexane/ethylacetate mobile phase?
A GC is operated close to the maximum column temperature and for a desired analyte, k = 10. Is this good? What change could be made to improve the analysis?

## Slide 4: Chromatography Selectivity
Selectivity is given by a= relative retention (also called selectivity coefficient)
a = ky/kx (where tr(y) > tr(x))
A larger a value means a better separation. An a value close to 1 means a difficult separation.
Note that a = Ky/Kx also applies

## Slide 5: Chromatography Selectivity – cont.
Determination of parameters from reading chromatogram (HPLC example)
a (for 1st 2 peaks) = kB/ kA = tRB’/ tRA’ = (5.757 – 2.374)/(4.958 – 2.374) = 1.31

## Slide 6: Chromatography Selectivity - Continued
How can a be increased?
  Not always easy to increase
  In GC, a new column often is needed (a only changes if Kx and Ky change with T differently – e.g. have different heats of vaporization)
  Example:
    Separation of hexane from acetone
    Both have similar boiling points
    With a weakly polar column a is near 1, but going to a polar column will cause greater retention of acetone.

## Slide 7: Chromatography Selectivity - Continued
How can a be increased?
  Mobile phase changes often can be used in HPLC (no need for column change)
  Possible changes:
    change in pH (e.g. adjust retention of weak acids by changing % in ion form)
    different analyte – solvent interactions
    for reversed phase, 3 common organic solvents are acetonitrile, methanol, and tetrahydrofuran (THF)

## Slide 8: Chromatography Selectivity - Continued
a values – research example for HPLC
Fatty acid separation example: - separating C16:0 (HO2C(CH2)14CH3) from C18:1 (HO2C(CH2)6CH=CH(CH2)6CH3) fatty acids with organic plus aqueous formic acid
  When using formic acid and acetonitrile, small a value
  Replacement of methanol for acetonitrile improves a value
Example chromatogram – looks similar to this when used acetonitrile + formic acid
C16 + C18:1
Note: actually went to 14% FA(aq) /21.5% acetonitrile/64.5% methanol to decrease tailing with methanol
C18:1
C16

## Slide 9: Chromatography Band Broadening – The Bad
Original theory developed from number of simple separation steps (e.g. from fractional distillation columns)
N = number of theoretical plates (or now plate number) = best absolute measure
N = 16(tr/w)2 or = 5.55(tr/w1/2)2
  w = peak width at baseline
  w1/2 = peak width at half height

## Slide 10: Chromatography Shape of Chromatographic Peak
Gaussian Distribution
Normal Distribution Area = 1
Widths
  σ (std deviation)
  w = 4σ
  w1/2 = 2.35σ
  w’ = Area/ymax = 2.51σ (commonly given by integrators)
Gaussian Shape (Supposedly)
2σ
Inflection lines
w
Height
Half Height
w1/2

## Slide 11: Chromatography Column Efficiency
Good efficiency means:
  Large N value
  Late eluting peaks still have narrow peak widths
Relative measure of efficiency = H = Plate height = L/N where L = column length
H = length of column needed to get a plate number of 1
Smaller H means greater efficiency
Note: H is independent of L, N depends on L
large N Value
low N value

## Slide 12: Chromatography Measurement of Efficiency
Measuring N and H is valid under isocratic/isothermal conditions
Later eluting peaks normally used to avoid effects from extra-column broadening (from injector, detector, etc.)
Example: N = 16(14.6/0.9)2 = 4200 (vs. ~3000 for pk 3)
H = L/N = 250 mm/4200 = 0.06 mm
W ~ 0.9 min

## Slide 13: Chromatography Causes of Band Broadening
There are three major causes of band broadening (according to theory)
These depend on the linear velocity (u = L/tm)
Given by van Deemter Equation:
  where H = Plate Height, and A, B, and C are “constants”

## Slide 14: Chromatography Band Broadening
u
H
Most efficient velocity
A term
B term
C term

## Slide 15: Chromatography Band Broadening
“Constant” Terms
  A term: This is due to “eddy diffusion” or multiple paths
  Independent of u
  Smaller A term for: a) small particles, or b) no particles (best)
X
X
X
dispersion

## Slide 16: Chromatography Band Broadening
B Term – Molecular Diffusion
  Molecular diffusion is caused by random motions of molecules
  Larger for smaller molecules
  Much larger for gases
  Dispersion increases with time spent in mobile phase
  Slower flow means more time in mobile phase
X
X
X
Band broadening

## Slide 17: Chromatography Band Broadening
C term – Mass transfer to and within the stationary phase
  Analyte molecules in stationary phase are not moving and get left behind
  The greater u, the more dispersion occurs
  Less dispersion for smaller particles and thinner films of stationary phase
X
X
dispersion
Column particle