## Slide 1: Chem. 133 – 5/9 Lecture

## Slide 2: Announcements I
Homework Set 3 – due today
Quiz 5 (Ave on Q5 was 1.75) –
Final Exam
  Thursday, May 18th 12:45-2:45
  About 50% Review/50% New Material
  Allowed 1 8.5” x 11” sheet of notes (no equations provided)
  Will review new material on Thursday (5/11)
  Final topic covered will be GC

## Slide 3: Announcements II
Today’s Lecture
  Chromatography (general)
    Band broadening
    Resolution
  Gas Chromatography
    Columns
    Injectors

## Slide 4: Chromatography Measurement of Efficiency
Measuring N and H is valid under isocratic/isothermal conditions
Later eluting peaks normally used to avoid effects from extra-column broadening (from injector, detector, etc.)
Example: N = 16(14.6/0.9)2 = 4200 (vs. ~3000 for pk 3)
H = L/N = 250 mm/4200 = 0.06 mm
W ~ 0.9 min

## Slide 5: Chromatography Causes of Band Broadening
There are three major causes of band broadening (according to theory)
These depend on the linear velocity (u = L/tm)
Given by van Deemter Equation:
  where H = Plate Height, and A, B, and C are “constants”

## Slide 6: Chromatography Band Broadening
u
H
Most efficient velocity
A term
B term
C term

## Slide 7: Chromatography Band Broadening
“Constant” Terms
  A term: This is due to “eddy diffusion” or multiple paths
  Independent of u
  Smaller A term for: a) small particles, or b) no particles (best)
X
X
X
dispersion

## Slide 8: Chromatography Band Broadening
B Term – Molecular Diffusion
  Molecular diffusion is caused by random motions of molecules
  Larger for smaller molecules
  Much larger for gases
  Dispersion increases with time spent in mobile phase
  Slower flow means more time in mobile phase
X
X
X
Band broadening

## Slide 9: Chromatography Band Broadening
C term – Mass transfer to and within the stationary phase
  Analyte molecules in stationary phase are not moving and get left behind
  The greater u, the more dispersion occurs
  Less dispersion for smaller particles and thinner films of stationary phase
X
X
dispersion
Column particle

## Slide 10: Chromatography Some Questions
Column A is 100 mm long with H = 0.024 mm. Column B is 250 mm long with H = 0.090 mm. Which column will give more efficient separations (under conditions for determining H)?
Which van Deemter term is negligible in open tubular GC?
How can columns in HPLC be designed to decrease H? In open tubular GC?
Both using a longer column or using a column of smaller H will improve resolutions. Which method will generally lead to a better chromatogram? Why?

## Slide 11: Chromatography Resolution
Resolution = measure of how well separated two peaks are
Resolution = Δtr/wav (where wav = average peak width) (use this equation for calculating resolution)
RS < 1, means significant overlap
RS = 1.5, means about minimum for “baseline resolution” (at least for two peaks of equal height)

## Slide 12: Chromatography Resolution Example
RS calculation example:
  1st two retained peaks:
    tR(1st pk) = 8.20 min., w (integrator) = w’ = 0.316 min, so w = 0.316·(4/2.5) = 0.505 min.
    tR(2nd pk) = 9.09 min., w = 0.536 min
    Resolution = 0.89/0.521 = 1.70 (neglecting non-Gaussian peak shape)
    Resolution not baseline due to peak tailing
mannosan – 8.20 min.
galactosan – 9.09 min.
main difference: axial – equatorial/axial switch of 2 vs. 4 C OH groups

## Slide 13: Chromatography Optimization – Resolution Equation
Will use equation qualitatively to figure out how to improve chromatograms
How to improve resolution
  Increase N (increase column length, use more efficient column)
  Increase a (use more selective column or mobile phase)
  Increase k values (increase retention)
Which way works best?
  Increase in k is easiest (but only if k is initially small)
  Increase in a is best, but often hardest
  Often, changes in k lead to small, but unpredictable, changes in a
not in version of text we are using
2 for 2nd component to elute

## Slide 14: Chromatography Graphical Representation
Initial Separation
Smaller H (narrower peaks)
Larger k or L - separation increases more than width
Increased alpha (more retention of 2nd peak)

## Slide 15: Chromatography Resolution/Optimization Questions
Why is it usually more difficult to improve the separation factor (a) when there are a larger number of analytes/contaminants?
Why is it effective to increase k to improve resolution ONLY if k is small to begin with?

## Slide 16: Chromatography Optimization – Some Questions
Indicate how the chromatograms could be improved?

## Slide 17: Gas Chromatography (GC) Introduction – Overview of Topics
Applications
  Most common for volatile compounds
  More common for non-polar to moderately polar compounds
Columns (packed vs. open tubular)
Sample Injection
Detectors

## Slide 18: GC Columns
Two Common Formats
  Packed columns (older style)
  Open tubular (typically long columns with small diameters)
Advantages of open tubular columns
  Greater Efficiency
  Better sensitivity with most detectors (due to less band broadening vs. lower mass through column)
Advantage of packed columns
  Greater capacity
Open Tubular
(end on, cross section view)
Column Wall (fused silica)
Mobile phase
Stationary phase

## Slide 19: GC Stationary Phase
Selection of stationary phase affects k and a values
Main concerns of stationary phase are: polarity, functional groups, maximum operating temperature, and column bleed (loss of stationary phase)
Type | Functional Groups | Polarity
OV-1 | methyl | Non-polar
OV-17 | 50% methyl/50% phenyl | Somewhat polar
OV-225 | Cyanopropyl, methyl, and phenyl | More polar
carbowax | Ether groups | polar

## Slide 20: GC Injection
Liquid Samples – Most Common
  Overload (solvent or sample) is a common problem
  split/splitless injector minimizes this (next page)
Gas Samples
  Syringe Injection (standard injector)
  Fixed Loop Injectors (common for HPLC)
  Solid Phase Microextraction (SPME)

## Slide 21: GC Sample Injection – Split/Splitless
outside
Septum
Syringe port
He in
To Column
Split vent
Split valve
liner
Split/Splitless Injectors
  Injectors capable of running in two modes: split and splitless
  Split injections used to avoid overloading columns
Injection Process
  Syringe pierces septum and depressing plunger deposits liquid
  Analyte volatilizes
  Part injected (usually smaller fraction)
  Part passed to vent
  Fraction vented depends on split valve
Notes: 21

## Slide 22: GC Injection
Split injection is used for:
  Higher concentrations
  Smaller diameter (OT) columns
  Greater need for high resolution than high accuracy
In split injection, solvent overload is less problematic
Splitless injection is used for trace analysis (~50% of injected sample put on column)