## Slide 1: Chem. 133 – 5/11 Lecture

## Slide 2: Announcements I
Still grading last homework and make up quiz
Posting solutions of these (soon)
Final Exam
  Thursday, May 18th 12:45-2:45
  About 50% Review/50% New Material
  Allowed 1 8.5” x 11” sheet of notes (no equations provided)
  Reviewing new material (since Exam 2) today
  Final topic covered will be GC

## Slide 3: Announcements II
Today’s Lecture
  Chromatography (general)
    Resolution
  Gas Chromatography
    Columns
    Injectors
  Teaching Evaluations (lecture part only)

## Slide 4: Chromatography Optimization – Resolution Equation
Will use equation qualitatively to figure out how to improve chromatograms (don’t use to calculate RS from chromatograms)
How to improve resolution
  Increase N (increase column length, use more efficient column)
  Increase a (use more selective column or mobile phase)
  Increase k values (increase retention)
Which way works best?
  Increase in k is easiest (but only if k is initially small)
  Increase in a is best, but often hardest
not in version of text we are using
2 for 2nd component to elute

## Slide 5: Chromatography Graphical Representation
Initial Separation
Smaller H (narrower peaks)
Larger k or L - separation increases more than width
Increased alpha (more retention of 2nd peak)

## Slide 6: Chromatography Resolution/Optimization Questions
Why is it usually more difficult to improve the separation factor (a) when there are a larger number of analytes/contaminants?
Why is it effective to increase k to improve resolution ONLY if k is small to begin with?
If the resolution between 2 pairs of peaks is 1.20 with an HPLC column length of 100 mm, what column length (same packing material) is needed to get to a resolution of 1.50?

## Slide 7: Chromatography Optimization – Some Questions
Indicate how the chromatograms could be improved?

## Slide 8: Gas Chromatography (GC) Introduction – Overview of Topics
Applications
  Most common for volatile compounds
  More common for non-polar to moderately polar compounds
Columns (packed vs. open tubular)
Sample Injection
Detectors

## Slide 9: GC Columns
Two Common Formats
  Packed columns (older style)
  Open tubular (typically long columns with small diameters)
Advantages of open tubular columns
  Greater Efficiency
  Better sensitivity with most detectors (due to less band broadening vs. lower mass through column)
Advantage of packed columns
  Greater capacity
Open Tubular
(end on, cross section view)
Column Wall (fused silica)
Mobile phase
Stationary phase

## Slide 10: GC Stationary Phase
Selection of stationary phase affects k and a values
Main concerns of stationary phase are: polarity, functional groups, maximum operating temperature, and column bleed (loss of stationary phase)
Type | Functional Groups | Polarity
OV-1 | methyl | Non-polar
OV-17 | 50% methyl/50% phenyl | Somewhat polar
OV-225 | Cyanopropyl, methyl, and phenyl | More polar
carbowax | Ether groups | polar

## Slide 11: GC Injection
Liquid Samples – Most Common
  Overload (solvent or sample) is a common problem
  split/splitless injector minimizes this (next page)
Gas Samples
  Syringe Injection (standard injector)
  Fixed Loop Injectors (common for HPLC)
  Solid Phase Microextraction (SPME)

## Slide 12: GC Sample Injection – Split/Splitless
outside
Septum
Syringe port
He in
To Column
Split vent
Split valve
liner
Split/Splitless Injectors
  Injectors capable of running in two modes: split and splitless
  Split injections used to avoid overloading columns
Injection Process
  Syringe pierces septum and depressing plunger deposits liquid
  Analyte volatilizes
  Part injected (usually smaller fraction)
  Part passed to vent
  Fraction vented depends on split valve
Notes: 12

## Slide 13: GC Injection
Split injection is used for:
  Higher concentrations
  Smaller diameter (OT) columns
  Greater need for high resolution than high accuracy
In split injection, solvent overload is less problematic
Splitless injection is used for trace analysis (~50% of injected sample put on column)

## Slide 14: Topics Since Exam 2
Mass Spectrometry Topics
  Isotope effect calculations*
  Multiple charging calculations to determine M and z*
  MS-MS use
Chromatography
  Liquid – liquid partitioning equation*
  How reactions in water (e.g. acid/base) affect distribution between two phases
  Partitioning Equation in Chromatography*
  Qualitative understanding of effect of partition coefficient on retention on a chromatographic column
*Means be able to solve problems

## Slide 15: Topics Since Exam 2
Chromatography – cont.
  Determination* and meaning of retention factor
  Factors affecting retention factors in GC and HPLC
  Knowledge of normal and reversed phase HPLC
  Relate partition coefficient and retention factor (including calculation of volumes)*
  Determination* and meaning of relative retention
  Practical ways to change retention in GC and HPLC
  Relationship between volume, flow rate and time*
  What factors affect relative retention
  Meaning of plate number (N) and plate height (H)

## Slide 16: Topics Since Exam 2
Chromatography – cont.
  14. How to calculate N and H from chromatograms*
  Three causes of band broadening and how each depends on flow velocity
  Meaning of resolution and how to calculate it from chromatograms*
  Ways to improve resolution and applications to specific separations
Gas Chromatography
  Advantages of open tubular and packed columns
  Column stationary phases
  Injectors (for different sample types)