## Slide 1: Or….so, when do we get to run the samples?
Prof. Justin P. Miller-Schulze, Ph.D.
CHEM 230
September 16 2014
Solid Phase Extraction (SPE)

## Slide 2: Solid Phase Extraction (SPE)
What is SPE?
Types of SPE
Why do we have to do SPE?
SPE Method Development Example (s)

## Slide 3: What is SPE?
Solid Phase Extraction is Liquid Chromatography (SPE is LC)
  We are forcing the analyte to make a decision between remaining attached to the stationary phase or going with the mobile phase
  In LC, this is upstream of a detector
  In SPE, this is upstream of subsequent sample processing steps

## Slide 4
Samples being extracted (in this case, aqueous water samples)
SPE “cartridges”: plastic tubes filled with specific mass (~250 mg) of a specific solid phase
Vacuum manifold-all the “extracted water” ends up here (combined)-if you wanted the “cleaned up” water, you would need a different set-up!
Vacuum line (with a trap, hopefully!) –this draws the water through the cartridges

## Slide 5: Example of Reversed-Phase SPE Steps

## Slide 6: What is SPE-Loading
Sample (contains analytes and a bunch of other stuff)
Solid Phase-
Can be reversed phase (i.e., C18),
Normal Phase (i.e., silica)
Cation or Anion exchange
(with + or – charge groups)
Plastic or Glass cylinder
Frits (porous grate to keep solid phase from falling out)
The efficiency of the loading step (how many analyte molecules get “stuck” onto the stationary phase) is dependent on the polarity of the:
-Analytes
-Stationary phase
-Mobile phase
You can change all of these!
To Trap Non-polar analytes, you want….
Nonpolar stationary phase and polar mobile phase
To Trap Polar analytes, you want….
Polar stationary phase and nonpolar mobile phase

## Slide 7
What is SPE-Elution
Elution Solvent
If reverse-phase, something like methanol, acetonitrile, etc (relatively polar organic solvent).
Retained compounds-either
undesired (interferences) or
desired (different analyte class from those eluted in elution 1/2/3)
Unretained compounds-analytes of interest in elution solvent matrix (subsequent concentration may be needed)

## Slide 8
Samples being extracted (in this case, aqueous water samples)
SPE “cartridges”: plastic tubes filled with specific mass (~250 mg) of a specific solid phase
Vacuum manifold-all the “extracted water” ends up here (combined)-if you wanted the “cleaned up” water, you would need a different set-up!
Vacuum line (with a trap, hopefully!) –this draws the water through the cartridges

## Slide 9: https://www.youtube.com/watch?v=D6SyHU6CcOU

## Slide 10: SPE Solid Phases
Reversed-Phase Groups
  C18 (most commonly used); best for trapping compounds with alkyl groups
  Phenyl: good for enhanced retention of aromatic compounds
  “Stronger” solvent is less polar
Normal-Phase Groups
  Cyano (-CN)
  Amino (-NH2)
  Hydroxy (diol or SiOH)
  “Stronger” solvent is more polar

## Slide 11: Advanced Extraction Techniques Solid Phase Extraction
Ion Exchange Stationary Phases
  Sulfonate groups common for cation exchange
  Ammonium groups –NR3+ common for anion exchange
  Trapping occurs in low ionic strength solvents; release occurs in high ionic strength
  Weak acids/bases need to be trapped in ion form but also can be released by pH adjustment

## Slide 12
Weak-Cation Exchanger
Since functional group is weak acid
SOMETIMES NEUTRAL,
SOMETIMES NEGATIVE
Strong-Cation Exchanger
Since functional group is strong(er) acid
RARELY NEUTRAL, MOSTLY NEGATIVE
Strong-Anion Exchanger
Since functional group is strong(er) base
RARELY NEUTRAL, MOSTLY POSITIVE
Weak-Anion Exchanger
Since functional group is weaker(er) base
SOMETIMES NEUTRAL,
SOMETIMES POSITIVE
http://www.waters.com/waters/en_US/Oasis-Sample-Extraction-Products/nav.htm?cid=513209

## Slide 13: Example Processing Steps for Cation Exchange
Analytes/Sample Matrix=
amphetamines (1o, 2o amines) in wastewater
Acidify Sample (To make amines +)
Load MCX cartridge (weak cation exchange)
Rinse with low pH organic (2% Formic Acid in methanol)
Elute with high pH organic (2% NH4OH in methanol)
Concentrate under N2
Slide Credit: Prof. Dan Burgard, University of Puget Sound

## Slide 14: Why do we have to do SPE?
Any thoughts?

## Slide 15: Why Do We Have To (or Want To) Do SPE?:
SPE can be used to enrich (increase the concentration of) trace chemical species
SPE can be used to remove interferences and simplify the matrix of the collected sample
  Complex sample matrices = urine, blood, serum, plasma, tissue, sediment…..
SPE can be used to reduce ion suppression in for techniques involving mass spectrometry detection
  Kind of a “sub-reason” of (2)
SPE can be used to separate the sample into different analyte classes
  Polar analytes can be analyze by LC-MS, non-polar analytes by GC-MS, etc.

## Slide 16: SPE can be used to enrich (increase the concentration of) trace chemical species
  Enrich = Concentrate
  i.e., to INCREASE the concentration of the analyte
  In many applications (environmental sample analysis, pharmaceutical applications, biomonitoring, etc.) there is too little of the analyte present to directly analyze collected samples

## Slide 17: SPE can be used to enrich (increase the concentration of) trace chemical species
  We can change some things about the methodology:
    Injection volume of method
    Volume of sample collected
    Volume of final extract
  These factors can make the necessary concentration factor less (i.e., you don’t need to concentrate as much)
  But everything is inter-related, and the method may or may not be amenable to modification
“Pay me now or pay me later…”

## Slide 18: Contaminants of Emerging Concern in Puget Sound: A Comparison of Spatial and Temporal Levels and Occurrence
Justin P. Miller-Schulze, Alex Gipe, Derek Overman, Joel E. Baker
May 2 2014

## Slide 19: Our CECs
CECs are of interest due to their impact on human health, environmental health/ecotoxicology, or source tracing
Our suite of CECs was developed primarily with source tracing in mind, although a few have toxicological relevance
CEC | Use/Application
Acetaminophen | Pain Reliever (Tylenol)
Atrazine | Herbicide
Caffeine | Stimulant
Carbamazepine | Anti-Seizure Medication
Cotinine | Nicotine Metabolite
Ethyl Paraben | Anti Microbial
Ethyl Vanillin | Artificial Flavoring
Ibuprofen | Anti-Inflammatory
Methyl Paraben | Anti Microbial
Mecoprop | Herbicide
Nicotine | Stimulant
Paraxanthine | Caffeine Metabolite
Ensulizole | UV Filter (Sunscreen Agent)
Propyl Paraben | Anti Microbial
Ractopamine | Feed Additive (Swine)
Sulfadimethoxine | Antibiotic (animal)
Sulfamethoxazole | Antibiotic (human)
Sulfamethazine | Antibiotic(animal)
Sucralose | Artificial Sweetener
Theobromine | Caffeine Metabolite/ Chocolate Ingredient

## Slide 20
Filtration
Spike w/ isotopically-labeled recovery surrogates
Filter (0.7, 0.45, 0.2 µm pore size in sequence)
removes dissolved matter and some biological material
pH
Stabilize pH at
8 ± 0.1
Extraction
Extraction with nonpolar “Oasis HLB” solid phase extraction cartridge concentrates analytes and removes (some) sample matrix interferences
Elution + Evaporation
Samples are eluted with organic solvent (methanol and/or methanol/MTBE mixture) and then concentrated to ~150 µl
Final
Sample Matrix
Preparation
150 µl sample is brought up to 1500 µl with pH = 2.8 acetic acid and spiked with 10 µl
Internal standard mixture
Measurement by HPLC-MS/MS
Samples collected in 1liter LDPE cubitainers or 1250 ml glass bottles
~18 samples = ~20 person-hours of lab time

## Slide 21: Typical concentrations of environmental tracers: Parts per trillion or nanograms per liter (ng/L) 1 part per trillion corresponds to about 3 seconds in 100,000 years OR 1 drop of water (50 µl) in 20 Olympic sized swimming pools
Some chemical tracers:
200 mg caffeine/cup of coffee
200 mg ibuprofen/tablet
325 mg acetaminophen/
Regular Strength Tylenol
(500 mg/ Extra Strength)
~50 mg sucralose/1 packet Splenda
SPE may be necessary to enrich the concentration of the analytes in the collected sample

## Slide 22: Sounds like a lot of work…and it is!
But it’s necessary:
Because the concentrations of these EC Tracers in the environment should be ~1 ng/L or less.
The injection volume of our final extract is 20 µl-at a nominal environmental sample concentration of 1 ng/L, this pencils out to a 2 femtogram injection
1 fg = 1 x 10-15 grams
So, in order to see the levels present in mixed surface and/or groundwater, we need this 1000-fold concentration factor
Volume =
1 ml
Volume =
1000 ml
COLLECTED SAMPLE
SAMPLE
EXTRACT

## Slide 23: SPE can be used to enrich (increase the concentration of) trace chemical species
Example Limit of Detection of a Mass Spectrometry-based detector method (i.e., GC-MS):
1 pg on column
Example GC-MS injection volume:
2 µl
Typical concentration of environmental tracer in water:
1 ng/L
Two good test questions (to me at least):
  True/False: The concentration of this tracer is high enough to be detected at a concentration above the LOD with out enrichment?
  If the answer to (1) is FALSE, what is the necessary amount of enrichment for this sample?

## Slide 24: Enrichment Sample Problem
  The method LOD for caffeine in surface water for an HPLC-MS/MS method is 25.00 ng/ml (concentration in the sample extract) What is the necessary amount of enrichment for this sample if 1250 ml of water is collected as a sample and the anticipated concentration range is 15.00-1300 ng/L in the samples?
  (The injection volume for this method is 15 µl)

## Slide 25: SPE can be used to remove interferences and simplify the matrix of the collected sample
Removal of interfering compounds by SPE (interferences stuck to SPE cartridge, and not eluted, or pass-through upon loading)
http://www.waters.com/waters/en_US/SPE---Sample-Enrichment-and-Purification-using-Solid-Phase-Extraction/nav.htm?cid=10083488

## Slide 26: A Few (personally) Relevant Examples
SPE may be necessary to remove matrix interferences/simplify the sample matrix (as in a sample matrix of urine

## Slide 27: SPE can be used to reduce ion suppression in for techniques involving mass spectrometry detection
http://www.waters.com/waters/en_US/SPE---Sample-Enrichment-and-Purification-using-Solid-Phase-Extraction/nav.htm?cid=10083488

## Slide 28: SPE can be used to separate the sample into different analyte classes
http://www.waters.com/waters/en_US/SPE-Method-Development/nav.htm?cid=10083845

## Slide 29: SPE Issues/Specific Method Development Issues
Sometimes, you are looking for 4 of the same class of analytes
  Good for you!
Other times, you are looking for a variety of analyte classes: weak bases, weak acids, zwitterions, etc.
  I’m sorry…

## Slide 30: Wastewater Tracers
Nicotine/Cotinine: Stimulant/
stimulant metabolite
Sucralose: Low-calorie
sweetener
Caffeine/Paraxanthine: Stimulant/stimulant metabolite

## Slide 31: Sulfonamide Antibiotics
Sulfamethoxazole: Human and veterinary antibiotics
Sulfamethazine: Widely used veterinary antibiotic for meat-producing animals
Sulfadimethoxine: Veterinary antibiotic, approved for human use in some countries (Russia)

## Slide 32: pKa Values
Sulfadimethoxine
pKa1 = 2.13, pKa2 = 6.08
1. McClure, E. L., Wong, C.S. J Chromatogr. A 1169, 2007, 53-62
2. Qiang, Z., Adams, C. Water Research, 38, 2004, 2874-2890
pKa 1
pKa 2

## Slide 33
Filtration
Spike w/ isotopically-labeled recovery surrogates
Filter (0.7, 0.45, 0.2 µm pore size in sequence)
removes dissolved matter and some biological material
pH
Stabilize pH at
8 ± 0.1
Extraction
Extraction with nonpolar “Oasis HLB” solid phase extraction cartridge concentrates analytes and removes (some) sample matrix interferences
Elution + Evaporation
Samples are eluted with organic solvent (methanol and/or methanol/MTBE mixture) and then concentrated to ~150 µl
Final
Sample Matrix
Preparation
150 µl sample is brought up to 1500 µl with pH = 2.8 acetic acid and spiked with 10 µl
Internal standard mixture
Measurement by HPLC-MS/MS
Samples collected in 1liter LDPE cubitainers or 1250 ml glass bottles
~18 samples = ~20 person-hours of lab time

## Slide 34
HPLC-MS/MS method:
20 µl injection volume
Agilent Zorbax
C18 Eclipse, 2.1 x 150 mm,
dp = 3.5 µm
Gradient Elution
MS/MS (ESI-QqQ) detection
TIC

## Slide 35
All recoveries in absolute percentage (no surrogate correction)
Some discrepancy between theory and experimental
High (relatively) spike level can mask issues….

## Slide 36: Quantification by Surrogate Correction I
How do we know that we are analyzing everything that was in our sample?
In other words: How much do we lose in the extraction process?
To account for CEC loss during extraction, we use isotopically-labeled surrogates that are identical chemically, but differ in mass, from our CEC analytes:
Corrected MassCEC =
Calculated MassCEC / Fractional Recovery of Appropriate Surrogate
Add 10 ng d6 sucralose before processing
2. Calculate recovery of d6 sucralose (i.e., recovery = 50%)
4. Corrected results = (15 ng/0.5)/water volume = 30 ng sucralose/Liter
3. Initial Result = 15 ng sucralose in sample

## Slide 37: Quantification by Surrogate Correction II
Acetaminophen Spike + Recovery Data |  |  |  |  |  |  |  | 
 | Name | Raw % Recovery | d3 Vanillin Corrected % Recovery | d4 Propylparaben Corrected % Recovery | d4 Sulfamethoxazole Corrected % Recovery | d5 Atrazine Corrected % Recovery | d6 Sucralose Corrected % Recovery | d6 Theobromine Corrected % Recovery
DI Water Spikes, pH=8 | DI SPK 1 PH8 | 62 | 95 | 124 | 96 | 98 | 94 | 144
 | DI SPK 2 PH8 | 46 | 70 | 86 | 81 | 71 | 70 | 279
 | DI SPK 3 PH8 | 52 | 81 | 104 | 89 | 78 | 73 | 103
CUW Dock Water Spikes, pH = 8 | D. SPK 1 PH8 | 38 | 124 | 118 | 168 | 100 | 156 | 136
 | D. SPK 2 PH8 | 66 | 126 | 123 | 151 | 100 | 145 | 310
 | D. SPK 3 PH8 | 47 | 120 | 108 | 136 | 86 | 126 | 378
Hylebos Creek Water Spikes, pH= 8 | STREAM SPK 1 PH8 | 47 | 116 | 133 | 124 | 112 | 123 | 179
 | STREAM SPK 2 PH8 | 46 | 80 | 95 | 109 | 72 | 79 | 323
 | STREAM SPK 3 PH8 | 50 | 100 | 115 | 118 | 92 | 99 | 261
 | AVERAGE | 50 | 101 | 112 | 119 | 90 | 107 | 235
 | RSD(%) | 17 | 21 | 13 | 24 | 16 | 29 | 41
We have multiple labeled surrogates, but not enough for each CEC (d6 sucralose = 225$/1 mg)
So, we need to evaluate which labeled compounds work best as surrogates for each CEC
We do this by spiking a known amount of the CEC analytes into relevant sample matrices and calculating the accuracy of the recovery using each surrogate
  Accuracy threshold = >70%, <130% accuracy (± 30%)
“Best” surrogate = d5 Atrazine: 90% accuracy on average w/ least variability

## Slide 38: Conclusions/Wrap-Up
SPE is a widely applicable tool for sample pre-treatment that can make analysis of low-level analytes in complex matrices possible
The variety in SPE strategies gives you a variety of strategies to process their samples:
  Enrichment
  Clean-Up
  Fractionation
You can adjust the efficacy of all of these with some knowledge of the factors at work
  pH, pH, pH
  Mobile phase
  Stationary Phase

## Slide 39: Seminar Advertisement
September 26 2014
Sequoia 338
1 PM
Contaminants of Emerging Concern: How Much is Out There, How Do We Measure Them, and Why Do We Care?

## Slide 40: Acknowledgements-Thank You!
Slides
Dr. Dan Burgard, University of Puget Sound
Dr. Roy Dixon, Sac State
Waters Corp.
UWT/CUW Interns
Alex Gipe
Derek Overman
Donny Glaser
Jessica Maves Connor Bacon