## Slide 1: Micellar Electrokinetic chromatography
Diana Cheng and Stephanie Clark
November 25, 2014

## Slide 2: Outline
Introduction and Background
Theory
Advantages
Disadvantages
Recent Applications
Conclusions

## Slide 3: Introduction and Background (1)
Electrophoresis: separating charged molecules in an electric field
Two important phenomena
  Thermal convection: interferes with separation
    Free-zone electrophoresis suppresses convection through capillary rotation or use of a narrow-bore capillary (capillary zone electrophoresis, CZE)
  Electroosmotic flow (EOF): caused by the charge on the inner capillary surface interacting with the applied field
    Strong EOF moves all analytes toward the cathode with negatively charged capillary surface (neutral and alkaline)

## Slide 4: Introduction and Background (2)
Micellar Electrokinetic Chromatography (MEKC) was developed as a mode of Capillary Electrophoresis (CE)
  Particularly for neutral/non-charged molecules
First developed in 1982 (published 1984) by Terabe et al.
  At that time, capillary GC offered >100000 theoretical plates, HPLC only offered ~5000
  Adding surfactant to the buffer of CZE separated unionized compounds under neutral conditions
    Successful separation lead to the conclusion that the surfactant formed a micelle which acted as a psuedostationary phase

## Slide 5: Introduction and Background (3)
Surfactant – contraction of “surface active agents”
  Reduce surface tension
  Form micelles at concentrations above critical micelle concentration
    Most common surfactant in MEKC is SDS (sodium dodecyl sulfate)
Micelle – polar head, long hydrocarbon tail
Ionic Micelle
Mixed Micelle
Core interaction
(hydrophobic)
Surface interaction
(ionic)
Cosurfactant interaction
Surface interaction
(non-ionic)

## Slide 6: Theory (1)
Separation is based on the micellar solubilization
  The process of incorporating analytes onto/into the micelle
  Selectivity (α) can be easily manipulated by changing the type(s) of surfactant(s) used
    For hydrophobic analytes, organic solvents can by added to the solution for better partitioning into the aqueous phase
    Extremely hydrophobic analytes are a challenge to separate

## Slide 7: Theory (2)
Migration velocity of micelle
  EOF velocity plus micelle electrophoretic velocity
  vmc – migration velocity
    Vector quantity (positive toward cathode)
  veo – EOF velocity
  vep(mc) – electrophoretic velocity of the micelle
    veo and vep(mc) usually have different signs
Assuming veo is positive and vep(mc) is negative, a large veo results in a positive vmc value (micelles move toward cathode)

## Slide 8: Theory (3)
MEKC schematic
Cathode
Anode

## Slide 9: Theory (4)
Migration time is related to the familiar retention time
  Analyte migration falls within range of EOF marker and micelle marker
  k – retention factor
  tr – analyte migration time
  t0 – EOF marker migration time
  tmc – micelle marker migration time
“Chromatogram” is known as Electropherogram in MEKC
t0 ≤ tr ≤ tmc

## Slide 10: Theory (5)
t0 ≤ tr ≤ tmc

## Slide 11: Theory (6)
EOF marker
  Neutral analyte that does not interact with the micelles
    Same velocity as EOF
    Gives t0
    Methanol
Micelle marker
  Analyte that is fully incorporated into micelle
    Same velocity as micelle
    Gives tmc
    Sudan III (lipophilic dye)

## Slide 12: Theory (7)
Resolution – similar to conventional
  Extra term is the virtual capillary length term
    Describes the actual zone in which micelles interact with analytes (corresponds to conventional column)
    Length depends on migration time

## Slide 13: Theory (8)
Plate number is not proportional to “column” or tube length
  N = µV/2D
    µ – electrophoretic mobility
    V – applied voltage
    D – molecular diffusion coefficient (not easy to modify)
  What does this really mean?
    Faster mobility and higher voltage = more efficient
      High voltage has some restrictions due to thermal conductivity issues

## Slide 14: Theory (9)
Optimum k to maximize resolution
Retention factor is also described as:
  Bottom line:
    Increasing surfactant concentration increases k
    Adding organic solvents decreases k

## Slide 15: Detectors
Intrinsic difficulty with transitioning CE detectors to MEKC
  Partitioning of analyte in micelles alter detection properties
Types of detectors
  Laser-induced fluorescence (LIF) – common
    “Solid choice” – Silva 2013 Review
    Many analytes not inherently fluorescent, but fluorescein analogues/derivatives have been successful labeling agents
    Good sensitivity
  UV Absorbance – common
    Short path length contributes to low concentration sensitivity
  MS – not that great
    Universal and sensitive
    Expensive and not quite successfully coupled to MEKC
Electrochemical and conductimetric detectors
  Better sensitivity, but not as universal or affordable as UV

## Slide 16: Advantages
Can separate molecules too small for gel electrophoresis
Can separate both ionic and neutral compounds with high efficiency and short retention time unlike in CE
High separation efficiency
Minimal consumption of sample compared to HPLC since concentration is detected on ng/L scale
Ability to separate chiral compounds efficiently
Equipment cheaper than HPLC
High sensitivity in absolute amounts
Quicker than HPLC for separating complex samples

## Slide 17: Disadvantages (1)
Limitation in detectors
  MEKC-DESI-MS
    Sensitivity not practical for real samples
  MEKC/MS
    Nonvolatile surfactants and chiral selectors contaminate ion source
In some studies, MEKC suffers from poor reproducibility of electroosomotic flow between samples

## Slide 18: Disadvantages (2)
Can’t detect at low concentrations
  First experiment conducted:
    Maximum capillary volume of 1.8 µL
    Injection volume estimated to be 12 nL
  Short pathlength of light and small injection volumes give low concentration sensitivity
    Sensitivity can be improved through preconcentration techniques like stacking or sweeping

## Slide 19: Applications (1)
Medical Analysis
    Determination and Quantification of Paclitaxel, morphine, and codeine in urine sample of patients with different cancer types (breast, head and neck, and gastric)
  Advantages:
    Separation of both neutral and ionic compounds at once
    Quick sample preparation -- centrifugation and filtration
    Robust – lack of external influences on results ( days, buffers, patients)
    Rugged – lack of internal influences on results (buffer, SDS voltage, etc.)
    Direct injection method with biological samples

## Slide 20: Applications (2)
Food Analysis
    Determination of procyanidins and other phenolic compounds in lentil samples (2001)
    Determination of Amoxicillin, Ampicillin, Sulfamethoxazole, and Sulfacetamide in Animal Feed (2009)
  Advantages
    Ability to separate chiral compounds
    Low solvent consumption (environmentally friendly)
    Efficient separation
    Relatively quicker compared to HPLC and GC
    Cheaper
      Chiral columns must be used for GC – more expensive

## Slide 21: Applications (3)
Environmental Analysis
    Determination of anti-inflammatory drugs in river water
  Advantages:
    Detection in ng/L scale
    Separation of several analytes in short time
    Sensitive
Pharmaceutical Analysis
  Ability to separate complex mixtures (natural products, crude drugs) with high resolution
  Results from study show separation of 26 analytes in 30 minutes with well resolved baseline.
  Another study showed separation of 17 amino acid derivatives within 15 minutes
Separation of vitamins and antibiotics
  Higher selectivity seen with MEKC method than CZE
  Shorter analysis time with MEKC than CZE

## Slide 22: Conclusions
Effective separation of neutral molecules
Inexpensive equipment
Selectivity easily manipulated through various combinations of surfactants and organic solvents
  Finding the right combination can be difficult
Could be more widely used if better detector interfaces are developed

## Slide 23: References (1)
(1) Terabe, S. Annu. Rev. Anal. Chem. 2009, 2, 99.
(2) Rodriguez, J.; Castaneda, G.; Contento, A. M.; Munoz, L. J. Chromatogr. A 2012, 1231, 66.
(3) Otsuka, K.; Terabe, S. J. Chromatogr. A 2000, 875, 163.
(4) Quirino, J. P.; Terabe, S. Science (Washington, D. C.) 1998, 282, 465.
(5) Poole, C. F.; Poole, S. K. J. Chromatogr. A 1997, 792, 89.
(6) Terabe, S. Anal. Chem. 2004, 76, 240A.
(7) Nishi, H.; Terabe, S. J. Chromatogr. A 1996, 735, 3.
(8) Silva, M. Electrophoresis 2011, 32, 149.
(9) Silva, M. Electrophoresis 2013, 34, 141.
(10) Molina, M.; Silva, M. Electrophoresis 2002, 23, 3907.
(11) Silva, M. Electrophoresis 2009, 30, 50.
(12) Muijselaar, P. G.; Otsuka, K.; Terabe, S. J. Chromatogr. A 1997, 780, 41.
(13) Kim, J.-B.; Terabe, S. J. Pharm. Biomed. Anal. 2003, 30, 1625.

## Slide 24: References (2)
(14) Nishi, H. J. Chromatogr. A 1997, 780, 243.
(15) Pappas, T. J.; Gayton-Ely, M.; Holland, L. A. Electrophoresis 2005, 26, 719.
(16) Wang, P.; Ding, X.; Li, Y.; Yang, Y. J. AOAC Int. 2012, 95, 1069.
(17) Rosen, M. J.; 4th ed.. ed.; Kunjappu, J. T., ebrary, I., Eds.; Hoboken, N.J. : Wiley: Hoboken, N.J., 2012, p 1.
(18) Terabe, S. Procedia Chem. 2010, 2, 2.
(19) Jorgenson, J. W.; Lukacs, K. D. Anal. Chem. 1981, 53, 1298.
(20) Terabe, S.; Otsuka, K.; Ichikawa, K.; Tsuchiya, A.; Ando, T. Anal. Chem. 1984, 56, 111.
(21) Cifuentes, A.; Bartolomé, B.; Gómez‐cordovés, C. ELECTROPHORESIS 2001, 22, 1561.
(22) Maijó, I.; Borrull, F.; Aguilar, C.; Calull, M. Journal of Liquid Chromatography & Related Technologies 2012, 35, 2134.
(23) Injac, R.; Kocevar, N.; Strukelj, B. Croat. Chem. Acta 2009, 82, 685.

## Slide 25: Acknowledgements
Dr. Dixon
Chemistry 230 class and fellow graduate students

## Slide 26: Questions