## Slide 1: Chem. 31 – 9/25 Lecture

## Slide 2: Announcements
Exam 1 – on Oct. 4th
  Next Week on Wednesday
  Will Cover Ch. 1, 3, 4, and parts of 6
Water Hardness Lab – Now due 10/2
Lab Manual Problem
Today’s Lecture
  Gaussian Statistics (Chapter 4)
    Statistical Tests (F-test, t-tests, Grubb’s Test)
    Value of data averaging
    Least Squares Regression (if time)

## Slide 3: F - Test
Used to compare precision of two different methods (to see if there is a significant difference in their standard deviations)
or to determine if two sample sets show different variability (e.g. standard deviations for mass of fish in Lake 1 – from a hatchery vs Lake 2 – native fish)
Example: butyric acid is analyzed using HPLC and IC. Is one method more precise?
Method | Mean (ppm) | S (ppm) | n
HPLC | 221 | 21 | 4
IC | 188 | 15 | 4
Notes: 3

## Slide 4: F - Test
Example – cont.
  IC method is more precise (lower standard deviation), but is it significant?
  We need to calculate an F value
Then, we must look up FTable (= 9.28 for 3 degrees of freedom for each method with 4 trials)
This requires S1 > S2, so 1 = HPLC, 2 = IC
Since FCalc < FTable, we can conclude there is no significant difference in S (or at least not at the 95% level)
Notes: 4

## Slide 5: Statistical Tests t Tests
Case 1
  used to determine if there is a significant bias by measuring a test standard and determining if there is a significant difference between the known and measured concentration
Case 2
  used to determine if there is a significant differences between two methods (or samples) by measuring one sample multiple time by each method (or each sample multiple times) – same measurements as used for F-test
Case 3
  used to determine if there is a significant difference between two methods (or sample sets) by measuring multiple sample once by each method (or each sample in each set once)
Notes: 5

## Slide 6: Case 1 t test Example
A new method for determining sulfur content in kerosene was tested on a sample known to contain 0.123% S.
The measured %S were:
0.112%, 0.118%, 0.115%, and 0.117%
Do the data show a significant bias at a 95% confidence level?
Clearly lower, but is it significant?
Notes: 6

## Slide 7: Case 2 t test Example
Back to butyric acid example
  Now, Case 2 t-test is used to see if the difference between the means is significant (F test tested standard deviations)
Method | Mean (ppm) | S (ppm) | n
HPLC | 221 | 21 | 4
IC | 188 | 15 | 4
Notes: 7

## Slide 8: Case 3 t Test Example
Case 3 t Test used when multiple samples are analyzed by two different methods (only once each method)
Useful for establishing if there is a constant systematic error
Example: Cl- in Ohio rainwater measured by Dixon and PNL (14 samples)
Notes: 8

## Slide 9: Case 3 t Test Example – Data Set and Calculations
Conc. of Cl- in Rainwater |  | 
(Units = uM) |  | 
Sample # | Dixon Cl- | PNL Cl-
1 | 9.9 | 17.0
2 | 2.3 | 11.0
3 | 23.8 | 28.0
4 | 8.0 | 13.0
5 | 1.7 | 7.9
6 | 2.3 | 11.0
7 | 1.9 | 9.9
8 | 4.2 | 11.0
9 | 3.2 | 13.0
10 | 3.9 | 10.0
11 | 2.7 | 9.7
12 | 3.8 | 8.2
13 | 2.4 | 10.0
14 | 2.2 | 11.0
7.1
8.7
4.2
5.0
6.2
8.7
8.0
6.8
9.8
6.1
7.0
4.4
7.6
8.8
Calculations
Step 1 – Calculate Difference
Step 2 - Calculate mean and standard deviation in differences
ave d = (7.1 + 8.7 + ...)/14
ave d = 7.49
Sd = 2.44
Step 3 – Calculate t value:
tCalc = 11.5
Notes: 9

## Slide 10: Case 3 t Test Example – Rest of Calculations
Step 4 – look up tTable
  (t(95%, 13 degrees of freedom) = 2.17)
Step 5 – Compare tCalc with tTable, draw conclusion
  tCalc >> tTable so difference is significant
Notes: 10

## Slide 11: t- Tests
Note: These (case 2 and 3) can be applied to two different senarios:
  samples (e.g. comparing blood glucose levels of two twins)
  methods (analysis method A vs. analysis method B)
Notes: 11

## Slide 12: Grubbs Test Example
Purpose: To determine if an “outlier” data point can be removed from a data set
Data points can be removed if observations suggest systematic errors
Example:
Cl lab – 4 trials with values of 30.98%, 30.87%, 31.05%, and 31.00%.
Student would like less variability (to get full points for precision)
Data point farthest from others is most suspicious (so 30.87%)
Demonstrate calculations

## Slide 13: Dealing with Poor Quality Data
If Grubbs test fails, what can be done to improve precision?
  design study to reduce standard deviations (e.g. use more precise tools)
  make more measurements (this may make an outlier more extreme and should decrease confidence interval)
  can also discard data based on observation showing error (e.g. loss of AgCl in transfer resulted in low % Cl for that trial)
Notes: 13

## Slide 14: Signal Averaging
For some type of measurements, particularly where they are made quickly, averaging many measurements can improve the sensitivity or the precision of the measurement
Example 1: NMR
1 scan
25 scans

## Slide 15: Signal Averaging
Example 2: High Accuracy Mass Spectrometry
To confirm molecular formula, error in mass should be < 5 ppm (for mass = 809 amu, error must be < 0.004 amu)
However, Smass = 0.054 amu
Can requirement be met?
Yes Smean mass = Smass/√n
What value is needed for n to meet 5 ppm requirement 95% of time?
Note: also requires accurate calibration
Example compound: expected mass = 809.4587 amu
To meet 5 ppm limit, meas. mass = 809.4547 to 809.4628
Measured Mass = 809.4569 amu

## Slide 16: Calibration
For many classical methods direct measurements are used (mass or volume delivered)
Balances and Burets need calibration, but then reading is correct (or corrected)
For many instruments, signal is only empirically related to concentration
Example Atomic Absorption Spectroscopy
  Measure is light absorbed by “free” metal atoms in flame
  Conc. of atoms depends on flame conditions, nebulization rate, many parameters
  It is not possible to measure light absorbance and directly determine conc. of metal in solution
  Instead, standards (known conc.) are used and response is measured
Light beam
To light Detector
Notes: 16

## Slide 17: Method of Least Squares
Purpose of least squares method:
  determine the best fit curve through the data
  for linear model, y = mx + b, least squares determines best m and b values to fit the x, y data set
  note: y = measurement or response, x = concentration, mass or moles
How method works:
  the principle is to select m and b values that minimize the sum of the square of the deviations from the line (minimize Σ[yi – (mxi + b)]2)
  in lab we will use Excel to perform linear least squares method
Notes: 17