## Slide 1: Chem. 31 – 10/25 Lecture

## Slide 2: Announcements
Statistical Calculations Lab
  Resubmissions due today
AA Lab – Scheduled due date is 10/30
Today’s Lecture
  Chapter 7 – Titrations
    Precipitations (covered qualitatively this semester)
  Chapter 18 - Spectroscopy

## Slide 3: Precipitation Titrations - covering qualitatively
Example: Titration of Hg22+ by CrO42-
  Hg22+ + CrO42- → Hg2CrO4 (s)
  Ksp(Hg2CrO4) = 2.0 x 10-9
  K = 1/Ksp = 5 x 108 = large (reaction near full to product)
  Titration has 3 regimes:
    Before equivalence point (excess Hg22+ in flask) – [Hg22+] is high
    At equivalence point (nHg2^2+/nCrO4^2- = 1/1) [Hg22+] is rapidly decreasing
    After equivalence point (excess CrO42- in flask) [Hg22+] is low
CrO42-
Hg22+
This is different than text example

## Slide 4: Titrations Shapes of Titration Curves – Precipitation Example
Plot of moles in flask vs. V(titrant)
Easier to understand
moles analyte
moles titrant
V(titrant)
V(eq. pt.)
However, moles are not readily measured. Concentration or log[Hg22+] more readily measured. Log[Hg22+] or pHg22+ ( = -log[Hg22+]) is plotted on y-axis
At equivalence point both Hg22+ and CrO42- are present in low amounts
[Hg22+] = Ksp1/2

## Slide 5: Titrations Shapes of Titration Curves – Precipitation Example
What affects sharpness at equivalence point?
  Ksp value (smaller means sharper)
  Concentration of ions (higher means sharper)
Ksp(CO32-) < Ksp(CrO42-) <Ksp(SO42-)

## Slide 6: Titrations Titration of a mixture
Example: Titration of a mixture of CrO42- and CO32- by Hg22+
  Since Ksp value for CO32- is smaller, it will precipitate first
  After CO32- precipitates to near completion, pHg drops to the point where CrO42- starts to precipitate
Which anion was initially present at higher concentration?

## Slide 7: Chapter 18 - Spectroscopy
A. Introduction
1. One of the main branches of analytical chemistry
2. The interaction of light and matter (for purposes of quantitative and qualitative analysis)
3. Topics covered:
- Properties of Light
- Absorption of Light
- Electromagnetic Spectrum
- Beer’s Law
- Spectrometers

## Slide 8: Spectroscopy
Fundamental Properties of Light
  Wave-like properties:
λ
λ = wavelength = distance between wave crests
n = frequency = # wave crests/s
= wave number = # wave crests/length measure
c = speed of light (in vacuum) = 3.00 x 108 m/s
Relationships: c = λ·n and = 1/λ
note: speed of light depends on medium (slower in water than in vacuum) – not considered here

## Slide 9: Spectroscopy Fundamental Properties of Light
1. Other wave-like properties
- diffraction, interference
2. Particle-like properties
a) Idea of photons (individual entities of light)
b) Energy of photons
E = hn = hc/l

## Slide 10: Spectroscopy Absorption vs. Emission
Absorption
  - Associated with a transition of matter from lower energy to higher energy
Emission
  - Associated with a transition from high energy to low energy
Ground State
Energy
Excited State
Photon in
Photon out
A + hn → A*
A* → A + hn
hn = photon

## Slide 11: Spectroscopy Regions of the Electromagnetic Spectrum
Many regions are defined as much by the types of transitions occurring (e.g. outer shell electron) as by the frequency or energy of the transitions
Long wavelengths
Short wavelengths
High Energies
Low Energies
Gamma rays
X-rays
Nuclear transitions
Inner shell electrons
UV + visible
Outer shell electrons
Infrared
Bond vibration
Molecular rotations
Microwaves
Radio waves
Electron spin
Nuclear spin

## Slide 12: Spectroscopy Some Example Questions
A nuclear magnetic resonance (NMR) spectrometer absorbs light at a frequency of 750 MHz. This is in the radio frequency and Hz = s-1. What is the wavelength of this light?
An infrared absorption band occurs at a wavenumber of 812 cm-1. What is the wavelength (in mm) and energy (J/photon) of that light?
What type of light involves transitions of inner shell electrons?

## Slide 13: Spectroscopy Beer’s Law
Light intensity in = Po
Light intensity out = P
Transmittance = T = P/Po
Absorbance = A = -logT
Light source
Absorbance used because it is proportional to concentration
A = εbC
Where ε = molar absorptivity and b = path length (usually in cm) and C = concentration (M)
b
ε = constant for given compound at specific λ value
sample in cuvette

## Slide 14: Spectroscopy Beer’s Law Question
Half of the 284 nm light is absorbed when benzoic acid at a concentration of 0.0080 M is in a cuvette with a path length of 0.50 cm. What is the molar absorptivity of benzoic acid at this wavelength?

## Slide 15: Spectroscopy More on Beer’s Law
Useful for determination of analyte concentrations
Some limitations
  Law not valid for high concentrations
  Deviations to law appear to occur when multiple wavelengths of light used or when multiple species exist but absorb light differently
  Uncertainties are lowest when 0.1 < A < 1
Example of deviations to Beer’s Law:
Unbuffered Indicator with ε(In-) = 300 M-1 cm-1, ε(HIn) = 20 M-1 cm-1; pKa = 4.0
HIn ↔ H+ + In-

## Slide 16: Spectroscopy Spectrometers
light source
sample in cuvette
light discriminator: monochromator (passes only a small range of wavelengths)
light detector – measures light intensity by converting it to an electrical signal
Data processor
Components can look very different in different types of spectrometers, but spectrometers will have all of the major components (except other methods of wavelength discrimination may replace monochromators)

## Slide 17: Spectroscopy Example Measurement: Ozone
Ozone (O3) is a pollutant (lower atmosphere) and in stratosphere provides UV protection
Instrument is used for measurement at station or in airplane
  compares absorbance through sample cell vs.
  absorbance through reference cell
Can also make measurements remotely (e.g. absorbance between two skyscrapers)
light source (l = 254 nm)
light detector
air in
O3 scrubber
sample cell
reference cell
chopper