## Slide 1: Chem. 31 – 11/1 Lecture

## Slide 2: Announcements I
Quiz 4
  Today
Syllabus error (Chromatography chapter = 23 – not 22)
Formal Lab Report Information
  Posted online (class website)
  Parts A (Introduction and Methods) and B (Results added)

## Slide 3: Announcements II
Exam 2
  Next Wednesday (Nov. 8th)
  Will Cover Ch. 6 (all except 6-1), Ch. 7 (except not calc. of conc. in precip. titrations), Ch. 18, and Ch. 23 (extractions and through retention part of chromatography)
  Review on Monday
Today’s Lecture
  Chapter 23 – Chromatography
    Chromatographs and Columns
    Transport and Retention

## Slide 4: Chromatography Partitioning in Chromatography (review – covered last time)
Separation Occurs in Column
Partitioning Requires Two Phases:
  Mobile phase
  Stationary phase (solid or liquid within column)

## Slide 5: Chromatography Equipment
Chromatograph = instrument
Chromatogram = detection vs. time (vol.) plot
Chromatograph Components
Mobile Phase Reservoir
Flow/Pressure Control
Sample In
Injector
Chromatographic Column
Detector
Waste or fraction collection
Signal to data recorder
Chromatogram

## Slide 6: Chromatography More on Stationary Phases
Open Tubular – in GC
(end on, cross section view)
Column Wall
Mobile phase
Stationary phase (wall coating)
Packed column (side view) (e.g. Silica in normal phase HPLC)
Packing Material (solid)
Stationary phase is surface (larger area than shown because its porous)
Bonded phase (liquid-like)
Expanded View
Stationary Phase
Chemically bonded to packing material
Packing Material

## Slide 7: Chromatography Overview – The Good, the Bad, and the Ugly
The Good: Differential partitioning of solute between a mobile and a stationary phases
The Bad: Band broadening
The Ugly: Non-ideal peak shapes (we will see this in the GC lab)
More realistic picture
Concentration profile
Yellow compound sticks to stationary phase more

## Slide 8: Chromatography Flow – Volume Relation
Relationship between volume (used with gravity columns) and time (most common with more advanced instruments):
  V = t·uV
  V = volume passing through column part in time t at flow rate uV
  Also, VR = tR·uV where R refers to retention time/volume (time it takes component to go through column or volume of solvent needed to elute compound)
Can also use linear velocity (ux)
  ux = L/tR where L = column length

## Slide 9: Chromatography More on Volume
Hold-up volume = VM = volume occupied by mobile phase in column
Stationary phase volume = VS
Calculation of VM:
  VM = tM·uV, where tM = time needed for unretained compounds to elute from column
  Unretained compound = compound 100% in mobile phase

## Slide 10: Chromatography Reading Chromatograms
Determination of parameters from reading chromatogram (HPLC example)
tM = 2.374 min. (normally determined by finding 1st peak for unretained compounds – contaminant below)
VM = uV·tM = (1.0 mL/min)(2.37 min) = 2.37 mL

## Slide 11: Chromatography Some Questions
What are the required two phases in chromatography called?
List two ways in which a stationary phase is “attached” to a column?
List 3 main components of chromatographs.
A GC has the flow rate set to 2.0 mL/min. When methane is injected (it is not retained at all on the stationary phase), it takes 2.85 min to appear. What is the mobile phase volume?
What phase is the mobile phase in HPLC?

## Slide 12: Chromatography Partition and Retention
Partition Coefficient = K = [X]S/[X]M
Higher K means slower elution
K is constant if T and/or solvent remain constant
K is not used that frequently in chromatography
Retention Factor = k = main measure of partioning/retention in column
k = (moles X)S/(moles X)M = K(VS/VM)
Retention Factor is more commonly used because of ease in measuring, and since VM/VS = constant, k = constant·K (for a given column)
Note: kColumn1 ≠ k Column2 (if VM/VS changes)

## Slide 13: Chromatography Definition Section – Partition and Retention
Since the fraction of time a solute molecule spends in a given phase is proportional to the fraction of moles in that phase,
k = (time in stationary phase)/(time in mobile phase)
Experimentally, k = (tR – tM)/tM
Note: t’R = tR – tM = adjusted retention time

## Slide 14: Chromatography Reading Chromatograms
1st peak, tR = 4.958 min.; k = (4.958 - 2.374)/2.374 = 1.088

## Slide 15: Chromatography What do all these Parameters Mean?
Large k value (or K value) means analyte prefers stationary phase
“Adjusting k (or K)” - in GC:
  k value will depend on volatility and polarity (analyte vs stationary phase)
  More volatile compound elutes first (if polarity is the same)
  k value adjusted by changing T (most common)
  higher T means less retention (lower k and K)

## Slide 16: Chromatography What do all these Parameters Mean? II
Adjusting k – in HPLC
  k value will depend on analyte vs. mobile phase and stationary phase polarity
  Oldest type (= Normal phase) stationary phase is polar and mobile phase is non-polar
  Most common type (= Reversed phase) has non-polar stationary phase and polar mobile phase
  k value adjusted by changing mobile phase polarity
  k value is decreased by making mobile phase more like stationary phase (= using “stronger” eluent)
  In reversed phase HPLC, less polar mobile phase means less retention
more polar
less polar
stationary phase
water
methanol
analyte

## Slide 17: Chromatography What do all these Parameters Mean? III
Retention Factor is a more useful measure of partitioning because value is related to elution time
Compounds with larger K, will have larger k, and will elute later
Practical k values
  ~0.5 to ~10
  Small k values → overlapping peaks likely
  Large k values → must wait long time

## Slide 18: Chromatography More Questions
A chemist is analyzing samples by normal phase HPLC using a mobile phase containing 90% hexane and 10% 2-propanol (2-propanol is the more polar solvent). The analysis is taking too long. How can she decrease k values?
From the chromatogram to the right, calculate kX.
unretained peak
X Y