## Slide 1: Chem. 31 – 11/13 Lecture

## Slide 2: Announcements I
Co/Cr Lab Report – Due today
Exam 2
  Average was 78% (still good)
  Performance on multiple choice poorer
  Key, your scores, and overall lecture % posted
Chart: Exam 2 Distribution
| 100s | 90s | 80s | 70s | 60s | <60
100s 90s 80s 70s 60s <60 | 1 | 17 | 31 | 17 | 13 | 10

## Slide 3: Announcements II
New Homework Assignment (to be posted soon)
Today’s Lecture
  Chapter 23 – Chromatography
    Relative Retention
    Band Broadening
    Resolution
  Chapter 8 – Advanced Equilibrium
    Overview
    Ionic Strength

## Slide 4: Chromatography Definition Section – Relative Retention
For a separation to occur, two compounds, A and B must have different k values
The greater the difference in k values, the easier the separation
Relative Retention = a = kB/kA (where B elutes after A) = measure of separation ease = “selectivity coefficient”
a value close to 1 means difficult separation

## Slide 5: Chromatography Reading Chromatograms
Determination of parameters from reading chromatogram (HPLC example)
a (for 1st 2 peaks) = kB/ kA = tRB’/ tRA’ = (5.757 – 2.374)/(4.958 – 2.374) = 1.31

## Slide 6: Chromatography What do all these Parameters Mean? Relative Retention
a values
  Can “adjust” value by choosing column (HPLC or GC) that is more “selective” for one compound than another or change the solvent (HPLC) to one which “dissolves” one compound better than another
  example: on a non-polar column, diethyl ether (Kow = 6.8, bp = 34.6°C) and methanol (Kow = 0.15, bp = 64.7°C) are observed to partially co-elute giving a small a value.
  switching to a polar column will increase retention of methanol (stronger interaction with new column) and decrease retention of diethyl ether (weaker interaction with new column), increasing a.
  with HPLC, it is often possible to change the eluent to increase a. Recent example: reversed phase separation with acetonitrile and water lead to poor C16:0/C18:1 separation (for biodiesel characterization). Switching organic to methanol lead to improvement. [show on next slide]

## Slide 7: Chromatography What do all these Parameters Mean? Relative Retention
a values – research example from last time
  Fatty acid separation example: - separating C16:0 (HO2C(CH2)14CH3) from C18:1 (HO2C(CH2)6CH=CH(CH2)6CH3) fatty acids with organic plus aqueous formic acid
  When using formic acid and acetonitrile, small a value
  Replacement of methanol for acetonitrile improves a value
Example chromatogram – looks similar to this when used acetonitrile + formic acid
C16 + C18:1
Note: actually went to 14% FA(aq) /21.5% acetonitrile/64.5% methanol to decrease tailing with methanol
C18:1
C16

## Slide 8: Chromatography Band Broadening
Band Shape given by Gaussian Distribution
Gaussian Distribution
Normal Distribution Area = 1
Widths
  σ (std deviation)
  w = 4σ
  w1/2 = 2.35σ
Gaussian Shape (Supposedly)
2σ
Inflection lines
w
Height
Half Height
w1/2
Will use most
Notes: 8

## Slide 9: Chromatography Column Efficiency
Number of Theoretical Plates = N = Primary measure of “efficiency”
N=1 corresponds to 1 liquid-liquid extraction
Good efficiency means:
  Large N value
  Late eluting peaks still have narrow peak widths
  Minimal band broadening
N = 16(tR/w)2M (other multipliers with other widths)
large N Value
low N value
Notes: 9

## Slide 10: Chromatography Column Efficiency
Relative measure of efficiency = H = Plate height = L/N where L = column length
H = length of column needed to get a plate number of 1
Smaller H means greater efficiency
Note: H is independent of L (although usually calculated using L), N depends on L
Improvement of Efficiency
  Increase column length (N = L/H) so doubled column length will have twice the N value (no change in H)
  Decrease H (use smaller diameter open tubular columns or smaller packing material) → greater N in same column length
or
Notes: 10

## Slide 11: Chromatography Measurement of Efficiency
Later eluting peaks normally used to avoid effects from extra-column broadening
Example: N = 16(14.6/0.9)2 = 4200 (vs. ~3000 for pk 3)
H = L/N = 250 mm/4200 = 0.06 mm
W ~ 0.9 min
Notes: 11

## Slide 12: Chromatography Resolution
Resolution = measure of how well separated two peaks are
Resolution = Δtr/wav (where wav = average peak width) (use this equation for calculating resolution)
RS < 1, means significant overlap
RS = 1.5, means about minimum for “baseline resolution” (at least for two peaks of equal height)
Notes: 12

## Slide 13: Chromatography Resolution Example
RS calculation example:
  1st two retained peaks:
    tR(1st pk) = 8.20 min., w = 0.505 min.
    tR(2nd pk) = 9.09 min., w = 0.536 min
    Resolution = 0.89/0.521 = 1.70
    Resolution not baseline due to peak tailing
mannosan – 8.20 min.
galactosan – 9.09 min.
(Data from past student)
main difference: axial – equitorial switch of 2 vs. 4 C OH groups is axial
Notes: 13

## Slide 14: Chromatography Optimization – Resolution Equation
How to improve resolution
  Increase N (increase column length, use more efficient column)
  Increase a (use more selective column or mobile phase)
  Increase k values (increase retention)
Which way works best?
  Increase in k requires no new column (try first) but it will require more time and will not work if kB is large to begin with
  Increase N requires a new column (same type)
  Increasing a is the best but often requires a new column (different type).
What if resolution is very good (e.g. = 5)?
  Can decrease k to have faster chromatogram
Returned to text (not in 8th Ed.) 
B for 2nd component
Notes: 14

## Slide 15: Chromatography Graphical Representation
Initial Separation
Smaller H (narrower peaks)
Larger k or longer column – Dt increases more than width
Increased alpha (more retention of 2nd peak)
Notes: 15

## Slide 16: Chromatography Recent Example
95% organic/5% aqueous formic acid
88% organic/4% aqueous formic acid
Improvement due to greater retention
Notes: 16

## Slide 17: Chromatography Last Questions
A GC is operated close to the maximum column temperature and for a desired analyte, k = 20. Is this good?
Two columns are tried for a GC separation of compounds X and Y. Both give initial resolution values of 1.2. Column A has a kY value of 0.8 while column B has a kY value of 5.0 (for 2nd eluting compound). Which column looks more promising?
Notes: 17