# Response of Linear Systems to Random Signals

# Properties of Random Signals

- Introduction: Since random signals are defined in terms of probability, one way to characterize a random signal is to analyze the long-term observation of the process. The following analysis assumes the (weakly) stationary/ergodic property.

- The four basic properties of random signals:

  - Autocorrelation function – A measure of the degree of randomness of a signal.

  - Cross-correlation function – A measure of correlation between two signals.

  - Autospectral density function – A measure of the frequency distribution of a signal.

  - Cross-spectral density function – A measure of the frequency distribution of one signal (output) due to another signal (input).

- Correlation functions:

  - Autocorrelation function: The autocorrelation function Rxx(t) of a random signal X(t) is a measure of how well the future values of X(t) can be predicted based on past measurements. It contains no phase information of the signal.

  - Cross-correlation function: The cross-correlation function Rxy(t) is a measure of how well the future values of one signal can be predicted based on past measurements of another signal.

  - Properties of correlations functions:

    - Rxx(-t) = Rxx(t)     (even function)

    - Rxy(-t) = Ryx(t)

    - Rxx(0) = (x2  + ( x2  = mean square value of x(t)

    - Rxx(() = ( x2

    - The cross-correlation inequality:

  - Example:

    - Rxx(t) of a sine wave process:

Since the envelop of the autocorrelation function is constant as (((, we can conclude that any future values of a sine wave process can be accurately predicted based on past measurements.

    - A time-delay system:

- Spectral density functions:

  - Autospectral density function (autospectrum): The autospectral density function Sxx(f) of a random signal X(t) is a measure of its frequency distribution. It is the Fourier transform of the autocorrelation function.

  - Cross-spectral density function (cross-spectrum): The cross-spectral density function Sxy(f) is a measure of the portion of the frequency distribution of one signal that is a result of another signal. It is the Fourier transform of the cross-correlation function.

  - Symmetry: Sxx(-f) = Sxx(f) (even function)   Sxy(-f) = Sxy*(f) = Syx(f)

  - Example:

    - White noise: The autocorrelation function of a white noise process is an impulse function. The implication here is that white noise is totally unpredictable since its autocorrelation function decays to zero at t > 0. Of course, this is what we expect to see in a white noise process, a random process with infinite energy.

    - Low-pass white noise: Assuming the low-pass white noise has a magnitude of 1 and the bandwidth will vary. The autocorrelation function is computed using IFFT.

    - The autocorrelation function of a low-pass white noise process is a sinc [sin(x)/x] function. The implication here is that the predictability of a low-pass white noise process is inversely proportional to the bandwidth of the noise. Since the noise energy is proportional to the bandwidth, this conclusion is consistent with common sense.

    - Band-pass white noise: Assuming the band-pass white noise has a magnitude of 1 and the bandwidth will vary. The autocorrelation function is computed using IFFT.

    - The autocorrelation function of a band-pass white noise process has the similar property – the predictability is inversely proportional to the bandwidth of the noise. In addition, the autocorrelation function approaches the sine wave process as the bandwidth decreases, a conclusion that can easily be drawn using LTI system theory for deterministic systems.

# LTI Systems

- Introduction: LTI systems are analyzed using the correlation/spectral technique. The inputs are assumed to be stationary/ergodic random with mean = 0.

- Ideal system:

- Ideal model:

  - Correlation and spectral relationships:

Total output noise energy:

  - Example: LPF to white noise

One-sided spectrum: G(f) = 2 S(f) for f ( 0

  - Example: LPF to a sine process

- Models uncorrelated input and output noise: Gmn(f) = Gum(f) = Gvn(f) = 0

# Text boxes

u(t)

x(t)     					     y(t)

n(t)

(

z-1

v(t)

n(t)

H(f) h(t)

y(t)

x(t)

(

m(t)

(

y(t)

x(t)

H(f) h(t)