## Slide 1: Wireless Networks
Cellular and land line telephone systems are responsible for providing coverage throughout a coverage region or market
The interconnection of many such systems defines a wireless network over the world

## Slide 2: Types of Networks
Fixed Networks(PSTN) | Wireless Network
Highly static High bandwidth possible (fiber Optic or coaxial) | Highly dynamic Low RF bandwidth provided for each user

## Slide 3: Interconnection of networks
BS1
BS2
Mobile Switching Center (MSC)
Radio Link
Voice and Data Links
PSTN

## Slide 4: Functions of PSTN
Highly integrated communications network that connects the world’s population
Each country is responsible for the regulation of PSTN within it’s borders.
PSTN has a network of fixed telephone exchanges
Over time, transition has occurred from manual to automatic exchanges

## Slide 5: History of PSTN network
Controlled by long distance companies like AT&T, Sprint, Verizon
1984 – Supreme Court issued Modified Final Judgement (MFJ)
Break up of AT&T into 7 major Bell operating companies (BOCs) each with its own service region.

## Slide 6: PSTN Exchange system
City
City
City
Local Exchange Carrier (LEC)
Local Exchange Carrier (LEC)
Inter Exchange Carriers
(IXC)
Local Access and Transport Area (LATA)

## Slide 7: Local PSTN telephone network
PBX
Home
Central
Office (CO)
Tandem
Switch
IXCC
IXCB
IXCA
Other CO.s

## Slide 8: Wireless Networks
Wireless Networks are extremely complex, unlike static fixed telephone networks.
Wireless networks requires air interface between base stations and randomly spaced subscribers
Complex propagation media
MSC provides connection to PSTN and other MSCs

## Slide 9: Functions of MSC
Provides overall System control for each region
Maintains mobile related information and handoff control
Performs all call processing; billing; fraud detection within the market

## Slide 10: Wireless network comparison
First, second and third generations
Modulation techniques (Analog, Digital, Spread Spectrum)
Switching (channel) techniques (Circuit switching, packet switching)
Signaling (control) techniques (in-band, CCS)
Practical systems (USDC, GSM, CDMA)
Network capabilities

## Slide 11: First Generation Networks
Analog Technology -FM modulation
AMPS (Advanced Mobile Phone Services) – in U.S.
Mobile Terminals
Base Stations
MSCs
PSTN is separate network from the signaling network (non CCS)

## Slide 12: IS-41 Network Protocol
Network protocol standard to allow automatic registration of roamers – inter-operator roaming
Allow MSCs of different service providers to pass information about subscribers to other MSCs on demand
HLR – Home Location Register – real time user list
VLR – Visitor Location Register
AUC – Authentication Center

## Slide 13: Roaming process
Mobile periodically keys up and transmits its identity information which allows MSC to constantly update it’s customer list.
The registration command is sent in over control channels at 5-10 minute intervals - MIN – Mobile Identification Number (Telephone No.)
ESN – Electronic Serial Number

## Slide 14: Registration
By comparing MIN of roaming subscriber with HLR database, the MSC identifies roamers
MSC sends registration request over landline signaling network to subscriber’s home MSC
Home MSC validates roamer’s MIN and ESN and returns a customer profile to visited MSC
Home and visitor MSC update their HLR and VLR
The roamer is then registered in the visited MSC.

## Slide 15: Switching in Networks
First generation Circuit Switching
MSC dedicates a voice channel connection between base station and PSTN for duration of cell phone call
As calls are initiated and completed, different radio circuits and dedicated PSTN voice circuits are switched in and out to handle traffic

## Slide 16: Second Generation Wireless Networks
Employ digital modulation and have advanced call processing capabilities.
Examples:
  Global system for Mobile (GSM)
  DECT (Digital European Cordless Telephone)
  Cordless Telephone (CT2) -British system
  JDC – Japanese Digital Cellular system

## Slide 17: Packet Switching network
Second generation switching network
Packet Switching implements connectionless services for large number of data users, who remain virtually connected
Packet switching breaks each message into smaller units for transmission and recovery
When a message is broken into packets, control information is added to each packet to provide source/ destination information and identification.

## Slide 18: Packet Structure
Header – contains source address, destination address, packet sequence number, and other routing and billing information
Trailer - contains cyclic redundancy checksum which is used for error detection at receiver
Header User Data Trailer

## Slide 19: Advances in Second Generation Networks
While 1st generation systems were primarily designed for voice, second generation networks provide paging, facsimile and high –data rate network access
Handoff is mobile-controlled-MAHO(Mobile assisted Handoff)
The mobile units in this generation perform functions like received power reporting, adjacent base station scanning, data encoding

## Slide 20: Common Channel Signaling (CCS)
Second generation signaling network
Digital Technique that provides simultaneous transmission of user data, signaling data and other related traffic through a network.
Advantage – high speed signaling is not limited by low speed voice data
Substantial increase in the number of users

## Slide 21: Advantages of CCS
Advantage – high speed signaling is not limited by low speed voice data
Substantial increase in the number of users

## Slide 22: CCS network structure
SMS
MSC
SEPs
SS7
SS7
STPs
STPs

## Slide 23: CCS network components
CCS network architecture is composed of geographically distributed central switching offices.
Service Management system (SMS)
Switching end points (SEPs)
Signaling transfer points(STPs)
Database service management system(DBAS)

## Slide 24: Third Generation Wireless Networks
Aim is to provide a single set of standards that can meet a wide range of wireless applications, and provide universal access around the globe => voice, data and video

## Slide 25: Integrated Services Digital Network (ISDN)
Parallel worldwide network for CCS signaling traffic that can be used to either route traffic on PSTN or provide new services between network nodes and end users
ISDN has 2 types of channels:
  Information bearing channels called Bearer channels (B channels)
  Out of band signaling channels, called data channels (D channels)

## Slide 26: Broadband ISDN (B-ISDN)
End user applications require greater bandwidth for computer systems and video imaging
Based on asynchronous transfer mode (ATM) technology which allows packet switching – 100 Gbps

## Slide 27: Future Wireless Networks
Based on B-ISDN to provide access to information networks such as Internet and other public and private databases
PCS - Personal Communication System
PCN - Personal Communication Network
International Mobile Telecommunication (IMT –2000)
Universal Mobile Telecommunication System (UMTS)- Europe