## Slide 1: Mobile Radio Propagation
Mobile radio channel is an important factor in wireless systems.
Wired channels are stationary and predictable, while radio channels are random and have complex models.
Modeling of radio channels is done in statistical fashion based on receiver measurements.

## Slide 2: Types of propagation models
Large scale propagation models
  To predict the average signal strength at a given distance from the transmitter
  Controlled by signal decay with distance
Small scale or fading models.
  To predict the signal strength at close distance to a particular location
  Controlled by multipath and Doppler effects.

## Slide 3: Radio signal pattern
-30
-40
-50
-60
-70
16
18
20
22
24
26
28
14
T-R Separation (meters)
Received Power (dBm)

## Slide 4: Measured signal parameters
Electrical Field (Volts/m)
Magnitude E = IEI
Vector
Direction E = xEx + yEy + zEz
Power (Watts or dBm)
  Power is scalar quantity and easier to measure.

## Slide 5: Relation between Watts and dBm
P (dBm) = 10 log10 [ P (mW)]
P(mW) | P(dBm)
10 | 10
1 | 0
10-1 | -10
10-2 | -20
10-6 | -60

## Slide 6: Physical propagation models
Free Space Propagation
  Transmitter/receiver have clear LOS (Line Of Sight) path
Reflection
  Wave reaches receiver after reflection off surfaces larger than wavelength
Diffraction
  Wave reaches receiver by bending at sharp edges (peaks) or curved surfaces (earth).
Scattering
  Wave reaches receiver after bouncing off objects smaller than wavelength (snow, rain)

## Slide 7: Free Space Propagation
Transmitter and receiver have clear, unobstructed LOS path between them.
(Courtesy: webbroadband.blogspot.com)

## Slide 8: LOS (Friis) transmission equation
Pr = Pt Gt Gr 2
(4)2 d2 L
Pt = Transmitted Power (W)
Pr = Received Power (W)
Gt = Transmitter antenna gain
Gr = Receiver antenna gain
L = System loss factor
  Due to line losses, but not due to propagation
  L  1

## Slide 9: Antenna Gain
Power Gain of antenna
G = 4Ae / 2,
Ae is effective aperture area of antenna
Wavelength  = c / f (Hz)
= 3 • 108 / f , meters

## Slide 10: Example
A transmitter produces 50W of power. If this power is applied to a unity gain antenna with 900 MHz carrier frequency, find the received power at a LOS distance of 100 m from the antenna. What is the received power at 10 km? Assume unity gain for the receiver antenna.

## Slide 11: Solution
Pr = Pt Gt Gr 2
(4)2 d2 L
Pt = 50 W, Gt = 1, Gr = 1, L = 1, d = 100 m
 = (3 • 108) / (900 • 106) = 0.33 m
Solving, Pr = 3.5 • 10-6 W
Pr (10 km) = Pr (100 m) • (100/10000)2
= 3.5 • 10-6 • (1/100)2
= 3.5 • 10-10 W

## Slide 12: Electric Properties of Material Bodies
Fundamental constants
Permittivity  = 0 r , Farads/m
Permeability  = 0 r ,Henries/m
Conductivity , Siemens/m
Types of materials
  Dielectrics – allow EM waves to pass
  Conductors – block EM waves
  Metamaterials – bend EM waves

## Slide 13: Ground Reflection (2-Ray Model)
Pi
PLOS
Pref
Pr = PLOS +Pref
R (receiver)
hr
ht
T (transmitter)
d

## Slide 14: Ground Reflection Equations
For d > 20hthr / ,
Received power Pr=

## Slide 15: Example
A mobile is located 5 km away from a base station, and uses a vertical /4 monopole antenna with a gain of 2.55dB.
Assuming carrier frequency of 900 MHz and transmitted power of 100 W with 10 dB antenna gain, find the received power at the mobile using the 2-ray model if the height of the transmitting antenna is 50 m and receiving antenna is 1.5 m above the ground.

## Slide 16: Solution
Pi
PLOS
Pref
Pr = PLOS +Pref
R (receiver)
1.5
50
T (transmitter)
d

## Slide 17
Gain of receiving antenna = 2.55 dB => 1.8
Gain of transmitting antenna = 10 dB => 10
Received power Pr=
= 100 • 10 • 1.8 • 502 • 1.52
(5 • 103)4
= 0.0162 mW

## Slide 18: Diffraction
Diffraction allows radio signals to propagate around the curved surface or propagate behind obstructions.
(Courtesy: electronics-notes.com)

## Slide 19: Knife-edge Diffraction Geometry
hr
h’
ht
R
T
h
d1
d2




## Slide 20: Diffraction Parameter and Gain
Diffraction parameter
v =
Diffracted power = LOS power+ Diffraction Gain
Pd = PLOS + Gd (dB)

## Slide 21: Empirical formula for Gain
v Gd (dB)
v  -1 0
-1  v  0 20 log (0.5 – 0.62 v)
0  v 1 20 log (0.5 e-0.95v )
1  v  2.4 20 log (0.4 – √ [0.1184 – (0.38 – 0.1 v)2]
v  2.4 20 log (0.225 / v)

## Slide 22: Example
Compute the diffraction power at the receiver assuming:
Transmitter frequency = 900 MHz
LOS received power = 50 mW
d1 = 1 km
d2 = 1 km
h = 25 m

## Slide 23: Solution
Diffraction parameter v =
 = (3 • 108) / (900 • 106) = 0.33 m
=> v = = 2.74
Using the table,
Gd (dB) = 20 log (0.225/2.74) = -22 dB
Hence diffracted power Pd = PLOS + Gd (dB)
= 10 log(50) -22
= -5.01 dBm => 0.316 mW

## Slide 24: Scattering
When a radio wave impinges on a rough surface, the reflected energy is spread out in all directions
Examples of scattering surfaces: lamp posts,
trees, cars, rain, snow.
(Courtesy:http://www.tpub.com/)

## Slide 25: Radar Cross Section (RCS) Model
RCS (Radar Cross Section) =
Power density of scattered wave in direction of receiver
Power density of radio wave incident on the scattering object

## Slide 26: Scattering Power Equation
PR = PT • GT • 2 • RCS
(4)3 • dT 2 • dR 2
PT = Transmitted Power
GT = Gain of Transmitting antenna
dT = Distance of scattering object from Transmitter
dR = Distance of scattering object from Receiver

## Slide 27: Practical Propagation models
Most radio propagation models are derived using a combination of analytical and empirical models.
Empirical approach is based on fitting curves or analytical expressions that recreate a set of measured data.

## Slide 28: Pros and cons of empirical models
Takes into account all propagation factors, both known and unknown.
Disadvantages: New models need to be measured for different environment or frequency.

## Slide 29: Path Loss (PL) Model
T d0 R
PT PR(d0) PR(d)
Transmitter – receiver model
PL(d) = PL(d0) + 10n log10 (d/d0)
Logarithmic model ( dB)
Received power( dBm)
PR(d) = Pt – PL(d)

## Slide 30: Emprical values of path loss factor n
Environment n
Free space 2
Urban area cellular radio 2.7 – 3.5
LOS in building 1.6 – 1.8

## Slide 31: More accurate propagation models
Logarithmic path loss normal gives only the average value of path loss.
Surrounding environment may be vastly different at two locations having the same T – R separation d.
More accurate model includes a random variable with standard deviation  to account for change in environment.

## Slide 32: Practical propagation model development
Values of n and  are computed from measured data.
Linear regression method which minimizes the difference between measured and estimated path
Estimated over a wide range of measurement locations and T – R separations.

## Slide 33: Random Propagation Model equation
Probability [ PR (d) >  ] =
Probability [ PR (d) <  ] =
Average received power is calculated
using logarithmic model

## Slide 34: Calculation of Q Function
e
-
x
2
/
2
z
x
Q(z) = Q function =
Q(z) table from Appendix F of book (Rappaport), for z values 0 < z < 3.9
For z > 3.9, use the approximation:

## Slide 35: Q Function Table

## Slide 36: Example
Four received power measurements were taken at the distances of 100m, 200m, 1 km and 3 km from a transmitter.
T-R distance Measured Power
100 m 0 dBm
200 m - 20 dBm
1 km - 35 dBm
3 km - 70 dBm

## Slide 37: Example
a. Find the minimum mean square error (MMSE) estimate for the path loss exponent n, assuming d0 = 100m.
b. Calculate the standard deviation about the mean value.
c. Estimate the received power at d = 2 km using the resulting model.
d. Predict the likelihood that the received signal at 2 km will be greater than –60 dBm.

## Slide 38: Solution
Let Pi be the average received power at distance di :
Pi (d) = P (d0) – 10n log (d /100)
d = d0 = 100m
= Pi (d0) = P0= 0 dBm

## Slide 39: a.
d1= 200 m, P1= -3n,
d2= 1 km, P3= -10n,
d3= 3 km, P4= -14.77n
Mean square error J =  (P – Pi)2
= (0 – 0)2 + [-20 – (-3n)] 2 + [-35 – (-10n)] 2 + [-70 – (-14.77n)] 2
= 6525 – 2887.8n + 327.153n2
Minimum value = > dJ(n) / dn
= 654.306n – 2887.8 = 0  n = 4.4

## Slide 40: b.
Variance 2 = J / 4 = ( P – Pi)2 / 4
= (0 + 0) + (-20 +13.2)2 + (-35 + 44)2 + (-70 + 64.988)2
4
= 152.36 / 4 = 38.09
  = 6.17 dB

## Slide 41: c.
Pi (d = 2 km)
= 0 – 10(4.4) log (2000/100)
= -57.24 dBm

## Slide 42: d.
Probability that the received signal will be greater than –60 dBm is:
_____
PR = [PR(d) > -60 dBm] = Q [(g- PR (d)) / s ]
= Q [(-60 + 57.24) / 6.17 ]
= Q [- 0.4473]
= 1 – Q [0.4473]
= 1 – 0.326
= 0.674 = > 67.4%

## Slide 43: Percentage of Coverage Area
Given a circular coverage area of radius R
In the area A, the received power PR  
The area A is defined as U()
Area A
r
R

## Slide 44: Calculation of Coverage Area U()
Use Figure 4.18 from book (Rappaport)

## Slide 45: Example
For the previous problem, predict the percentage of area with a 2 km radius cell that receives signals greater than –60 dBm.

## Slide 46: Solution
From solution to previous example,
Prob [PR (R) > ] = 0.674
=>( / n) = 6.17 / 4.4
= 1.402
From table 4.18, Fraction of total area = 0.92 => 92%

## Slide 47: Outdoor Propagation Models
  Longley Rice model point-to-point communication systems (40MHz–100MHz)
  Okumara’s model widely used in urban areas (150 MHz – 300 MHz)
  Hata model graphical path loss (150 MHz – 1500 MHz)

## Slide 48: Indoor Propagation Models
  Log-distance path loss model
  Ericsson multiple breakdown model