## Slide 1: Multiple Access Techniques for wireless communication
Multiple access schemes allow many mobile users to share a finite amount of radio spectrum
High quality of communications must be maintained during the sharing process

## Slide 2: Multiple Access Techniques
Multiple Access Techniques
FDMA
TDMA
CDMA/SDMA
Frequency Division Multiple Access (FDMA)
Time Division Multiple Access (TDMA)
Code Division Multiple Access (CDMA)
Space Division Multiple Access (SDMA)

## Slide 3: Multiple Access (MA) Technologies
Cellular System | MA Technique
AMPS ( Advanced Mobile Phone system ) | FDMA / FDD
GSM ( Global System for Mobile ) | TDMA / FDD
US DC ( U. S Digital Cellular ) | TDMA / FDD
JDC ( Japanese Digital Cellular ) | TDMA / FDD
IS – 95 ( U.S Narrowband Spread Spectrum ) | CDMA / FDD

## Slide 4: Capacity of Cellular Systems
Channel capacity of a wireless system is the maximum number of users possible in the system
Channel capacity depends on:
  Bandwidth available
  Signal to Noise ratio (SNR) in the channel

## Slide 5: Principle of FDMA Operation
Each user is allocated a unique frequency band or channel. These channels are assigned on demand to users who request service
In FDD, the channel has two frequencies – forward channel & reverse channel

## Slide 6: Cell capacity of FDMA System Capacity/cell N

## Slide 7: Example
In the US, each cellular carrier has 416 channels. Assuming negligible noise input, calculate the number of users possible.

## Slide 8: TDMA Operating principle
TDMA systems divide each FDMA channel into time slots
Each user occupies a cyclically repeating time slot
TDMA can allow different number of time slots for separate user

## Slide 9: TDMA Frame Structure
Preamble | Information message | Trail Bits
Slot 1 | Slot 2 |  | Slot N
Trail Bit | Sync Bit | Information Bit | Guard Bits

## Slide 10: Components of TDMA Frame
Preamble  Address and synchronization information for base station and subscriber identification
Guard times  Synchronization of receivers between different slots and frames

## Slide 11: Efficiency of TDMA
Frame Efficiency

## Slide 12: Cell capacity in TDMA System m = number of TDMA users (slots) in channel

## Slide 13: Example
If a GSM timeslot consists of 6 trailing bits, 8.25 guard bits, 26 training bits, and 2 traffic bursts of 58 bits of data, find the frame efficiency.
Solution
Time slot has 6+ 8.25+ 26 + 2(58) = 156.25 bits.
Frame has 8 * 156.25 = 1250 bits / frame.
The number of overhead bits per frame is:
bOH = 8(6) + 8(8.25) + 8(26) = 322 bits
Frame efficiency = (1250 – 322 )/1250 = 74.24 %

## Slide 14: Capacity of Digital Cellular CDMA
Capacity of FDMA and TDMA system is bandwidth limited.
Capacity of CDMA system is interference limited.
The link performance of CDMA increases as the number of users decreases.

## Slide 15: Number of possible users in CDMA
h is the background thermal noise
S is the average user power
W is the total RF bandwidth
R is the information bit rate

## Slide 16: Techniques to improve capacity
Antenna Sectorization
Sectoral antennas at 120 degrees increases the capacity by a factor of 3
Monitoring or Voice activity a
Each transmitter is switched off during period of no voice activity

## Slide 17: Capacity Improvement
Number of users/sector
Number of users x Number of sectors

## Slide 18: Example
If W = 1.25 MHz, R= 9600 bps and SNR is 10 dB, determine the maximum number of users that can be supported in a CDMA system using:
(a) omni directional base station antennas and no voice activity detection
(b) 3 sectors at base station and a = 3/8. Assume the system is interference limited. h = 0.

## Slide 19: Solution
(a)
users

## Slide 20
(b) Users per sector
Total users in 3 sectors = 3 x 35.7 ~ 107 users

## Slide 21
Total users N in 3 sectors