## Slide 1: Chapter 1: Types of Electronic Communication Systems

## Slide 2: Technology that links the world
Types of communication systems
  Coaxial (Wired)
  Microwave (Wireless)
  Satellite (Wireless)
  Cable (Wired)
  Cellular (Wireless)

## Slide 3: Coaxial
Courtesy: customer.xfinity.com

## Slide 4: Microwave
Courtesy: https://www.smithandfisher.com

## Slide 5: Satellite
Courtesy: www.airforce-technology.com

## Slide 6: Cable (undersea network)
Courtesy: TeleGeography:
https://www.submarinecablemap.com/

## Slide 7: Cellular
Courtesy: https://dgtlinfra.com/cell-tower-locations-4g-lte-5g-towers/

## Slide 8: Path loss in communication links
Transmitter Pt, W
Receiver Pr, W

## Slide 9: Path loss factors
Path loss is the loss of power in the transmitted signal
Causes of path loss
  Dispersion which causes power to spread out in all directions from transmitter
  Objects such as buildings, trees, street lights, snow, rain
Amplifiers can be used in path to boost the signal => repeaters

## Slide 10: Path loss calculation
Path loss (PL, magnitude) is defined as:
PL, magnitude = Transmitted power,W
Received power, W
Path loss (PL, dB) is defined as:
PL, dB = Transmitted power, dBm – Received power, dBm

## Slide 11: Power calculation
Power (dBm) = 10 log [Power (mW)]
dB is unit of path loss
For example, if Pt = 10 dBm; path loss = 30 dB
=> Pr = 10 dBm – 30 dB = -20 dBm
Power (mW) | Power (dBm)
0.01 | -20
0.1 | -10
1 | 0
10 | 10
100 | 20

## Slide 12: Introduction to Matlab/Simulink
Matlab and Simulink are widely used to design and simulate Communication Systems
Matlab is program based solution
  Ideal for programming complex system formulae
  Equation solving and optimization
Simulink is graphic based solution
  Ideal for simulation of system models
  System block based approach gives visual perspective
  New blocks can be created from Matlab programs

## Slide 13: Basic Matlab command symbols
Mathematical symbols
  + Addition
  - Subtraction
  * Multiplication
  / Division
  ^ Exponent
  ’ Transpose of vector or matrix
Logical symbols
  & And
  | Or
  > (>=) Greater than (or equal)
  < (<=) Less than (or equal)

## Slide 14: Basic Matlab commands
Vector command
  >>t=0:0.1:0.8
  generates the vector t from 0 to 0.8 in steps of 0.1:
  t = [0 0.1 0.2 0.3 0.4 0.5 0.6 0.7 0.8]
To generate a function y(t) = cos(2t) t2,
  t = 0,2 sec., use the following commands:
  >> t = 0:0.1:2
  >> y = cos(2*t).*t.^2
  Note the “.” symbol after vector commands

## Slide 15: Simulink Basics
Simulink is based on assembling blocks to create a model
Simulink blocks are selected from the Library Browser and copied into the Model window
Different blocks are connected together by joining the input/output block connectors
The full model is ready and ready for simulation

## Slide 16: Simulink Library
Simulink library is composed of many sub-libraries and toolboxes
Sub-libraries are general blocks
  Sinks and sources
  Continuous and discrete
  Math operations
Toolboxes are specialized blocks
  DSP
  Communications
  Control systems
  Simscape (Power systems)

## Slide 17: Simulink Example Model

## Slide 18: Simulink output generation
Set Simulink parameters
  Start time and stop time
  Type of solver (fixed time or variable time)
  Time step size (default is auto)
Run the simulation
Trouble shoot if error messages appear
Obtain output in different formats
  Plots
  Output files
  Output code (C, Verilog)

## Slide 19: Communication system equipment
Sources are used to generate communication signals from the transmitter
Measurement devices are used to monitor and record communication signals at both transmitter and receiver
Radio Frequency Integrated Circuits are complete communication systems built on chips- also called as System on Chips (SOCs)

## Slide 20: Sources
Keysight 33600A Waveform Generator
(Courtesy: Keysight Technologies)

## Slide 21: Measurement devices - Time
Keysight DS090254A digital storage oscilloscope
(Courtesy: Keysight Technologies)

## Slide 22: Measurement devices - Frequency
Keysight N9000A Signal Analyzer
(Courtesy: Keysight Technologies)

## Slide 23: Radio Frequency Integrated Circuits (RFICs)
TI CC2540 Bluetooth SOC (System on Chip)
(Courtesy: Texas Instruments)