## Slide 1: Chapter 2: Time/Frequency analysis of communication signals and systems

## Slide 2: Concept of carrier signal in communication systems
Carrier is strong and stable sinusoidal signal x(t) = A cos(wc t + q)
Carrier transports information (audio, video, text, email) across the world
Why is the carrier required?
  Audio and video signals cannot travel over large distances since they are weak
  A carrier is like a plane which transports passengers over long distances

## Slide 3: Signal power
General equation for signal power Px
For periodic signals, integration is over one period:
For sinusoidal signals: x(t) = A cos(wc t + q)
Power Px = A2/2

## Slide 4: Signal bandwidth
Signal bandwidth is the difference between its maximum frequency and minimum frequency
  Example : x(t) = 5 cos(1500t + 46 o) + 10 sin(2400t + 10 o)
  Maximum frequency= 2400 rad./s
  Minimum frequency= 1500 rad./s
  Hence, bandwidth = 2400-1500 = 900 rad./s
Commonly used signals
  Audio (Speech, Music) has 20 KHz bandwidth
  Video has 5 MHz bandwidth

## Slide 5: Estimation of signal spectrum by Fourier Transform
Frequency content or bandwidth of a signal x(t) is estimated by Fourier Transform (FT)
The signal can be recovered from its spectrum by Inverse Fourier Transform (IFT)

## Slide 6: Spectrum of periodic signals
A periodic signal x(t) has discrete spectrum, existing only at frequencies of nw0, n an integer:
The signal can be recovered from its spectrum by the Fourier series

## Slide 7: Power and Energy relations in the Fourier domain
Parseval’s theorem for signal energy Ex
Power relation for periodic signals

## Slide 8: Practical communication signals and their frequency spectra

## Slide 9: Frequency analysis of communication systems
Input-output system
Types of systems
  Linear systems (ex. resistor)
  Non-linear systems (ex. transistor)

## Slide 10: Linear Systems
Linear systems obey the law of superposition
Time domain input/output relation
Frequency domain input/output relation

## Slide 11: Nonlinear Systems
Nonlinear systems do not obey superposition
Time domain input/output relation (example)
Frequency domain input/output relation (above )example

## Slide 12: Practical methods of Spectrum Analysis: DFT and IDFT
Discrete Fourier Transform (DFT)
Inverse Discrete Fourier Transform (IDFT)
Time-frequency relation in DFT
Dw = 2p/(N Dt)

## Slide 13: Discrete-time system analysis - Circular Convolution
N point circular convolution
y(n) = x(n) N h(n)
=
Shift is done circularly, not linearly
All sequences (x,h,y) are of length N
  Very convenient for computer usage
  N is usually a power of 2

## Slide 14: Computation of circular convolution using FFT
Step1: Obtain the N-point DFTs of the sequences x(n) and h(n)
Step2: Multiply the two DFTs X(k) and H(k), for k = 0, 1, 2……N-1
Step3: Obtain the N-point IDFT of the sequence Yk), to yield the final output y(n)

## Slide 15: The Fast Fourier Transform (FFT)
FFT is a fast way to compute DFT
N-point DFT is slow to compute
  Number of computations is N2
Radix-2 (N is power of 2) FFT is most efficient
  Number of computations is N log2N
Example: For N = 64 =>
DFT requires 64 x 64 = 4096 computations
FFT requires 64 x 6 = 384 computations

## Slide 16: FFT for convolution
Number of computations using DFT
Step 1: 2N2
Step 2: N
Step 3: N2
Total computations = 3N2 + N
T
Number of computations using FFT
Step 1: 2N log2N
Step 2: N
Step 3: log2N
Total computations = 3 log2N + N