## Slide 1: Chapter 3: First generation systems-Analog Modulation

## Slide 2: What is modulation
Message signals such as audio, video, text, email are weak power signals
Message signals need a carrier signal to travel long distances
The process of combining message and carrier signals is called modulation

## Slide 3: Amplitude Modulation (AM)

## Slide 4: Double sideband modulation (DSB)
Time domain equation
    yAM(t) = Information or message x carrier
    = m(t) x A cos(wct)
Frequency domain equation

## Slide 5: DSB power and bandwidth
Power in DSB signal
  DSB-C (with carrier)
  = Carrier Power + Carrier Power x Message power
  DSB-SC (suppressed carrier)
              = Carrier Power x Message power
Bandwidth of DSB signal = 2wm

## Slide 6: Single Sideband Modulation (SSB)
Balanced Modulator SSB generation
ySSB(t)=0.5m(t)cos(wct)±0.5 sin(wct)
SSB power and bandwidth
  SSB power = DSB power/2
  SSB bandwidth = DSB bandwidth/2

## Slide 7: Balanced modulator for SSB generation

## Slide 8: AM Parameters
Modulation index m
Modulation efficiency h
, -1 < m < 1,

## Slide 9: AM Receiver or demodulation
Demodulation is the process of extracting the message from the AM signal

## Slide 10: Angle Modulation

## Slide 11: Types of Angle Modulation
Frequency Modulation (FM)
Phase Modulation (PM)

## Slide 12: FM/PM power and bandwidth
Power in FM/PM signal
Bandwidth of FM/PM signal
BFM/PM = 2B (1+b)
Modulation index

## Slide 13: Comparison of AM and FM modulation systems
FM is less susceptible to noise as compared to AM
FM has better sound quality than AM; however, this also requires higher bandwidth than AM.
Power requirement is less in FM as compared to AM
FM has shorter range of transmission, requiring Line of Sight (LOS) propagation.

## Slide 14: Noise performance of AM and FM circuits
Channel interference is estimated by Signal to Noise ratio (SNR)
SNR in AM is constant
SNRAM = SNRbaseband
SNR in FM can be improved by increasing the modulation index b
SNRFM = 1.5 b2SNRbaseband

## Slide 15: Output SNR of AM/PM systems

## Slide 16: Filtering techniques in AM/FM systems
Filters can minimize noise in AM/FM systems
Weiner Filter can adapt to signal power (Sx) and channel noise power (Sn) densities