## Slide 1: EEE 244-3: MATRICES AND EQUATION SOLVING

## Slide 2: Application of Matrices
Matrices occur in solution of linear equations
for Electrical Engineering problems
Example of linear equations:
Voltage-current relation
  V1 = Z11 I1 + Z12 I2
  V2 = Z21 I1 + Z22 I2

## Slide 3: Matrix structure
A matrix consists of a rectangular array of elements represented by a single symbol (example: A).
An individual entry of a matrix is an element (example: a23)
A =

## Slide 4: Matrix elements
A horizontal set of elements is called a row and a vertical set of elements is called a column
The first subscript of an element indicates the row while the second indicates the column
The size of a matrix is given as m rows by n columns, or simply m by n (or m x n)

## Slide 5: Special Matrices
Matrices where m=n are called square matrices
There are a number of special forms of square matrices:

## Slide 6: Matrix Inverse
The inverse of a square, nonsingular matrix A is that matrix which, when multiplied by A, yields the identity matrix.
  A A-1= A A-1 = I
Matlab | Python
A = [ 3 6 7; 5 -3 0;1 1 1] B = inv(A) | import numpy as np A = np.array([[3,6,7],[5 -3, 0],[1, 1, 1]]) B = np.linalg.inv(A) print(B)

## Slide 7: Matrix Transpose
The transpose of a matrix involves transforming its rows into columns and its columns into rows.
  (aij)T=aji
Matlab | Python
A = [ 3 6 7; 5 -3 0] B = A’ | import numpy as np A = np.array([[3, 6, 7], [5, -3, 0]]) B = np.transpose(A) print(B)

## Slide 8: System of linear equations
  a11 x1 + a12 x2 + a13 x3 ……… a1n xn = c1
  a21 x1 + a22 x2 + a23 x3 ……… a2n xn = c2
  .
  .
  .
  an1 x1 + an2 x2 + an3 x3 ……… ann xn = cn

## Slide 9: Matrix equation
AX = C

## Slide 10: Solving With MATLAB/Python
MATLAB/Python can solve system of linear algebraic equations
AX = C
Matlab | Python
% Matrix inversion A = […] C = […] X = inv(A)*C % Gaussian elimination % or Left division X = A\C | import numpy as np A = np.array([[…..]) C = np.array([[…..]) X = np.linalg.inv(A) X = X.dot(C) print(X)

## Slide 11: Example electric circuit problem
Find the resistor currents in the circuit below:

## Slide 12: KVL equations
I1
I2
-10 + (I1-I2) x 100 = 0 => 100 I1 -100 I2 = 10
(I2-I1) x 100 + I2 x 100 -10 = 0 => -100 I1 +200 I2 = 10

## Slide 13: Matrix equation

## Slide 14: MATLAB/Python solution
MATLAB/Python can solve system of linear algebraic equations
AX = C
Matlab | Python
clear A = [100 -100; -100 200] C = [10; 10] X = inv(A)*C | import numpy as np A = np.array([[100, -100],[-100, 200]]) C = np.array([[10],[10]]) X = np.linalg.inv(A) X = X.dot(C) print(X)

## Slide 15: Roots of equations
Engineering problems involve finding roots of complex equations
Equations can be of different types:
  Polynomials with powers of x
  Example: x3 + 2x2 – 4x +1 = 0
  Transcendental functions containing sin(x), ex, log(x)
  Example: sin(x) – 4x +1 = 0
Solution of complex equations require
numerical techniques

## Slide 16: Graphical Methods
Zero crossing is a simple method for obtaining the estimate of the root of the equation f(x)=0
Graphing the function can also indicate types of roots:
  Same sign, no roots
  Different sign, one root
  Same sign, two roots
  Different sign, three roots

## Slide 17: Search Method
Make two initial guesses that bracket the root:
f(x)=0
Find two guesses xi and xi+1 where the sign of the function changes; that is, where f(xi ) f(xI+1 ) < 0
.

## Slide 18
Incremental Search Method
Tests the value of the function at evenly spaced intervals
Finds brackets by identifying function sign changes between neighboring points

## Slide 19: Incremental Search Hazards
If the spacing between the points of an incremental search are too far apart, brackets may be missed
Incremental searches cannot find brackets containing even-multiplicity roots regardless of spacing.

## Slide 20: Bisection
The bisection method is the incremental search method in which the interval is always divided in half
If a function changes sign over an interval, the function value at the midpoint is evaluated

## Slide 21: Newton-Raphson Method
Form the tangent line to the f(x) curve at some guess x,
then follow the tangent line to where it crosses the x-axis.

## Slide 22: Transcendental Functions
MATLAB/Python use fsolve command to find roots of transcendental function
Step 1: Define the function, for example
f(x) = 2x+cos(x) = 0
Step 2: Use the fsolve command (initial guess x0)
Matlab | Python
clear f=@(x) 2*x+cos(x) x0=0.01 x = fsolve(f,x0) | import numpy as np from scipy.optimize import fsolve def fun(x): return 2*x+np.cos(x) x=fsolve(fun,0.01)

## Slide 23: Polynomials
MATLAB/Python have built in program called roots to determine all the roots of a polynomial
Step 1: Define the vector c with polynomial coefficients. Example: For x3+2x2+4x+1=0
c = [1 2 4 1]
Step 2: Use the roots command
Matlab | Python
clear c = [1 2 4 1] x = roots(c) | import numpy as np c = [1,2,4,1] x = np.roots(c) print(x)

## Slide 24: Polynomial commands
MATLAB/Python have poly function which can be used to determine polynomial coefficients if roots are given:
  b = poly([v])
    v is the vector containing roots of the polynomial
    b is the vector with polynomial coefficients
MATLAB/Python have polyval function which can evaluate a polynomial at one or more points:
  polyval(b, 1)
    This calculates the value of the polynomial at x=1