## Slide 1: EEE 244-8: Optimization techniques for System Design

## Slide 2: Introduction to optimization
Objective of optimization is to maximize or minimize some function, called the object function f
General examples of optimization are:
  Maximize profit for a company (object function: profit)
  Minimize production costs of a company (object function: production costs)
Engineering examples of optimization are:
  Maximize gain of an amplifier (object function: gain)
  Minimize resistive loss in power line from generator to load (object function: resistive loss)

## Slide 3: Types of optimization
Optimization is mainly of two types:
  Unconstrained optimization
  Constrained optimization
Example of unconstrained optimization:
  Minimize or maximize y = 2x2 – 3x
  => dy/dx = 4x – 3 = 0
  => x = 3/4 gives position of minimum or maximum
Example of constrained optimization:
  Minimize or maximize y = 2x2 – 3x in the range of x = 3,5
  Solution x = 3/4 will not satisfy this constraint

## Slide 4: Practical optimization
The object function f may be dependent of many control variables x1, x2, x3….xn
Constrained optimization is generally more complex than unconstrained optimization
Computational methods are very useful in solving constrained optimization problems

## Slide 5: Matlab solution by plotting function
Solve the constrained optimization below :
  Minimize or maximize y = 2x2 – 3x in the range of x = 3,5;
% Matlab program to plot function
clear
x=3:.01:5
y=2*x.^2-3*x;
plot(x,y); verify maximum and minimum values from plot

## Slide 6: Unconstrained optimization
Given an object function f that is dependent on control variables x1, x2, x3….xn; the minimum or maximum at point P is given by the condition:
Practical implementation of this formula is called Method of Steepest Descent
  Solution moves iteratively from point to point until optimum point is reached

## Slide 7: Matlab/Python commands for unconstrained optimization
Given an object function f(x), and starting value x0, the point at which the function reaches a minimum is given by the following commands:
x can be vector of variables x = [x1 x2 …….xn]
Matlab | Python
clear f=@(x) f(x) [xmin fmin]=fminunc(f,x0) | import numpy as np from scipy import optimize def f(x): return f(x) [x1,x2,] = optimize.fmin(f, x0)

## Slide 8: Matlab/Python commands for unconstrained maximization
Given an object function f(x), and starting value x0, the point at which the function reaches a maximum is given by the following commands:
Matlab | Python
clear f1=@(x) -f(x) [xmax fmax] = fminunc(f1,x0) fmax=-fmax | import numpy as np from scipy import optimize def f1(x): return -f(x) xmax = optimize.fmin(f1, x0) fmax=-fmax

## Slide 9: Unconstrained optimization with 2 variables
Minimize the function f(x,y) = 2x +3y + x2 + y2 -9, given the initial condition x0 = 2, y0 = 3
  clear
  f = @ (x) 2*x(1) + 3*x(2) + x(1)^2 + x(2)^2 -9;
  x0 = [2 3];
  [xmin fmin] = fminunc(f,x0)

## Slide 10: Conditions for constrained optimization
Given an object function f that is dependent on control variables x1, x2, x3….xn; find the minimum or maximum at point P
In addition, we have the inequality constraints
or, A*X <= B

## Slide 11: Matlab/Python commands for constrained optimization
Given an object function f(x), and starting value x0, the point at which the function reaches a minimum, with the inequality constraints are A*x <=B, is given by the following commands (Note: for Python use A*x >=B):
Matlab | Python
clear f=@(x) f(x) xmin = fmincon(f,x0,A,B) | import numpy as np from scipy import optimize def f(x): return f(x) cons = ({'type': 'ineq', 'fun' : lambda x: np.array()}, xmin = optimize.minimize(f, x0,constraints =cons)

## Slide 12: Matlab example for constrained optimization
Minimize the function f(x,y) = 2x +3y + x2 + y2 -9, given the initial condition x0 = 2, y0 = 3, and the constraints: x +y <= 3; 2x – 3y <= -5
  clear
  f = @ (x) 2*x(1) + 3*x(2) + x(1)^2 + x(2)^2 -9;
  A=[1 1; 2 -3];
  B=[3;-5];
  x0 = [2 3];
  [xmin fmin] = fmincon(f,x0,A,B)