# Chapter 6 Solutions

1.	OT = 450 minutes

a.	Minimum cycle time = length of longest task, which is 2.4 minutes.

Maximum cycle time = ( task times = 18 minutes.

b.	Range of output:

c.

d.

e.	Potential output:

(1)

(2)

2.

Desired output = 33.33 units per hour

Operating time = 60 minutes per hour

Solutions (continued)

a.

| Task | Number of following tasks | Positional Weight |
| --- | --- | --- |
| A | 7 | 6 |
| B | 6 | 4.6 |
| C | 2 | 1.6 |
| D | 2 | 2.2 |
| E | 2 | 2.3 |
| F | 1 | 1.0 |
| G | 1 | 1.5 |
| H | 0 | 0.5 |

Assembly Line Balancing Table  (CT = 1.8)

| Work Station | Task | Task Time | Time Remaining | Feasible tasks Remaining |
| --- | --- | --- | --- | --- |
| I | A | 1.4 | 0.4 | – |
| II | B | 0.5 | 1.3 | C, D, E |
|  | E | 0.8 | 0.5 | – |
| III | D | 0.7 | 1.1 | C |
|  | C | 0.6 | 0.5 | F |
|  | F | 0.5 | 0 | – |
| IV | G | 1.0 | 0.8 | H |
|  | H | 0.5 | 0.3 | – |

b. 		Assembly Line Balancing Table  (CT = 1.8)

| Work Station | Task | Task Time | Time Remaining | Feasible tasks Remaining |
| --- | --- | --- | --- | --- |
| I | A | 1.4 | 0.4 | – |
| II | B | 0.5 | 1.3 | C, D, E |
|  | E | 0.8 | 0.5 | – |
| III | D | 0.7 | 1.1 | C |
|  | C | 0.6 | 0.5 | F |
|  | F | 0.5 | 0 | – |
| IV | G | 1.0 | 0.8 | H |
|  | H | 0.5 | 0.3 | – |

Solutions (continued)

c.

3.

Desired output = 4

Operating time = 56 minutes

| Task | # of Following tasks | Positional Weight |
| --- | --- | --- |
| A | 4 | 23 |
| B | 3 | 20 |
| C | 2 | 18 |
| D | 3 | 25 |
| E | 2 | 18 |
| F | 4 | 29 |
| G | 3 | 24 |
| H | 1 | 14 |
| I | 0 | 5 |

Solutions (continued)

a.	First rule: most followers. Second rule: largest positional weight.

Assembly Line Balancing Table  (CT = 14)

| Work Station | Task | Task Time | Time Remaining | Feasible tasks Remaining |
| --- | --- | --- | --- | --- |
| I | F | 5 | 9 | A,D,G |
|  | A | 3 | 6 | B,G |
|  | G | 6 | – | – |
| II | D | 7 | 7 | B, E |
|  | B | 2 | 5 | C |
|  | C | 4 | 1 | – |
| III | E | 4 | 10 | H |
|  | H | 9 | 1 | – |
| IV | I | 5 | 9 | – |

b. 	First rule: Largest positional weight.

## Assembly Line Balancing Table  (CT = 14)

| Work Station | Task | Task Time | Time Remaining | Feasible tasks Remaining |
| --- | --- | --- | --- | --- |
| I | F | 5 | 9 | A,D,G |
|  | D | 7 | 2 | – |
| II | G | 6 | 8 | A, E |
|  | A | 3 | 5 | B,E |
|  | B | 2 | 3 | – |
| III | C | 4 | 10 | E |
|  | E | 4 | 6 | – |
| IV | H | 9 | 5 | I |
|  | I | 5 | – |  |

c.

Solutions (continued)

4.	a, b

a.	l.

2. 	Minimum Ct = 1.3 minutes

|  | Task | Following tasks |
| --- | --- | --- |
|  | a | 4 |
|  | b | 3 |
|  | c | 3 |
|  | d | 2 |
|  | e | 3 |
|  | f | 2 |
|  | g | 1 |
|  | h | 0 |

| Work Station | Eligible | Assign | Time Remaining | Idle Time |
| --- | --- | --- | --- | --- |
| I | a | A | 1.1 |  |
|  | b,c,e, (tie) | B | 0.7 |  |
|  |  | C | 0.4 |  |
|  |  | E | 0.3 | 0.3 |
| II | d | D | 0.0 | 0.0 |
| III | f,g | F | 0.5 |  |
|  |  | G | 0.2 | 0.2 |
| IV | h | H | 0.1 | 0.1 |
|  |  |  |  | 0.6 |

3.

4.

Solutions (continued)

b.	1.

2. 	Assign a, b, c, d, and e to station 1: 2.3 minutes [no idle time]

Assign f, g, and h to station 2: 2.3 minutes

3.

4.

5.	a.

b. 	The minimum cycle time = maximum task time =1.2 minutes

The maximum cycle time = .2 +.4 +.2 +.4 +1.2 +1.2 + 1.0 = 4.6 minutes

c.

d.

| Task | Number of following tasks |
| --- | --- |
| A | 4 |
| B | 3 |
| C | 2 |
| D | 2 |
| E | 1 |
| F | 1 |
| G | 0 |

Solutions (continued)

Assembly Line Balancing Table  (CT = 2 minutes)

| Work Station | Task | Task Time | Time Remaining | Feasible tasks Remaining |
| --- | --- | --- | --- | --- |
| I | A | 0.2 | 1.8 | B,D |
|  | B | 0.4 | 1.4 | C, D |
|  | D | 0.4 | 1.0 | C |
|  | C | 0.2 | 0.8 | – |
| II | E | 1.2 | 0.8 | – |
| III | F | 1.2 | 0.8 | – |
| IV | G | 1.0 | 1.0 | – |

e.

## 6.	a.

(1,2)

Positional weights

in parentheses

Solutions (continued)

- b. 	Using both the greatest positional weight and the greatest number of following tasks rules result in the following balance.

Assembly Line Balancing Table  (CT = 1.5 minutes)

| Work Station | Task | Task Time | Time Remaining | Feasible tasks Remaining |
| --- | --- | --- | --- | --- |
| I | A | 0.1 | 1.4 | B |
|  | B | 0.2 | 1.2 | C |
|  | C | 0.9 | 0.3 | E |
|  | E | 0.1 | 0.2 | – |
| II | D | 0.6 | 0.9 | F |
|  | F | 0.2 | 0.7 | G |
|  | G | 0.4 | 0.3 | H |
|  | H | 0.1 | 0.2 | I |
|  | I | 0.2 | – | – |
| III | J | 0.7 | 0.8 | K |
|  | K | 0.3 | 0.5 | L |
|  | L | 0.2 | 0.3 | – |

## Total idle time = 0.2 + 0 + 0.3 = 0.5

c.	For positional weights and greatest number of following tasks

7.	a.

Solutions (continued)

b.	.84 minutes = 50.4 seconds (maximum cycle time)

Minimum cycle time = maximum task time = 45 seconds  (results in 560 units of production)

c.

## d.

| Task | Number of followers | *PW |
| --- | --- | --- |
| A | 6 | 106 |
| B | 5 | 61 |
| C | 4 | 50 |
| D | 4 | 106 |
| E | 3 | 56 |
| F | 2 | 30 |
| G | 2 | 31 |
| H | 2 | 29 |
| I | 1 | 19 |
| J | 0 | 10 |

*Positional weight

CT = 50 seconds

| Work Station | Task | Task Time | Time Remaining | Feasible tasks Remaining |
| --- | --- | --- | --- | --- |
| I | A | 45 | 5 | – |
| III | D | 50 | – | – |
| III | B | 11 | 39 | C, E |
|  | E | 26 | 13 | C, F |
|  | C | 9 | 4 | – |
| IV | G | 12 | 38 | H, F |
|  | F | 11 | 27 | H |
|  | H | 10 | 17 | I |
|  | I | 9 | 8 | – |
| V | J | 10 | 40 | – |

Solutions (continued)

e.

8.

## b.

|  | Station | Tasks | Time | Idle/Time |
| --- | --- | --- | --- | --- |
|  | 1 | a,b | 1.9 | .1 |
|  | 2 | c,d | 1.9 | .1 |
|  | 3 | e,f,i | 2.0 | 0 |
|  | 4 | g,h,j | 1.5 | .5 |
|  | 5 | k,m | 1.2 | .8 |
|  |  |  |  | 1.5 |

|  | c. | Tasks | Positional Weight |
| --- | --- | --- | --- |
|  | a | 8.5 |
|  | b | 4.6 |
|  | c | 4.4 |
|  | d | 4.2 |
|  | e | 3.2 |
|  | f | 3.5 |
|  | g | 1.9 |
|  | h | 1.5 |
|  | i | 2.5 |
|  | j | 2.0 |
|  | k | 1.2 |
|  | m | .3 |

Solutions (continued)

| Work Station | Task | Task Time | Time Remaining | Feasible tasks Remaining |
| --- | --- | --- | --- | --- |
| I | a | .5 | 1.5 | b, c, d |
|  | b | 1.4 | .1 | – |
| II | c | 1.2 | .8 | d, e |
|  | d | .7 | .1 |  |
| III | f | 1.0 | 1.0 | e, i |
|  | e | .5 | .5 | i, g |
|  | i | .5 | 0 | – |
| IV | j | .8 | 1.2 | g |
|  | g | .4 | .8 | h |
|  | h | .3 | .5 | – |
|  | k | .9 | 1.1 | m |
|  | m | .3 | .8 | – |

Total idle time = .1 + .1 + 0 + .5 + .8 = 1.5 minutes

d.	Balance delay: part b and c 1.5/10 = 15%

| 9. | 1 | 4 | 3 |
| --- | --- | --- | --- |
|  | 2 | 5 | 6 |
| 11. | 1 | 5 | 4 |
|  | 3 | 8 | 7 |
|  | 6 | 2 |  |

## Solutions (continued)

| 12. | 3 | 1 | 4 | 8 | Or | 5 | 1 | 4 | 8 | Or | 5 | 1 | 4 | 6 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | 5 | 2 | 7 | 6 |  | 3 | 2 | 7 | 6 |  | 3 | 2 | 7 | 8 |
|  | 5 | 1 | 7 | 8 | Or | 3 | 1 | 7 | 8 | Or | 3 | 1 | 4 | 6 |
|  | 3 | 2 | 4 | 6 |  | 5 | 2 | 4 | 6 |  | 5 | 2 | 7 | 8 |
|  | 3 | 1 | 7 | 6 | Or | 5 | 1 | 7 | 6 |  |  |  |  |  |
|  | 5 | 2 | 4 | 8 |  | 3 | 2 | 4 | 8 |  |  |  |  |  |

| 13. | 3 | 1 | 8 |
| --- | --- | --- | --- |
|  | 9 | 7 | 4 |
|  | 5 | 2 | 6 |

- First rank or arrange the number of trips from high to low.

Department	Number of trips

  - 90

  - 80

  - 55

  - 40

From this we can see that departments 2 and 4 have the greatest interdepartmental work flow, so they should be close, perhaps locations C and B. Next, we can see that the work flows for 1 and 4, and 3 and 4 are high. Therefore department 4 has to be located at a central location (location B), while department 2 is in location C, department 1 is in location A, and department 3 is in location D.

Distance * Number of trips matrix

| Department | 1 | 2 | 3 | 4 |
| --- | --- | --- | --- | --- |
| 1 | – | (10 x 80) = 800 | (20x 70) = 1400 | (80 x 40) = 3200 |
| 2 | – | – | (40 x 60) = 2400 | (90 x 40) = 3600 |
| 3 | – | – | – | (55 x 50) = 2750 |
| 4 | – | – | – | – |

Total cost = $14,150

Solutions (continued)

| 15. | No. of trips (two way) |  | Order of Assignment |  |
| --- | --- | --- | --- | --- |
|  | 1–2 | 10 |  |  |  |
|  | 1–3 | 5 |  |  | A reasonable (intuitive) set of assignments is: |
|  | 1–4 | 90 |  | 11 |  |
|  | 1–5 | 370 |  | 1 |  | A #1 | B #5 |  |  |
|  | 1–6 | 135 |  | 6 |  |  |  |  |  |
|  | 1–7 | 125 |  | 7 |  | C #7 | D #4 | E #3 |  |
|  | 1–8 | 0 |  |  |  |  |  |  |  |
|  | 2–3 | 360 |  | 2 |  | F #6 | G #2 | H #8 |  |
|  | 2–4 | 120 |  | 8 (tie) |  |  |  |  |  |
|  | 2–5 | 40 |  |  |  |
|  | 2–6 | 115 |  | 9 | This set of assignments has a total cost of $143,650 per day. |
|  | 2–7 | 45 |  |  |  |
|  | 2–8 | 120 |  | 8 (tie) |  |
|  | 3–4 | 350 |  | 3 | Slight variations would also be reasonable, as long as departments 2, 4 and 8 are close to 3, 4 is close to 5, and 5 is close to 1. |
|  | 3–5 | 110 |  | 10 |  |
|  | 3–6 | 40 |  |  |  |
|  | 3–7 | 20 |  |  |  |
|  | 3–8 | 200 |  | 4 |  |
|  | No. of trips (two way) |  | Order of Assignment |  |
|  | 4–5 | 190 |  | 5 (tie) |  |
|  | 4–6 | 70 |  | 12 |  |
|  | 4–7 | 50 |  |  |  |
|  | 4–8 | 190 |  | 5 (tie) |  |
|  | 5–6 | 10 |  |  |  |
|  | 5–7 | 40 |  |  |  |
|  | 5–8 | 10 |  |  |  |
|  | 6–7 | 50 |  |  |  |
|  | 6–8 | 20 |  |  |  |
|  | 7–8 | 20 |  |  |  |

## Solutions (continued)

| 16. | No. of trips (two way) |  |  |  |
| --- | --- | --- | --- | --- |
|  | 1–2 | 0 |  |  |  |
|  | 1–3 | 40 |  |  | A reasonable (intuitive) assignment is: |
|  | 1–4 | 110 |  |  | 3–A, 5–B, 1–C, 4–D, 6–E, 2–F. |
|  | 1–5 | 80 |  |  | An equivalent solution is the reverse order: |
|  | 1–6 | 50 |  |  | 2–F, 6–B, 4–C, 1–D, 5–E, 3–F. |
|  | 2–3 | 0 |  |  |  |
|  | 2–4 | 50 |  |  |  |
|  | 2–5 | 40 |  |  |  |
|  | 2–6 | 120 |  |  |  |
|  | 3–4 | 10 |  |  |  |
|  | 3–5 | 250 |  |  |  |
|  | 3–6 | 10 |  |  |  |
|  | 4–5 | 40 |  |  |  |
|  | 4–6 | 90 |  |  |  |
|  | 5–6 | 20 |  |  |  |
|  | (Ignore Reception since all locations are the same distance from it.) |

17.	Two-way trips can not be used here because of the one-way route restriction. Consequently, students are forced to develop a heuristic that will yield reasonable assignments. One possible heuristic is the following:

Beginning with Department 1, identify the department which receives the greatest number of trips from that department (e.g., 40 to Department 2). Assign that department to the next location counter-clockwise.

For that department (e.g., 2) identify the department which receives the greatest number of trips (e.g., 5) and assign it to the next position.

Continue in this manner until all departments have been assigned.

The resulting set of assignments for this problem is: A–1, 2–B, 5–C, 4–D, 9–E, 8–F, 6–G, 10–H, 7–I, 3–J.

Students may raise the question about return trips to the original departments after delivery, which would seem to make all locations comparable. Three possible explanations are:

1.	Return trips cost less because they are unloaded.

2.	Unloaded trips may be permitted to move clockwise.

3.	Material handlers (?) pick up new load at each new department and move it to the next department.

(The last explanation seems to appeal most to students.)

## Solutions (continued)

| Work Station | Task | Task Time | Time Remaining | Feasible tasks Remaining |
| --- | --- | --- | --- | --- |
| I | D | 50 | 0.4 | – |
| II | A | 45 | 5.4 | – |
| III | E | 26 | 24 | B ,F |
|  | B | 11 | 13 | C, F |
|  | F | 11 | 2.4 | – |
| IV | C | 9 | 41 | G, H |
|  | G | 12 | 29 | H |
|  | H | 10 | 19 | I |
|  | I | 9 | 10 | J |
|  | J | 10 | 0.4 |  |

# Text boxes

0.6

0.7

0.8

0.5

1.0

0.5

0.5

1.4

c

f

h

g

d

e

b

a

3

a

d

f

7

5

2

b

4

c

4

e

9

h

5

i

6

g

a

b

d

c

f

e

g

h

a

b

d

c

f

e

g

.2

.4

.2

1.2

1.0

1.2

.4

0.1

(3.9)

0.2

(3.8)

0.9

(3.6)

0.6

(2.7)

0.1

(2.2)

0.2

(2.1)

0.4

(1.9)

0.1

(1.5)

0.2

(1.4)

0.7

(1.2)

a

b

c

d

e

f

g

h

i

j

k

l

(0.5)

(0.2)

0.3

0.2

CT = 1.5

a

b

c

e

d

h

g

f

i

j

a

c

e

j

k

m

g

h

d

f

i

b

10.

1

2

3

4

5

6

A

o

o

o

A

X

o

o

o

o

A

o

o

o

o